# State of New Jersey

Department of Transportation

Supplementary Specifications

For

Federal Aid Projects

#### Chris Christie							    James S. Simpson

#### Governor									Commissioner

#### Kim Guadagno

#### Lt. Governor

Edition 2011

SUPPLEMENTARY SPECIFICATIONS

FOR FEDERAL AID PROJECTS

FOR THE ______________________________ OF

_________________________________________

IN THE _____________ OF _________________

COUNTY OF _______________________________

1********************************************************************************************************1

include PROJECT DESCRIPTION AS SHOWN ON THE KEY sheet, AND FEDERAL PROJECT NUMBER (CONSTRUCTION) WHEN APPLICABLE.

1********************************************************************************************************1

AUTHORIZATION OF CONTRACT

-----------------------------------------------

The contract for this project is authorized by the provisions of local public contracts law, NJSA 40A: 11-1 et seq and Title 23 of the United States Code - Highways.

SPECIFICATIONS TO BE USED

The 2007 Standard Specifications for Road and Bridge Construction, of the New Jersey Department of Transportation as amended herein will govern the construction of this Project and the execution of the Contract.

These Supplemental Specifications consist of the following:

1********************************************************************************************************1

complete and include the following

Pages 1 to ___ inclusive.

1********************************************************************************************************1

1********************************************************************************************************1

INclude THE FOLLOWING FOR fhwa funded projects

General wage determinations issued under Davis-Bacon and related acts, published by US Department of Labor, may be obtained from the Davis-Bacon web site at http://www.access.gpo.gov/davisbacon/nj.html under the appropriate county, select the construction type heading:  HIGHWAY.

Pay the prevailing wage rates determined by the United States Secretary of Labor and the New Jersey Department of Labor.  If the prevailing wage rate prescribed for any craft by the United States Secretary of Labor is not the same as the prevailing wage rate prescribed for that craft by the New Jersey Department of Labor, pay the higher rate.

State wage rates may be obtained from the New Jersey Department of Labor & Workforce Development (Telephone:  609-292-2259) or by accessing the Department of Labor & Workforce Development’s web site at http://lwd.dol.state.nj.us/labor/wagehour/wagehour_index.html The State wage rates in effect at the time of award are part of this Contract, pursuant to Chapter 150, Laws of 1963 (NJSA 34:11-56.25, et seq.).

If an employee of the Contractor or subcontractor has been paid a rate of wages less than the prevailing wage, the Department may suspend the Work, and declare the Contractor in default.

The following FHWA funded project Attachments that are located after Division 1000 in these Supplemental Specifications:

1.	Required Contract Provisions, Federal-Aid Construction Contracts (Form FHWA-1273).

2.	Standard Federal Equal Employment Opportunity Construction Contract Specifications (Executive Order 11246).

3.	Notice of Requirement for Affirmative Action to Ensure Equal Employment Opportunity (Executive Order 11246).

4.	State of New Jersey Equal Employment Opportunity for Contracts Funded by FHWA.

2**************************************************************************************2

5.	Emerging Small Business Enterprise Utilization Attachment, FHWA Funded Contracts.

OR

5.	Disadvantaged Business Enterprise Utilization Attachment, FHWA Funded Contracts

5(A)	The Incentive Program, Disadvantaged Business Enterprise Utilization Attachment for FHWA Funded Contracts.

The fOLLOWING WILL BE COMPLETED AND PROVIDED BY LOCAL AID

Contact the office of civil rights, Contract Compliance at least 10 days in advance, by e-mailing, Jeffry Overton at Jeffrey.Overton@dot.state.nj.us, the completed ESBE/DBE goals request form available at http://www.state.nj.us/transportation/eng/documents/procedures/DesigUnitTask.shtm#act_3150

along with COMPLETED worksheet and a copy of the Engineer’s Estimate. Request for a determination on which of the two attachments (ESBE or DBE & Incentive Program DBE) is to be used for the project.

upon receiving the information, fill in the blank (GOALS FOR THIS PROJECT) on the attachment (and delete CORRESPONDING ATTACHMENT) located after Division 1000.

2**************************************************************************************2

2**************************************************************************************2

6.	Equal Employment Opportunity Special Provisions.

The fOLLOWING WILL BE COMPLETED AND PROVIDED BY LOCAL AID

Follow instructions and fill out the training request form at http://www.state.nj.us/transportation/eng/documents/procedures/DesigUnitTask.shtm#act_3150

submit request to the Civil Rights, Contract Compliance at least 10 days in advance, by e-mailing, Jeffry Overton at Jeffrey.Overton@dot.state.nj.us. Obtain required information.

upon receiving the information, fill in the blank on the attachment located after Division 1000.

2*************************************************************************************2

7.	Special Contract Provisions for Investigating, Reporting, and Resolving Employment Discrimination and Sexual Harassment Complaints.

8.	list & include additional project specific ATTACHMENTS required for the project, SUCH AS ASBESTOS ABATEMENT

1********************************************************************************************************1

GENERAL

-------------

All awards shall be made subject to the approval of the New Jersey Department of Transportation.  No construction shall start before approval of said award by the New Jersey Department of Transportation.  Prior to the start of construction the contractor must submit a Material Questionnaire (SA-11) listing all sources of materials.  Any materials used on the project from a non-approved New Jersey Department of Transportation source will be considered non-participating.  The contractor is also notified that the District Office, Division of Local Aid and Economic Development must be notified of the construction commencement date at least five (5) calendar days prior to the start of construction.

Award of contract and subletting will not be permitted to, materials will not be permitted from, and use of equipment will not be permitted that is owned and/or operated by, firms and individuals included in the report of suspensions, debarments and disqualifications of firms and individuals as maintained by the Department of the Treasury, General Services Administration, CN-039, Trenton NJ 08625 (609-633-3990).

Payment for a pay item in the proposal includes all the compensation that will be made for the work of that item as described in the contract documents unless the "basis of payment" clause provides that certain work essential to that item will be paid for under another pay item.

Whenever any section, subsection, subpart or subheading is amended by such terms as changed to, deleted or added it is construed to mean that it amends that section, subsection, subpart or subheading of the 2007 Standard Specifications unless otherwise noted.

Whenever reference to page number is made, it is construed to refer to the 2007 Standard Specifications unless otherwise noted.

Henceforth in this supplementary specification whenever reference to the State, Commissioner, Department, Engineer or Inspector is made, it is construed to mean the particular municipality or county executing this contract.

Whenever reference to Title 27 is made, it is construed to mean Title 40.

Division 100 – General Provisions

Section 101 – General Information

101.01  Introduction

1********************************************************************************************************1

complete and include the funding dollar amounts with the appropriate state and/or federal fiscal year for PROJECTs with advanced construction (MULTI-YEAR) FUNDING.

sme contact – project manager

THE FOLLOWING IS ADDED:

Pursuant to NJSA 27:1B-21.6 and USC (United States Code) Section 115, the Department intends to enter into a contract for the advancement of the Project.  However, sufficient funds for the Project may not have been appropriated, and only amounts appropriated by law may be expended.  Payment under the Contract is restricted to the amounts appropriated for a fiscal year (FY).

Governing bodies have no legal obligation to make such an appropriation.  There is no guarantee that additional funds will be appropriated.  Failure by governing bodies to appropriate additional funds will not constitute a default under, or a breach of, the Contract.  However, if the Department terminates the Contract or suspends work because funds have not been appropriated, the parties to the Contract will retain their rights for suspension and termination as provided in 108.13, 108.14 and 108.15; except as indicated below.

Do not expend or cause to be expended any sum in excess of the amount allocated in the current fiscal year's Capital Program (as specified below).  The Department will notify the Contractor when additional funding has been appropriated.  Any expenditure by the Contractor which exceeds the amount appropriated is at the Contractor's risk and the Contractor waives its right to recover costs in excess of that appropriated amount.

The approved _____ Capital Program has an item with $ _____ million for the construction of the Project.

2**************************************************************************************2

INCLUDE ALL APPROPRIATE STATEMENT(S)

The Department anticipates that _____ million dollars in additional funds will be provided during State FY _____.

The Department anticipates that _____ million dollars in additional funds will be provided during Federal FY ____.

The Department anticipates that the balance of the funds necessary to complete the Project will be provided during State FY _____.

The Department anticipates that the balance of the funds necessary to complete the Project will be provided during Federal FY _____.

2**************************************************************************************2

The Federal FY begins October 1 of the previous calendar year and the State FY begins July 1 of the previous calendar each year.

1********************************************************************************************************1

1********************************************************************************************************1

INclude THE FOLLOWING FOR PROJECTs that are funded wholly or in part by the American Recovery and Reinvestment Act (ARRA), 2009; (stimulus Act).

sme contact – project manager

2**************************************************************************************2

BDC09s-03R dated Apr 16, 2009

THE FOLLOWING IS ADDED:

This Contract is funded in whole or in part with funding provided under the American Recovery and Reinvestment Act of 2009 (ARRA).  The Contractor is responsible for complying with the applicable provisions of the ARRA which are incorporated herein by reference.

Section 902 of the American Recovery and Reinvestment Act (ARRA) of 2009 requires that each contract awarded using ARRA funds must include a provision that provides the U.S. Comptroller General and his representatives with the authority to:

1.	to examine any records of the contractor or any of its subcontractors, or any State or local agency administering such contract, that directly pertain to, and involve transactions relating to, the Contract or subcontract.

2.	to interview any officer or employee of the Contractor or any of its subcontractors, or of any State or local government agency administering the contract, regarding such transactions.

Accordingly, the Comptroller General and his representatives shall have the authority and rights as provided under Section 902 of the ARRA with respect to this contract, which is funded with funds made available under the ARRA. Section 902 further states that nothing in this section shall be interpreted to limit or restrict in any way any existing authority of the Comptroller General.

Section 1515(a) of the ARRA requires that the Inspector General has the authority to:

1.	Examine records of the Contractor or its subcontractors

2.	Interview the Contractor’s or its subcontractor’s employees or officers working on this Contract.

Nothing in this section is to be interpreted to limit or restrict the existing authority of the Inspector General.

2**************************************************************************************2

2**************************************************************************************2

BDC09s-09 dated Oct 09, 2009

THE FOLLOWING IS ADDED:

Section 7 of Executive Order No. 151, (E.O. 151). dated August 28, 2009 provides that:

"Since the funds supporting this contract, grant, or agreement are provided through the American Recovery and Reinvestment Act of 2009 (ARRA), the subrecipient, contractor, subcontractor, local education agency, or vendor will post any jobs that it creates or seeks to fill as a result of this contract, grant, or agreement. The subrecipient, contractor, subcontractor, local education agency, or vendor will post jobs to the New Jersey State Job Bank by submitting a job order using the form available at http://NJ.gov/JobCentralNJ, notwithstanding any other posting the subrecipient, contractor, subcontractor, local education agency, or vendor might make. Any advertisements posted by the subrecipient, contractor, subcontractor, local education agency, or vendor for positions pursuant to this contract, grant, or agreement must indicate that the position is funded with ARRA funds."

Posting of the job opening is not required when:

a.	the employer intends to fill the opening with a present employee, a laid-off former employee, or a job candidate from a previous recruitment;

b.	a pre-existing, legally binding collective bargaining agreements provides otherwise; or

c.	an exception has been granted to the Reporting Agency by the Department of Labor and Workforce Development.

2*************************************************************************************2

1********************************************************************************************************1

101.03  Terms

The following terms are changed.

2**************************************************************************************2

INclude THE FOLLOWING FOR fhwa funded projects

Completion.

(3) is changed to:

3.	the Contractor has satisfactorily executed and delivered to the RE all documents, including CC-257R, certifications, and proofs of compliance required by the Contract Documents, it being understood that the satisfactory execution and delivery of documents, certificates, and proofs of compliance is a requirement of the Contract.

department: Shall be defined as the contracting agency.

resident engineer (RE) shall be defined as a representative of the contracting agency.

********************************************************************************************************

include the following for all projects.

101.04  Inquiries Regarding the Project.

THE FOLLOWING IS ADDED TO THIS SUBSECTION:

Inquiries regarding the various types of work of this Contract shall be directed to the following representatives of the Department:

- Before Award of the Contract.

******************************************************

INSERT the APPROPRIATE NAME, ADDRESS, PHONE NUMBER AND FAX NUMBER.

All inquiries shall include the following:

- Name of the company;

- Telephone number, fax number, and contact person; and

- Specifics of the inquiry, including anticipated impacts.

The Department will investigate the information provided in the inquiry and then respond through an addendum only if determined to be necessary.

- After Award of the Contract.

******************************************************

INSERT the APPROPRIATE NAME, ADDRESS, PHONE NUMBER AND FAX NUMBER.

**********************************************************************************************************

SECTION 103 – award and excecution of contract

This section shall be deleted and local requirements used *

SECTION 104 - SCOPE OF WORK

104.03.04  Contractual Notice

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

the second paragraph is changed to:

Immediately provide written notice to the RE of a circumstance that is believed to be a change to the Contract.  Include the following in the initial written notice:

1.	A statement that this is a notice of a change.

2.	The date when the circumstances believed to be a change were discovered.

3.	A detailed and specific statement describing the nature and circumstances of the change.

4.	If the change will or could affect costs to the Department.

5.	If the change will or could affect Contract Time as specified in 108.11.01.C.

In addition to the hard copy of the notice, email the notice to the RE.  It is not necessary to attach listed documents to the email.

Section 105 – Control of Work

105.05  Working Drawings

THE SECOND PARAGRAPH is CHANGED TO:

Ensure that working drawing submissions also conform to the Department design manuals and other Department standards for the proposed work.  Ensure that working drawings are signed and sealed by a Professional Engineer.  After Award, the Department will provide additional formatting information, the number of copies required, and the designated design unit to which the Contractor shall submit working drawings.

1********************************************************************************************************1

complete and include the following if the DEPARTMENT will REQUIRE less or more than 30 days to review and certify, or reject and return, working drawings. provide a justification to increased time frames and obtain project manager’s approval.

1.	Certified Working Drawings.

the last sentence of the FIRST paragraph is changed to:

The Department will require ___days for review and certification or rejection and return of certified working drawings.

1********************************************************************************************************1

complete and include the following if the DEPARTMENT will REQUIRE less or more than 45 days to review and approve, or reject and return, working drawings. provide a justification to increased time frames and obtain project manager’s approval.

2.	Approved Working Drawings.

the last sentence of the FIRST paragraph is changed to:

The Department will require ___days for review and approval or rejection and return of working drawings.

105.07.01  Working in the Vicinity of Utilities

2**************************************************************************************2

BDC08s-02 dated Feb 17, 2009

the second PARAGRAPH is changed to:

Protect and support existing Department electrical and ITS facilities and ensure that there is no interruption of service.  Use hand tools only while working within two feet of the fiber optic network.  At least 30 days before beginning the work, submit a plan to the RE for approval showing the method of support and protection.

2

2

the FOLLOWING IS ADDED TO the SIXTH PARAGRAPH

Access within railroad right-of-way is restricted.  Comply with the railroad’s permit requirements for working within the railroad right-of-way.  Coordinate the work with the railroad’s access and safety restrictions.

1

105.07.02  Work Performed by Utilities

THIS SECTION SHALL BE DELETED **********************************************************************************************************1

complete and include the following for all utility companies that are affected by the project for the advance notice requirements

Section 108 – Prosecution and Completion

108.01  Subcontracting

1********************************************************************************************************1

include details, in the appropriate sections, regarding: SPECIALIZED KNOWLEDGE, experience, CRAFTSMANSHIP, and/OR EQUIPMENT required. the subcontractor must be qualified to perform certain SPECIALTY items (such as: segmental bridge, drilled shafts, blasting, ETC.).

1********************************************************************************************************1

1.	Values and Quantities.

1.

1********************************************************************************************************1

list “SPECIALTY ITEMS"

items MAY BE CONSIDERED “SPECIALITY ITEMS” DUE TO SPECIAILIZED KNOWLEDGE, CRAFTSMANSHIP, OR EQUIPMENT REQUIRED TO perform THE WORK. obtain APPROVAL of contracting agency.

2**************************************************************************************2

select one of the following.

There are no Specialty Items in this Project.

*****OR*****

Specialty Items are as listed below:

3************************************************3

Drilling and blasting.

3************************************************3

*****AND/OR*****

3

Above ground highway lighting items.

*****AND/OR*****

Above ground sign lighting items.

***** AND/OR *****

Above and below bridge deck lighting items.

***** AND/OR *****

Electrical wire items.

3************************************************3

*****AND/OR*****

ITS items, except for foundations, standards, and junction boxes.

3************************************************3

3************************************************3

list additional “specialty items”

as approved by the contracting agency

3************************************************3

2**************************************************************************************2

1********************************************************************************************************1

108.02  Commencement of Work

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

The Subpart 4 in the first paragraph is changed to:

4.	Progress schedule as specified in 153.03

1********************************************************************************************************1

1********************************************************************************************************1

BDC09s-12 dated JAN 19, 2010

108.06 NIGHT OPERATIONS

- Visibility Requirements for Workers and Equipment.

THE FIRST PARAGRAPH IS CHANGED TO:

Ensure that workers wear a 360° high-visibility retro-reflective safety garment meeting ANSI/ISEA Class 3, Level 2 standards.

1********************************************************************************************************1

108.10  Contract Time

1********************************************************************************************************1

2**************************************************************************************2

complete and include the following WHEN dates are specified.

delete A, if not applicable and renumber

A.	Complete all work required for Interim Completion for ____________on or before __________.

B.	Complete all work required for Substantial Completion on or before __________.

C.	Achieve Completion on or before __________.

2**************************************************************************************2

*****OR*****

2**************************************************************************************2

complete and include the following WHEN a number of DAYS are specified.

delete A, if not applicable and renumber

A.	Complete all work required for Interim Completion for ____________ in _______ days.

B.	Complete all work required for Substantial Completion in _______ days.

C.	Achieve Completion in _______ days.

2**************************************************************************************2

1********************************************************************************************************1

108.11.01  Extensions to Contract Time

B.	Types of Delays.

2.	Excusable, Non-Compensable Delays.

1******************************************************************************************************1

include the following, IF the project DURATION is less than 1 year, and amount of duration of utility work performed by utility company is minor. Subject to review and approval of contracting agency

THE last PARAGRAPH is CHANGED TO:

If approved excusable, non-compensable delays exceed a total of 90 days, the time in excess of 90 days will become excusable and compensable as specified in 108.11.01.B.3.

1********************************************************************************************************1

108.14  Default and Termination of Contractor’s Right to Proceed

1********************************************************************************************************1

complete and include the following if start of work is restricted by department action

List (1) of the first PARAGRAPH is changed to:

1.	Fails to begin construction operations within __ days of execution of the Contract.

1********************************************************************************************************1

108.19  Completion and Acceptance

THE FOLLOWING IS ADDED:

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

if no incentive payment for early completion is to be specified include the following:

No Incentive Payment for Early Completion is specified for this project.

1********************************************************************************************************1

108.20  Liquidated Damages

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

select APPROPRIATE condition from the following list

Liquidated damages are as follows:

2**************************************************************************************2

complete and include the following.

delete A, if not applicable and renumber

A.	For each day that the Contractor fails to complete the work as specified in Subpart A of Subsection 108.10 of these Special Provisions, for Interim Completion, the Department will assess liquidated damages in the amount of $______.

use only the road user cost.

B.	For each day that the Contractor fails to complete the work as specified in Subpart B of Subsection 108.10 of these Special Provisions, for Substantial Completion, the Department will assess liquidated damages in the amount of $______.

use the total cost of the road user and construction engineering costs.

C.	For each day that the Contractor fails to achieve Completion as specified in Subpart C of Subsection 108.10 of these Special Provisions, the Department will assess liquidated damages in the amount of $_____.

Use only the construction engineering cost divided by 2.

2**************************************************************************************2

2**************************************************************************************2

THE FOLLOWING IS ADDED:

When the Contractor may be subjected to more than one rate of liquidated damages established in this Section, the Department will assess liquidated damages at the higher rate.

**********************************************************************************************************

SECTION 109 – MEASUREMENT AND PAYMENT

109.01  Measurement of Quantities

THE SECOND PARAGRAPH IS DELETED:

109.02  Scope of Payment

THE THIRD SENTENCE OF THE FIRST PARAGRAPH IS CHANGED TO:

The Department will not make additional or separate payment for work or portion of work unless specifically provided for in the “Measurement and Payment” Subsection.

Division 150 – Contract Requirements

Section 152 – Insurance

152.03.01  Owner’s and Contractor’s Protective Liability Insurance

A.	Policy Requirements.

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

THE fourth SENTENCE of the first paragraph IS CHANGED TO:

Ensure that policies are underwritten by companies with a current A.M. Best rating of A- with a Financial Size Category of VII or better.

Section 153 – Progress Schedule

THIS SECTION SHALL BE DELETED AND contracting agency REQUIREMENT MAY BE INSERTED

1********************************************************************************************************1

Section 155 – Construction Field Office

155.03.01  Field Office

1********************************************************************************************************1

provide THE project specific items.

complete and include the following list.

4.	Communication Equipment.

a.	Telephones.  Provide ___ cordless phones with auto-switching.

c.	Cell Phones.  Provide ____ cellular phones.  Ensure the cellular phone plan provides for unlimited mobile to mobile in-network usage, unlimited push-to-talk/ walkie-talkie usage and an anticipated monthly usage of 900 any-time minutes for each phone.  Ensure the phones are on the same plan.  Ensure the cellular phone plan has a home rate with no roaming charges within the state.  Ensure each cellular phone has the following features:

1.	Push to Talk / Walkie-Talkie capable

2.	Camera with 1 megapixel picture capability

3.	Battery life capable of 180 minutes of continuous use and 72 hours of standby use

4.	Equipped with a hands-free headset

5.	Base charger and car charger

d.	Computer System.  Provide a computer system meeting the following requirements:

___ computer configurations each meeting the following:

1.	Equipped with an Intel Pentium ___ processor with Hyper Threading technology having a clock speed of ___ GHz or faster, ___ GB RAM, ___ MB Video RAM, ___ Gigabyte hard drive designated as drive C, one DVD (+/-) Writer Drive, one CD-R Recordable Drive.  Ensure the system is USB 2.0 compatible and has at least two front USB ports.

2.	Wireless Ethernet Hub Switch with appropriate number of ports and cables and a print server.

3.	High-speed broad band connection and service with a minimum speed of ___ Megabytes per second (mbps) with dynamic IP address for the duration of the project.

4.	19 inch or larger Flat Screen LCD monitor with tilt/swivel capabilities.

5.	___ Megabyte or larger Zip Drive internal or external with backup software for MS-Windows and DOS, and fifteen corresponding formatted data cartridges corresponding to the tape drive size.

6.	___ Flatbed USB version 2.0 or greater Color Scanner with automatic document feed.

7.	Uninterruptible power supply (UPS).

8.	Surge protector for the entire computer configuration to be used in conjunction with the UPS.

9.	___ computer workstations, chair, printer stand, and/or table having both appropriate surface and chair height.

10.	One can of compressed air and screen cleaning solution every other month of the duration of the contract.

Ensure one computer has a 56K baud data/fax modem.  If more than one computer configuration is specified, provide one wireless network card for the base computer configuration and hardwire connections between computer configurations as directed by the RE.

Also provide:

___ USB ___ GB Flash/Jump memory drives

___ CD-R ___ MB (or larger) recordable CD’s compatible with the CD drive and ___ recordable DVD’s.

___ CD/DVD Holder (each holds 50)

___ color laser printers and supplies as follows:

1.	HP PCL 5 emulation, with a minimum of 192 Megabytes of expanded memory, printer cable, and legal size paper tray .

2.	One set of printer ink cartridges every other month for the duration of the construction project for each printer.

Software as follows:

1.	Microsoft Windows, latest version with future upgrades for the duration of the entire project. Ensure 1 computer has a Microsoft Windows 32 Bit Operating System for ACES, Extra and Groupwise.

2.	Microsoft Office Professional, latest version.

3.	Norton’s System Works for Windows, latest version, or compatible software package with future upgrades and latest virus patches.

4.	Anti-Virus software, latest version with monthly updates for the duration of the contract.

5.	Visio Professional Graphics Software for Windows, latest version

6.	 Primavera Project Planner, latest version

7.	PaperPort, latest version, for Scanner

THE third PARAGRAPH IS CHANGED TO:

When the computer system is no longer required by the RE, the Department will remove and destroy the hard drive, and return the computer system to the Contractor.  The Department will retain other data storage media.

6.	Office Equipment.

2.	___ digital camera(s).  Ensure each digital camera has auto-focus, with rechargeable batteries and charger, __ MB memory card, USB Memory Card Reader compatible with camera and field office computer, 1.5 inch LCD monitor, ___ mega pixel resolution, __ X optical zoom lens, built in flash, image stabilization, computer connections, and a carrying case

3.	___ video camcorder(s).  Ensure each video camcorder is a mini DVD camcorder with ___ optical zoom, 2" LCD monitor, USB 2.0 compatible and includes USB 2.0 connections.

7.	Inspection Equipment.

1.	___ Calculators with trigonometric capability

2.	___ Date/ Received stamp and ink pad

3.	___ Electronic Smart level, 4 foot

4.	___ Carpenter rulers

5.	___ Steel tape, 100 feet

5.	___ Cloth tape, 100 feet

7.	___ Illuminated measuring wheel

8.	___ Plumb bob and cord

9.	___ Line level and cord

10.	___ Surface thermometer

11.	___ Concrete thermometer

12.	___ Digital infrared asphalt thermometer

13.	___ Direct Tension Indicator (DTI) Feeler Gage, 0.005 inch

14.	___ Sledge hammer, 8lb

15.	___ Self leveling laser level with range of 100 feet and an accuracy of ¼ inch per 100 feet

16.	___ Hard hats - orange, reflectorized hard hats according to ANSI Z89.1

17.	___ Safety garments – orange, reflectorized, 360º high visibility safety garments according to ANSI/ISEA Class 3, Level 2 standards.  To be replaced yearly for the duration of the contract.

18.	___ Sets of rain gear with reflective sheeting

19.	___ Sets of hearing protection with a Noise Reduction Rating of 22 dB

20.	___ Sets of eye protection according to ANSI Z87.1

21.	___ Sets of fall arrest equipment according to ANSI Z359.1 standards consisting of a full body harness, lanyard and anchor

22.	___ Light meter - capable of measuring the level of luminance in foot-candles

23.	___ Lantern flashlight, 6V with monthly battery replacements

24.	Testing equipment and apparatus conforming to AASHTO T23, T119, T152

1********************************************************************************************************1

155.03.03  Telephone Service

this Subsection is changed to:

Telephone service consists of monthly charges for telephone and cellular phones provided for the field office and materials field laboratory excluding set up charges.

155.04  Measurement and Payment

THE third PARAGRAPH IS CHANGED TO:

The Department will make payment for TELEPHONE SERVICE for the actual costs of the charges as evidenced by paid bills submitted within 60 days of receipt from the service provider for telephone and cell phones.

Section 156 – Materials Field Laboratory and Curing facility

THIS SECTION SHALL BE DELETED AND contracting agency REQUIREMENT MAY BE INSERTED

1*******************************************************************************************************1

Section 158 – Soil Erosion and Sediment Control
and Water Quality Control

158.03.02  SESC Measures

19.	Oil-Only Emergency Spill Kit.

THE second SENTENCE OF THE first PARAGRAPH IS CHANGED TO:

Include Oil-only Emergency Spill Kit, Type 1 consisting of the following:

Section 159 – Traffic Control

1

159.02.02  Equipment

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

Include the following if the REMOTELY OPERATED PVMS OR PORTABLE TRAILER MOUNTED CCTV CAMERA ASSEMBLY are needed

The following is added to the list of equipment references:

Portable Variable Message Sign w/Remote Communication…….………………...……………………1001.04

Portable Trailer Mounted CCTV Camera Assembly……………….……………………………………1001.05

1********************************************************************************************************1

159.03.02  Traffic Control Devices

1*******************************************************************************************************1

BDC09s-08 dated DEC 07, 2009

2.	Construction Barrier Curb.

THE last paragraph is changed to:

Provide top and side mounted flexible delineators on the construction barrier curb.  For delineators located on the right side when facing in the direction of traffic, ensure that the retroreflective sheeting is white.  For delineators located on the left side when facing in the direction of traffic, ensure that the retroreflective sheeting is yellow.  Attach flexible delineators according to the manufacturer’s recommendations.

Starting at the beginning of the construction barrier curb section mount top delineators at 100-foot intervals on tangent sections, curves of radii greater than 1,910 feet, and at 50-foot intervals on curves of radii of 1,910 feet or less.

Mount side delineators at the lead end of each barrier segment with the top of the delineator 3 inches from the top of the barrier.

6.	Traffic Control Truck with Mounted Crash Cushions.

THE last sentence is changed to:

Submit drawings to the RE detailing the manner of securing the ballast, signed and sealed by a Professional Engineer, certifying that it is capable of withstanding the impact forces for which the impact attenuator is rated.

1*****************************************************************************************************1

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

Include the following if the REMOTELY OPERATED PVMS OR PORTABLE TRAILER MOUNTED CCTV CAMERA ASSEMBLY are needed

THE FOLLOWING IS ADDED to the second paragraph:

8.	Portable Variable Message Sign w/Remote Communication (PVMSRC).  Place the PVMSRC at the location directed by the RE.  Ensure that a designated representative familiar with the operation and programming of the unit is available on the Project for On-Site Configuration.  Only display messages authorized by the Department for the Project and make the signs available for use remotely from the Traffic Operation center (TOC) specified in 105.07.01.B.  Repair or replace malfunctioning PVMSRC within 12 hours of notification by the RE.

Provide a broadband cellular telephone service plan with unlimited data service on an IP based packet network for the intended operational and functional requirements of the PVMSRC.  Ensure that the PVMSRC has remote operation capability from the specified TOC using the Department’s current DMS control software at the time of deployment.

Provide for one week of testing by the TOC for remotely operating the PVMSRC before the start of construction operations that require lane or shoulder closures, or other impacts to traffic.  At least 10 days before testing, submit to the RE for approval a plan for any work to be completed in the TOC.  Submit a request to the RE at least 4 days in advance to access the TOC for any work.

9.	Portable Trailer Mounted CCTV Camera Assembly (PTMCCA).  Place the PTMCCA at the location directed by the RE.  Ensure that a designated representative familiar with the operation and programming of the unit is available on the Project for initial installation.  Repair or replace malfunctioning PTMCCA within 12 hours of notification by the RE.  .

Provide a system that includes a robotic network camera remotely controllable, including Pan, Tilt and Zoom (PTZ), and viewable over the internet through a password protected website.  Provide for internet access through the website hosted by Earth Cam for Department cameras.  No substitution is permitted.  Provide broadband communication service and On-Site Camera Configuration for remote operation and control from the web site to the field site.  Provide continuous viewable image at a minimum of 320H x 240V resolution and 1 frame per sec (fps) through the web site.  If required by the Traffic Operation center (TOC) specified in 105.07.01.B, establish password level designations, camera presets, and camera image displays.  Provide any incidental equipment or material required for successful remote operation and communications.

Provide for one week of testing by the TOC for remotely operating the PTMCCA before the start of construction operations that require lane or shoulder closures, or other impacts to traffic.

1********************************************************************************************************1

159.03.08  Traffic Direction

A.	Flagger.

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

The last sentence is changed to:

Ensure that the flagger is equipped with a STOP/SLOW paddle and follows MUTCD flagging procedures.

1********************************************************************************************************1

159.04  MEASUREMENT AND PAYMENT

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

THE FOLLOWING ITEMs are ADDED:

Item	Pay Unit

Portable Variable Message Sign w/Remote Communication	UNIT

Portable Trailer Mounted CCTV Camera Assembly	UNIT

1*******************************************************************************************************1

Section 160 – Price Adjustments

160.03.01  Fuel Price Adjustment

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

throughout this subsection, TABLE 161.03.01-1 is CHANGED TO TABLE 160.03.01-1

THE third PARAGRAPH IS CHANGED TO:

If the as-built quantity of an Item listed in Table 160.03.01-1 differs from the sum of the quantities in the monthly Estimates, and the as-built quantity cannot be readily distributed among the months that the Item listed in Table 160.03.01-1 was constructed, then the Department will determine fuel price adjustment by distributing the difference in the same proportion as the Item’s monthly Estimate quantity is to the total of the Item’s monthly estimates.

the 25 th LINE IN THE TABLE 160.03.01-1 is changed to:

HOT MIX ASPHALT ___ ___ ___ BASE COURSE		2.50 Gallons per Ton

1********************************************************************************************************1

2**************************************************************************************2

BDC09s-07 dated aug 13, 2009

THE FOLLOWING are ADDED to table 160.03.01-1

| Items | Fuel Usage Factor |
| --- | --- |
| NON-VEGETATIVE SURFACE, HOT MIX ASPHALT | 2.50 Gallons per Ton |
| COLOR-COATED NON-VEGETATIVE SURFACE, HOT MIX ASPHALT | 2.50 Gallons per Ton |

2**************************************************************************************2

160.03.02  Asphalt Price Adjustment

1********************************************************************************************************1

2**************************************************************************************2

BDC08s-02 dated Feb 17, 2009

note 1 of the Third PARAGRAPH IS CHANGED TO:

1.	The N. J. Department of Transportation will determine the weight of asphalt binder for price adjustment by multiplying the percentage of new asphalt binder in the approved job mix formula by the weight of the item containing asphalt binder.  If a Hot Mix Asphalt item has a payment unit other than ton, the Department will apply an appropriate conversion factor to determine the number of tons used.

2**************************************************************************************2

2**************************************************************************************2

the fourth PARAGRAPH IS CHANGED TO:

A = B ( [(MA − BA)/BA] ( C ( M ( G

Where:

A = Asphalt Price Adjustment

B = Bid Price for Tack Coat/Prime Coat

MA = Monthly Asphalt Price Index

BA = Basic Asphalt Price Index

C = Petroleum Content of the Tack Coat and Prime Coat in Percent by Volume:

Use 100% for cutbacks and Tack Coat 64-22

60% for Polymer Modified Tack Coat

60% for RS or similar type emulsions

M = Percentage of Bid Price Applicable to Materials Only: Use 82%

G = Gallons of Tack Coat and Prime Coat Furnished and Applied

DIVISION 200 - EARTHWORK

SECTION 201 - CLEARING SITE

201.03.01  Clearing Site

201.03.02  Clearing Site, Bridge and Clearing Site, Structure

the following is added to the first paragraph.

Only the following equipment is permitted for the work:

1.	Pneumatic or Electric Equivalent Hand Operated Hammers.

a.	When demolishing concrete not closer than 6 inches to structural members: hammers weighing no more than 90 lbs (exclusive of bit), equipped only with chisel point bits.

b.	When demolishing concrete within 6 inches of structural members: hammers weighing no more than 30 lbs (exclusive of bit).

2.	Saw Cutters.

a.	When cutting concrete within 6 inches of structural members:  concrete cutters and concrete saws.  While using water in the cutting operation, provide shielding beneath the cutting operation to prevent water leakage.  Continuously collect slurry and dispose of as specified in 201.03.09.  Ensure that the slurry does not enter the structure or highway drainage system.

3.	Hydraulic Breakers.  Ram-hoe type breakers, hydraulic breakers, and demolition shears may be used with the following restrictions:

a.	Submit required data to the RE for Department’s analysis of stresses induced to the girders.

b.	Delineate the centerline and limits of the top flange of girders before the equipment operation.

c.	Do not use equipment within 6 inches of the delineated flanges.

d.	Do not pull or twist the reinforcement steel.

4.	Hydraulic Splitters.  Hydraulic splitters.

5.	Other Equipment.  Obtain RE approval before use.

1********************************************************************************************************1

2**************************************************************************************2

include THE FOLLOWING FOR DECK AND/OR BEAM ENCASEMENT REMOVAL WHEn THE REMAINDER OF EXISTING SUPERSTRUCTURE IS TO REMAIN.

the following is added:

The procedure is described below:

1.	Prestressed Concrete Stringers and Concrete Diaphragms.  Repair damage to prestressed concrete stringers and concrete diaphragms using nonshrink grout conforming to Subsection 903.08 before deck placement.

2.	Steel Stringers, Floorbeams, Cross Frames, and Diaphragms.

a.	Repair procedures to tensile components in conformance with ASTM A 6/A 6M and the following:

1	Repair gouges up to 1/8 inch by grinding flush in the direction of principal stress.

2	Repair gouges deeper than 1/8 inch by first grinding; then, depositing weld metal and grinding flush with the surface of the metal in the direction of principal stress.  Weld using low hydrogen electrodes conforming to current AWS Specifications A5.1 and A5.5.

3	Repair kinks and deformations by flame straightening or a combination of flame straightening and jacking.  Ensure flame straightening is performed by personnel having a minimum of three years of documented experience.  Submit the names of the personnel to the RE for review and approval prior to performing the work.

b.	Repair procedures to compression components for kinks and deformations as outlined in 2.a (3) above.  Where more than five percent of the cross-sectional area of the member is damaged, submit a repair procedure to the RE for review and approval.

Clean and paint exposed existing top flanges of beams with prime coat as specified in Subsection 554.03.

2**************************************************************************************2

2**************************************************************************************2

INCLUDE THE FOLLOWING IF grounding and bonding for ELECTRIFIED RAIL LINES is required

Bonding and Grounding for Electrified Railroad.  For the required materials, submit a list to the RE for approval 21 days before construction operation.  In the list, include:  material description, manufacturer and catalog number.  After obtaining the RE’s approval, submit the list to the railroad for review and approval.  Do not order the materials prior to obtaining the railroad’s approval.  Furnish and deliver the materials to the railroad.  Obtain a receipt for the materials from the railroad and provide a copy to the RE.

2**************************************************************************************2

2*************************************************************************************2

ENTER THE QUANTITIES BELOW AND ANY REVISIONS TO THE MATERIALS LISTED AFTER CONSULTATION WITH THE RAILROAD.

| List of Materials |
| --- |
| Description | Quantity Required |
| U-bolt, ⅞-inch diameter by 4-inch, BS fastener | -------- |
| Strap, clevis, 1¼ by 2 inches stock, 12-inch connecting length, 1-inch diameter hole, ⅝-inch diameter bolt, ultimate strength 25 psi, Brewer Tilchener Corp.-3074 C | -------- |
| Dead end eye bolt, compression type steel, use DIE 6010SH, compression tool, 60A ALCOA 9190-332 | -------- |
| Jumper cable, compression type aluminum, use DIE 6020AH, compression tool 60A ALCOA 5120-781 | -------- |
| Terminal - Bundy AK2C39B1 to 336400 Cable (1) | -------- |
| Ground terminal - Bundy AK2C39B1 to 336400 Cable (2) | -------- |
| Terminal - solid barrier to 0.17 square inch cable Bundy KC28B1 | -------- |
| Compound, aluminum to copper connection (ALNOX) CANS | -------- |
| Termination, dead end strand clamp, ALCO 336 4 KCM | -------- |
| Clip, bronze, complete type BC, Ohio brass | -------- |
| Thimble-Bronx 336 4 KCM | -------- |
| U-bolt, 1¼-inch diameter by 1½-inch loop 336 4 KCM 11, 30/7 STR ACSR, ANACONDA insulated aluminum cable having a diameter of 0.17 square inches, ANACONDA | -------- |

2**************************************************************************************2

1*******************************************************************************************************1

201.03.04  Removing Underground Storage Tanks

1***************************************************************************************************1

Complete and include following information, when removal of underground storage tank(s) are required

Remove following:

| Parcel No. | Tank Size | Contents | Tank Registration No. |
| --- | --- | --- | --- |

1**************************************************************************************************1

201.03.08  Asbestos Removal

1**************************************************************************************************1

include location and other requirements for the removal of Asbestos

1********************************************************************************************************1

201.04  Measurement and Payment

THE FOLLOWING IS ADDED:

1********************************************************************************************************1

2**************************************************************************************2

complete and include amount using Engineer’s estimate

The Department will not make payment for the Item CLEARING SITE in excess of $_______________ until Completion.

2**************************************************************************************2

2**************************************************************************************2

INCLUDE PARTIAL PAYMENTS, IF REQUIRED for REMOVAL OF THE BRIDGE OR STRUCTURE SCHEDULED IN STAGES.

THE FOLLOWING EXAMPLE REPRESENTS A BRIDGE SCHEDULED TO BE REMOVED IN THREE STAGES.  THE SEQUENCE OF CONSTRUCTION REQUIRED REMOVAL OF 20 PERCENT OF THE BRIDGE IN STAGE I, 40 PERCENT IN STAGE II, AND 40 PERCENT IN STAGE III.  THE ENGINEER’S ESTIMATE FOR THE ITEM AMOUNT WAS $4,000,000.  THE PAYMENT SCHEDULE FOR “CLEARING SITE, BRIDGE (STRUCTURE NO.)” WILL BE AS FOLLOWS:

- for the item “clearing site bridge (structure no.)”, The department will not make IN EXCESS OF $4,000,000 UNTIL SUBSTANTIAL COMPLETION.

- the department will make payment of TWENTY PERCENT OF THE PRICE BID (OR $800,000, WHICHEVER IS LESS) UPON ACCEPTANCE OF STAGE I DEMOLITION.

- the department will make payment of FORTY PERCENT OF THE PRICE BID (OR $1,600,000, WHICHEVER IS LESS) UPON ACCEPTANCE OF STAGE II DEMOLITION.

- the department will make payment of FORTY PERCENT OF THE PRICE BID (OR $1,600,000, WHICHEVER IS LESS) UPON ACCEPTANCE OF STAGE III DEMOLITION.

3************************************************3

complete and include THE VALUE

The Department will not make payment for the Item CLEARING SITE, BRIDGE (___) in excess of $_______________ until Substantial Completion.

The Department will not make payment for the Item CLEARING SITE, STRUCTURE (___) in excess of $_______________ until Substantial Completion.

3************************************************3

2**************************************************************************************2

1********************************************************************************************************1

Section 202 – Excavation

202.02  Materials

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

the FIRST in the list IS CHANGED TO:

Coarse Aggregate (No. 57, or 67)	901.03

1********************************************************************************************************1

202.03.04  Excavating Regulated Material

3.	Temporarily Storing.

THE first PARAGRAPH is CHANGED TO:

Temporarily store regulated or hazardous material in stockpiles within the Project Limits and as shown on the Plans.  Construct stockpiles on polyethylene sheeting.  Contain stockpiles with haybales or silt fence placed continuously at the perimeter of the stockpiles.  For hazardous material, if a stockpile area is not available within the Project Limits, sample and analyze materials in-situ for disposal.  Excavate and place the hazardous regulated material directly into trucks, and haul it directly to the approved disposal facility.

203.02.01  Materials

this subsection IS CHANGED TO:

Provide materials as specified:

Soil Aggregate (I-7, I-9, I-10, I-11, I-13, and I-14)	901.11

Division 400 – Pavements

Section 401 – Hot Mix Asphalt (HMA) Courses

401.02.02  Equipment

THE LAST PARAGRAPH is changed to:

When an MTV is used, install a paver hopper insert with a minimum capacity of 14 tons in the hopper of the HMA paver.

401.03.01  Preparing Existing Pavement

A.	Milling of HMA.

1********************************************************************************************************1

complete and include TIME INTERVAL FOR RESURFACING THE MILLED PAVEMENT BASED ON THE project STAGING. MAXIMUM TIME INTERVAL MAY VARY BUT SHALL NOT EXCEED 72 HOURS.

| Stage | Max. time interval allowed |
| --- | --- |

1*******************************************************************************************************1

401.03.03  HMA Cours

D.	Transportation and Delivery of HMA.

THE FIRST PARAGRAPH IS CHANGED TO:

Deliver HMA using HMA trucks in sufficient quantities and at such intervals to allow continuous placement of the material.  Do not allow trucks to leave the plant within 1 hour of sunset unless nighttime lighting is provided as specified in 108.06.  The RE will reject HMA if the HMA trucks do not meet the requirements specified in 1009.02.  The RE will suspend construction operations if the Contractor fails to maintain a continuous paving operation.  Before the truck leaves the plant, obtain a weigh ticket from a fully automatic scale.  Before unloading, submit for each truckload a legible weigh ticket that includes the following:

1.	Name and location of the HMA plant.

2.	Project title.

3.	Load time and date.

4.	Truck number.

5.	Mix designation.

6.	Plant lot number.

7.	Tare, gross, and net weight.

E.	Spreading and Grading.

1*******************************************************************************************************1

2**************************************************************************************2

include the following if one of these conditions is applicable

- THE LENGTH OF CONTINUOUS THROUGH TRAVEL LANE CONSTRUCTION IS less THAN 2,500 FEET.

- the total tonnage of the course is less than 2,000 tons.

- the staging of the project results in less than 2,500 feet of continuous paving.

THE THIRD PARAGRAPH IS CHANGED TO:

The use of an MTV is optional for the construction of intermediate and surface course in the traveled way.  If an MTV is used, ensure that the MTV independently delivers HMA from the HMA trucks to the HMA paver.  Operate the MTV to ensure that the axle loading does not damage structures, roadway, or other infrastructure.

2**************************************************************************************2

or

2**************************************************************************************2

include one of the following if any one of the above conditions is not applicable

THE THIRD PARAGRAPH IS CHANGED TO:

Use an MTV for the construction of intermediate and surface course in the traveled way.  Ensure that the MTV independently delivers HMA from the HMA trucks to the HMA paver.  Operate the MTV to ensure that the axle loading does not damage structures, roadway, or other infrastructure.

*******OR*******

Use an MTV for the construction of surface course in the traveled way.  Ensure that the MTV independently delivers HMA from the HMA trucks to the HMA paver.  Operate the MTV to ensure that the axle loading does not damage structures, roadway, or other infrastructure.

2**************************************************************************************2

use 100% of the surface course joint length to estimate the quantity of Polymerized joint adhesive

2**************************************************************************************2

***********************************************************************************************************

SECTION 401 –HOT MIX ASPHALT (HMA) COURSES

ALTERNATE SUBSECTIONS 401.03.03 H, I AND J

FOR

LOCAL AID PROJECTS

***********************************************************************************************************

401.03.03 HMA Courses

REPLACE 401.03.03.H WITH THE FOLLOWING:

H.	Air Void Requirements.

Pavement lots are defined as approximately 15,000 square yards of pavement in Surface area.  If pavement lot area is less than 5000 square yards, the Regional District Local Aid Office may waive the air voids requirements.

The RE will designate an independent testing agency (Laboratory) to perform the quality assurance sampling, testing and analysis.  The Laboratory is required to be accredited by the AASHTO Accreditation Program (www.amrl.net).  The Laboratory’s accreditation must include AASHTO T 166 and AASHTO T 209.

The Laboratory Technician who performs the quality assurance sampling shall be certified by the Society of Asphalt Technologists of New Jersey as an Asphalt Plant Technologist, Level 1.

The Laboratory will determine air voids from 5 (Five) 6 inch diameter cores taken from each lot in random locations within the traveled way and at least one core in each travel lane.  The Laboratory will determine air voids of cores from the values for the maximum specific gravity of the mix and the bulk specific gravity of the core.  The Laboratory will determine the maximum specific gravity of the mix according to NJDOT B-3 and AASHTO T 209, except that minimum sample size may be waived in order to use a 6-inch diameter core sample.  The Laboratory will determine the bulk specific gravity of the compacted mixture by testing each core according to AASHTO T 166.

The Laboratory will calculate the in-place air voids of each completed lot outside the acceptable range of 2 percent air voids to 8 percent air voids.

The RE will assess a reduction in lot due to nonconformance to air voids according to the Table 401.03.03-3.

| Table 401.03.03-3 Reduction for Nonconformance to Air Voids Requirements |
| --- |
| Lot Average Air Void Value (Five Samples) | Reduction Per Lot (Percent of Lot) |
| 0.0 to 1.9 | 10 |
| 2.0 to 8.0 | 0 |
| 8.1 to 9.0 | 5 |
| 9.1 to 10.0 | 15 |
| 10.1 to 12.0 | 30 |
| Over 12.0 | Remove & Replace |

If the average air voids for the lot is greater than 12.0 percent, remove and replace the lot.  The replacement work is subject to the same requirements as the initial work.

REPLACE 401.03.03.I WITH THE FOLLOWING:

I.	Thickness Requirements.

Thickness requirements will apply when full-depth, uniform-thickness HMA pavement construction is shown.

Pavement lots are defined as approximately 15,000 square yards of pavement area.  The Engineer will not include areas consisting of different HMA mixtures or thicknesses in the same lot.  If thickness lot area is less than 5000 square yards, the Regional District Local Aid Office may waive the thickness requirements.

The RE will designate an independent testing agency (Laboratory) to perform the quality assurance sampling, testing and analysis.  The Laboratory is required to be accredited by the AASHTO Accreditation Program (www.amrl.net).  The Laboratory’s accreditation must include AASHTO T 166 and AASHTO T 209.

The Laboratory Technician who performs the quality assurance sampling shall be certified by the Society of Asphalt Technologists of New Jersey as an Asphalt Plant Technologist, Level 1.

The Laboratory will test for thickness using the full-depth cores taken for surface course air voids, evaluated according to NJDOT B-4. The Laboratory will base acceptance on total thickness and thickness of the surface course.

1.	Total Thickness.  The Laboratory will calculate the percent defective (PD) as the percentage of the lot that is less than the design thickness.  The Department will base total thickness acceptance on the percentage of the lot estimated to fall below the specified thickness as follows:

a.	Sample Mean () and Standard Deviation (S) of the N Test Results (X1, X2,..., XN).

b.	Quality Index (QI).

QL = ( − Tdes)/S, and Tdes is the design thickness.

c.	Percent Defective (PD).  Using NJDOT ST - Statistical Tables (NJDOT Standard Specs for Roads and Bridges 2007-NJDOT TEST METHODS) for the appropriate sample size, determine the percentage of material (PD) falling below the design thickness associated with QL (lower limit).

d.	Reduction in Payment.  The Department will determine the reduction in payment based on the quantity of the surface course multiplied by the percent reduction in payment from Table 401.03.03-5.

| Table 401.03.03-5 Reduction in Payment for Nonconformance to Requirements for Total Thickness |
| --- |
| Percent Defective | Percent Reduction |
| 0 to 25.0 | 0 |
| 25.1 to 30.0 | 2 |
| 30.1 to 35.0 | 5 |
| 35.1 to 40.0 | 10 |
| 40.1 to 45.0 | 20 |
| Over 45.0 | Remove & Replace |

e.	Removal and Replacement.  If the lot PD ( 45, remove and replace, or mill and overlay, the lot.  The replacement work is subject to the same requirements as the initial work.

2.	Surface Course Thickness.  The Laboratory will evaluate the surface course solely to determine whether a remove-and-replace or an overlay condition exists, not for pay adjustment.  The Laboratory will calculate the percent defective (PD) as the percentage of the lot that is less than the allowable thickness for the nominal maximum aggregate used in the surface course.  The Laboratory will accept pavement lots with PD ( 25 and will reject pavement lots with PD > 25.

The Laboratory will base surface thickness acceptance on the percentage of the lot estimated to fall below the allowable thickness as follows:

a.	Sample Mean () and Standard Deviation (S) of the N Test Results (X1, X2,..., XN).  Calculate using the formula as specified in 401.03.03.I.1.

b.	Quality Index (Q).

QL = ( – Tall)/S, where Tall is the minimum allowable thickness from Table 401.03.03-6.

| Table 401.03.03-6 Surface Course Thickness Requirements |
| --- |
| HMA Mix Design Size Designation | Minimum Allowable Compacted Lift Thickness (Tall) |
| 4.75 MM | 0.75 inch |
| 9.5 MM | 1.00 inch |
| 12.5 MM | 1.25 inches |
| 19 MM | 2.00 inches |

c.	Percent Defective.  Using NJDOT ST - Statistical Tables (NJDOT Standard Specs for Roads and Bridges 2007-NJDOT TEST METHODS) for the appropriate sample size, determine the percentage of material (PD) falling below the allowable thickness associated with QL (lower limit).

d.	Removal and Replacement.  If the surface course fails to meet the acceptance requirement with a PD ≤ 25, the Department will require removal and replacement of the lot.  The replacement work is subject to the same requirements as the initial work.

*******************************************************************************************************************************

ADD THE FOLLOWING FOR RESURFACING PROJECTS.

*******************************************************************************************************************************

THIS SUBSECTION IS DELETED.  IN NO INSTANCE WILL A COMPACTED AVERAGE THICKNESS OF LESS THAN 1.25 INCHES BE ACCEPPTABLE.

*******************************************************************************************************************************

ADD THE FOLLOWING FOR NEW CONSTRUCTION, COMPLETE RECONSTRUCTION OR WIDENINGS GREATER THAN EIGHT FEET.

*******************************************************************************************************************************

REPLACE 401.03.03.J WITH THE FOLLOWING:

J.	Ride Quality Requirements. The Department may evaluate the HMA surface course placed in travel lanes using the International Roughness Index (IRI) according to ASTM E 1926. Other areas will be tested with a ten foot straight edge. The Department will use the measured IRI and straight edge to compute pay adjustment (PA). The PA will be negative for defective work.

The RE will designate an independent testing agency to perform the ride quality testing and analysis.  The testing agency is required to comply with certification requirements according to NJDOT R-1.

The Department will calculate the Pay Adjustment (PA) as specified in Table 401.03.03-7 and will base PA on lots of 0.01mile length for each travel lane.

- Smoothness Measurement.

The testing agency will test the longitudinal profile of the HMA surface course for ride quality with a Class 1 Inertial Profiling System according to AASHTO MP 11 approved according to AASHTO PP 49.

The testing agency will test the full extent of the pavement in the direction of travel in each wheel path. The single IRI value reported for each 0.01-mile lot of pavement is the average of 3 runs.

2.   Other Areas.

In addition to the above, a 10-foot straightedge shall be used for the following   areas: transverse profile of the finished riding surface, longitudinal and transverse profile of shoulders and ramps, utility hardware, drainage inlets and manholes, and any other areas so designated in the Special Provisions.  Any areas that have more than a 1/4-inch deviation between any two contact points of the straightedge shall be corrected by the Contractor using infrared heating to rework the material in a manner approved by the Engineer.  Following correction, the area will be retested to verify compliance, each individual non-complying location will be assessed $250 negative PA.

- Control Testing.

Perform control testing during HMA placement to ensure compliance with the ride quality requirements specified in Table 401.03.03-7.

- Preparation for IRI Testing.

Provide the necessary traffic control when the testing agency performs IRI testing.  Perform required mechanical sweeping of the surface course before IRI testing.  To facilitate auto triggering on laser profilers, place a single line of preformed traffic marking tape perpendicular to the roadway baseline 300 feet before the beginning of each lane to be tested.

- Acceptance.

The Engineer will determine acceptance and make payment adjustments based on the following:

i.	Pay Adjustment.

The pay equations in Table 401.03.03-7 express the pay adjustment in dollars per lot of 0.01 mile. For lots of any other length, the Engineer will scale the pay adjustment up or down in proportion to the actual length of the lot. IRI numbers are in inches per mile.

| Table 401.03.03-7 Pay Equations for IRI Ride Quality for 0.01 Mile |
| --- |
| Local Roadways with Posted Speed ≥ 45 MPH | IRI ≤ 100 | PA = $0 |
|  | 100 < IRI ≤ 170 | PA = (IRI − 100) × (− $1.43) |
|  | IRI > 170 | Remove & Replace |
| Local Roadways with Posted Speed < 45 MPH | IRI ≤ 120 | PA = $0 |
|  | 120 < IRI ≤ 220 | PA = (IRI − 120) × (− $1.00) |
|  | IRI > 220 | Remove & Replace |

ii.	Retest provision.

After testing, if the IRI exceeds the Remove and Replace value (RRV) in Table 401.03.03-7, the testing agency will retest the lot.  The testing agency will average the IRI values from the initial test and the retest to determine the final result.

iii.	Removal and Replacement.

If the average IRI is greater than the RRV after a retest is performed, remove and replace the lot.  Any replacement work is subject to the same requirements as the initial work.  If only a small percentage (less than 8 percent) of paving lots falls under the RRV, the RE may allow the Contractor to submit a plan for corrective action.  If the Contractor’s plan for corrective action is not approved, the RE may require removal and replacement, or may allow the lot to remain in place and the lot will be subject to the pay adjustment as computed in Table 401.03.03-7.  If the Contractor’s plan for corrective action is approved and the lot is reworked, the testing agency will test and evaluate it as a new lot that must meet the same requirements as the initial work.

2**************************************************************************************2

1********************************************************************************************************1

1****************************************************************************************************1

401.04  Measurement and Payment

THE FOLLOWING IS ADDED:

The Department will make a payment adjustment for HMA air void quality by the following formula:

Pay Adjustment = Q x  BP x PPA

Where:

BP = Bid Price

Q= Air Void Lot Quantity

PPA= air void PPA as specified in 401.03.03H.

The Department will make a payment adjustment for HMA thickness quality by the following formula:

Pay Adjustment = Q x  BP x PPA

Where:

BP = Bid Price

Q= Thickness Lot Quantity

PPA= thickness PPA as specified in 401.03.03I

The Department will make a payment adjustment for HMA ride quality, as specified in 401.03.03J.

Section 402 – HMA Friction Course

402.04  Measurement and Payment

THE FOLLOWING IS ADDED:

The Department will make a payment adjustment for HMA thickness quality by the following formula:

Pay Adjustment = Q x  BP x PPA

Where:

BP = Bid Price

Q= Thickness Lot Quantity

PPA= thickness PPA as specified in 401.03.03I

The Department will make a payment adjustment for HMA ride quality, as specified in 401.03.03J.

Section 403 – Ultra-Thin Friction Course

403.03.01  Ultra-Thin Friction Course

E.	Spreading and Grading.

THE second paragraph is changed to:

Apply polymer modified tack at a temperature of 140 to 175 °F.  Continuously monitor rate of spray, ensuring a uniform application rate over entire width to be overlaid.  Apply at the rate of 0.20 ± 0.05 gallons per square yard.  Do not allow traffic, equipment, tools, or any other disturbance to the polymer modified tack coat before placing the ultra-thin friction course.

403.04  Measurement and Payment

THE FOLLOWING IS ADDED:

The Department will make a payment adjustment for HMA thickness quality, by the following formula:

Pay Adjustment = Q x  BP x PPA

Where:

BP = Bid Price

Q= Thickness Lot Quantity

PPA= thickness PPA as specified in 401.03.03I

The Department will make a payment adjustment for HMA ride quality, as specified in 401.03.03J.

Section 404 – Stone Matrix Asphalt (SMA)

404.03.01  SMA

H.	Air Void Requirements.

This part is changed to:

Drill cores as specified in 401.03.05.

Mainline lots are defined as the area covered by a day’s paving production of the same job mixed formula between 1000 and 4000 tons for the traveled way and auxiliary lanes.  The RE will combine daily production areas less than 1000 tons with previous or subsequent production areas to meet the minimum lot requirements.  When the maximum lot requirement is exceeded in a day’s production, the RE will divide the area of HMA placed into 2 lots with approximately equal areas.

Ramp pavement lots are defined as approximately 10,000 square yards of pavement in ramps.  The RE may combine ramps with less than the minimum area into a single lot.  If 2 or more ramps are included in a single lot, the RE will require additional cores to ensure that at least 1 core is taken from each ramp.

Other pavement lots are defined as approximately 10,000 square yards of pavement in shoulders and other undefined areas.

The ME will calculate the percent defective (PD) as the percentage of the lot outside the acceptable range of 2 percent air voids to 7 percent air voids.  The acceptable quality limit is 10 percent defective.  For lots in which PD < 10, the Department will award a positive pay adjustment.  For lots in which PD > 10, the Department will assess a negative pay adjustment.

The ME will determine air voids from 5 cores taken from each lot in random locations.  The ME will determine air voids of cores from the values for the maximum specific gravity of the mix and the bulk specific gravity of the core.  The ME will determine the maximum specific gravity of the mix according to NJDOT B-3 and AASHTO T 209, except that minimum sample size may be waived in order to use a 6-inch diameter core sample.  The ME will determine the bulk specific gravity of the compacted mixture by testing each core according to AASHTO T 166.

The ME will calculate pay adjustments based on the following:

1.	Sample Mean () and Standard Deviation (S) of the N Test Results (X1, X2,..., XN).

2.	Quality Index (Q).

3.	Percent Defective (PD).  Using NJDOT ST for the appropriate sample size, the Department will determine PDL and PDU associated with QL and QU, respectively.  PD = PDL + PDU

4.	Percent Pay Adjustment (PPA).  Calculate the PPA for traveled way and ramp lots as specified in Table 401.03.03-3.

| Table 401.03.01-1 PPA for Mainline Lots and Ramp Lots |
| --- |
|  | Quality | PPA |
| Surface | PD ( 10 | PPA = 4 − (0.4 PD) |
|  | 10 ( PD ( 30 | PPA = 1 − (0.1 PD) |
|  | PD ( 30 | PPA = 40 − (1.4 PD) |
| Intermediate and Base | PD ( 30 | PPA = 1 − (0.1 PD) |
|  | PD ( 30 | PPA = 40 − (1.4 PD) |

Calculate the PPA for other pavement lots as specified in Table 401.03.03-4.

| Table 401.03.01-2 PPA for Other Pavement Lots |
| --- |
|  | Quality | PPA |
| All Courses | PD ( 50 | PPA = 1 − (0.1 PD) |
|  | PD ( 50 | PPA = 92 − (1.92 PD) |

5.	Outlier Detection.  The ME will screen all acceptance cores for outliers using a statistically valid procedure.  If an outlier is detected, replace that core by taking an additional core at the same offset and within 5 feet of the original station.  The following procedure applies only for a sample size of 5.

1.	The ME will arrange the 5 core results in ascending order, in which X1 represents the smallest value and X5 represents the largest value.

2.	If X5 is suspected of being an outlier, the ME will calculate:

3.	If X1 is suspected of being an outlier, the ME will calculate:

4.	If R > 0.642, the value is judged to be statistically significant and the core is excluded.

6.	Retest.  If the initial series of 5 cores produces a percent defective value of PD ( 30 for mainline or ramp lots, or PD ( 50 for other pavement lots, the Contractor may elect to take an additional set of 5 cores at random locations chosen by the ME.  Take the additional cores within 15 days of receipt of the initial core results.  If the additional cores are not taken within the 15 days, the ME will use the initial core results to determine the PPA.  If the additional cores are taken, the ME will recalculate the PPA using the combined results from the 10 cores.

7.	Removal and Replacement.  If the final lot PD ( 75 (based on the combined set of 10 cores or 5 cores if the Contractor does not take additional cores), remove and replace the lot and all overlying work.  The replacement work is subject to the same requirements as the initial work.

404.04  Measurement and Payment

THE FOLLOWING IS ADDED:

The Department will make a payment adjustment for HMA air void quality by the following formula:

Pay Adjustment = Q x  BP x PPA

Where:

BP = Bid Price

Q= Air Void Lot Quantity

PPA= air void PPA as specified in 401.03.03H.

The Department will make a payment adjustment for HMA thickness quality by the following formula:

Pay Adjustment = Q x  BP x PPA

Where:

BP = Bid Price

Q= Thickness Lot Quantity

PPA= thickness PPA as specified in 401.03.03I

The Department will make a payment adjustment for HMA ride quality, as specified in 401.03.03J

Section 405 – Concrete Surface Course

405.03.02  Concrete Surface Course

I.	Thickness Requirements.

This part is changed to:

I.	Thickness Requirements.  The ME will divide the concrete pavement into lots of approximately 5000 square yards.  The ME will divide each lot into 5 equal sections.  The RE will direct the Contractor to drill 1 core, as specified in 405.03.03, from a randomly selected location within each section.  The ME will test these cores for thickness as specified in ASTM C 174.

The Department will determine conformance with thickness requirements as follows and will either assess the greater of the pay reduction for average core thickness or individual core thickness, or the Department will direct the Contractor to remove and replace the lot:

1.	Average Core Thickness.  If the average core thickness is greater than or equal to the specified core thickness, the Department will not apply a payment reduction.  If the average thickness is less than the specified thickness, but is greater than or equal to the specified thickness minus 1/2 inch, the Department will determine payment reduction by the following formula:

Payment Reduction = Q x BP x PPR Where: Q = Thickness Lot Quantity BP = Bid Price TS = Specified Thickness. TA = Average Thickness PPR = Percent Payment Reduction =

2.	Individual Core Thickness.  When more than 2 individual cores in the lot are less than the specified thickness minus 1/4 inch, the Department will determine the payment reduction using for the above noted formula and using a PPR = 2 percent.

3.	Remove and Replace.  If the average thickness is less than the specified thickness minus 1/2 inch, the RE will require that the lot be removed and replaced.

405.04  Measurement and Payment

THE FOLLOWING IS ADDED:

The Department will make a payment adjustment for Concrete Surface thickness quality, as specified in 405.03.02.

The Department will make a payment adjustment for HMA ride quality, as specified in 401.03.03J

Division 450 – Concrete Pavement Rehabilitation

Section 453 – Full Depth Concrete Pavement Repair

453.03.01  Full Depth Repair Using Concrete

C.	Setting Forms, Joint Ties, and Dowels.

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

THE third SENTENCE OF THE seventh PARAGRAPH IS CHANGED TO:

Slowly withdraw the tube as the hole is filled.

1********************************************************************************************************1

Division 500 – Bridges and Structures

Section 502 – Load Bearing Piles

502.03.03  Driving Piles

B.	Methods of Driving.

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

The following is added to the last paragraph:

4.	Cast-In-Place Piles.  Ensure that reinforcement steel is installed as specified in 504.03.01.  Place concrete as specified in 504.03.02.  Clean out open end piles to the elevation shown on Plans.  Weld closure plates for closed-end pipe piles as shown on Plans.

1********************************************************************************************************1

C.	Test Piles.

1.	Static Pile Load Test.

1********************************************************************************************************1

complete and include static test load to be applied

Apply a total of _____ tons of static test load to the piles.

1********************************************************************************************************1

2.	Dynamic Pile Load Tests.

1********************************************************************************************************1

Specify if restrike is required

1********************************************************************************************************1

Section 503 – Drilled Shaft Foundations

503.03.04  Crosshole Sonic Logging (CSL)

A.	CSL Tube Installation.

THE third paragraph is changed to:

Ensure that each pipe is fitted with a watertight shoe at the bottom and a removable cap at the top.  Attach the pipes securely to the interior of the reinforcement cage with a minimum cover of 4 inches.  Install the tubes as near to parallel as possible.

503.03.06  Constructing Drilled Shafts

F.	Constructing Using Casings.

2.	Removable Casing.

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

THE last SENTENCE OF THE second PARAGRAPH IS CHANGED TO:

Do not expose the shaft concrete to salt water or moving water for 7 days.

1*******************************************************************************************************1

Section 504 – Structural Concrete

504.03.02  Constructing Concrete

G.	Removal of Forms and Falsework.

1********************************************************************************************************1

Complete and include the following if concrete strength required for the removal of forms and false work

Do not remove forms and false work until the concrete obtains a compressive strength of ____ psi.

1********************************************************************************************************1

Section 506 – Structural Steel

506.03.01  Structural Steel

E.	Installing High-Strength Steel Bolts.

THE second paragraph is changed to:

Provide a Skidmore-Wilhelm calibrator or an acceptable equivalent tension measuring device on the Project during erection.  Ensure that the manufacturer’s representative is present during the first full day of tensioning work to provide technical assistance.  Verify each lot of DTIs using the Skidmore-Wilhelm calibrator as specified in NJDOT S-3.

506.03.06  Repair Galvanizing

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

THE last SENTENCE OF THE second PARAGRAPH IS CHANGED TO:

If painting is directed, treat the galvanized surface according to the manufacturer’s recommendations, then apply the epoxy intermediate and urethane finish coats only.

1********************************************************************************************************1

Section 507 – Concrete Bridge Deck and Approaches

507.03.07  Concrete Bridge Approach

THE FOLLOWING IS ADDED:

Ensure the concrete conforms to the surface requirements as specified in 507.03.02 N, except each lot will be equal to the number of cubic yards of approach concrete placed in the lane.

507.04  Measurement and Payment

1********************************************************************************************************1

2**************************************************************************************2

BDC10s-01 dated Mar 29, 2010

THE second paragraph is changed to:

The Department will include payment for epoxy coated reinforcement steel for the bridge approach under the item CONCRETE BRIDGE APPROACH; for other concrete items, the Department will make payment for reinforcement steel under REINFORCEMENT STEEL, REINFORCEMENT STEEL, EPOXY-COATED, and REINFORCEMENT STEEL, GALVANIZED as specified in 504.04.

2**************************************************************************************2

2**************************************************************************************2

THE FOLLOWING IS ADDED:

The Department will make a payment adjustment for concrete surface requirement quality in deck slabs and approach, by the following formula:

Pay Adjustment = Q x  BP x PR

Where:

BP = Bid Price

Q= Surface Requirement Lot Quantity

PR= percent reduction as specified in Table 507.03.02-2

2**************************************************************************************2

1********************************************************************************************************1

1********************************************************************************************************1

2**************************************************************************************2

BDC08s-02 dated Feb 17, 2009

THE second paragraph is changed to:

The Department will make payment for reinforcement steel under REINFORCEMENT STEEL, REINFORCEMENT STEEL, EPOXY-COATED, and REINFORCEMENT STEEL, GALVANIZED as specified in 504.04.

2**************************************************************************************2

2**************************************************************************************2

THE FOLLOWING IS ADDED:

The Department will make a payment adjustment for concrete surface requirement quality in deck slabs and approach, by the following formula:

Pay Adjustment = Q x  BP x PR

Where:

BP = Bid Price

Q= Surface Requirement Lot Quantity

PR= percent reduction as specified in Table 507.03.02-2

2**************************************************************************************2

1********************************************************************************************************1

1********************************************************************************************************1

BDC09s-11 dated JAN 26, 2010

SECTION 508 – BRIDGE DRAINAGE

508.02 MATERIALS

THE FOLLOWING IS ADDED TO LIST OF MATERIALS:

Fiberglass Pipe .............................................................................................................................................. 909.02.09

THE FOLLOWING SUBPART IS ADDED:

508.03.03 Fiberglass Pipe and Fittings

Ensure that pipe supports are located at spacings that do not exceed the pipe manufacturer’s recommendations. Avoid supports that have point contact or narrow supporting areas. Standard sling, clamp, and clevis hangers and shoe supports designed for use with steel pipe may be used. Ensure that the minimum strap width of all pipe hangers meets the pipe manufacturer’s recommendations. Ensure that straps have a minimum of 120 degrees of contact with the pipe. On pipe supported on surface with less than 120 degrees of contact use a split fiberglass pipe protective sleeve bonded in place with adhesive.

Ensure that all connections of pipes and fittings shown on the plans to facilitate future removal for maintenance cleanout or flushing are made with a threaded, gasketed coupler or a bolted gasketed flange system. Use only female – male threaded plugs for cleanouts.

508.04 MEASUREMENT AND PAYMENT

THE FOLLOWING ITEM IS ADDED:

Item 										Pay Unit

___" FIBERGLASS PIPE								LINEAR FOOT

1********************************************************************************************************1

Section 510 – Timber Structures

510.03.02  Sheeting and Wales

1********************************************************************************************************1

include the corrosion requirements for metal components, if NECESSARY

1********************************************************************************************************1

510.04  Method of Measurement

This subsection Heading is changed to:

510.04  Measurement and Payment

Section 511 – Bulkhead, Fender, and Dolphin Systems

511.02.01  Materials

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

14 th on the list is changed to:

Fiberglass Reinforced Plastic Lumber (FRPL)	916.01

1********************************************************************************************************1

Section 513 – Retaining Walls

513.02.01  Materials

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

The following is added:

For MSE Walls, use either Soil Aggregate, I-15 or Coarse Aggregate, No. 57. For Prefabricated Modular Retaining Walls and T-Wall, use either Soil Aggregate, I-9 or Coarse Aggregate, No. 57.

1********************************************************************************************************1

513.03.01  Proprietary Retaining Walls

F.	Backfilling.

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

the heading and first PARAGRAPH under subpart (1) are changed to:

1.	Soil Aggregate.

1*******************************************************************************************************1

G.	Compacting.

1*******************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

the heading and first PARAGRAPH under subpart (1) are changed to:

1.	Soil Aggregate.  With the exception of the 5-foot zone directly behind the units, compact soil aggregate with large, smooth drum, vibratory rollers using the density control method as specified in 203.03.02.D.

1*******************************************************************************************************1

513.04  Measurement and Payment

THE FOLLOWING IS ADDED AFTER THE FIRST PARAGRAPH:

The Department will make payment for reinforcement steel under REINFORCEMENT STEEL, and REINFORCEMENT STEEL, EPOXY-COATED as specified in 504.04 for reinforcement steel in cast-in-place retaining walls.

1*******************************************************************************************************1

include the following upon ASSIGNING an APPROPRIATE SECTION/SUBSECTION NUMBERs if DRILLED SHAFT foundations FOR SIGN SUPPORT STRUCTURES is necessary

The following section is added:

SECTION 51x - DRILLED SHAFT foundations FOR SIGN SUPPORT STRUCTURES

51x.01  DESCRIPTION

This work describes the requirements for installing drilled shafts for sign support structures.

51x.02  MATERIALS

51X.02.01  Materials

Provide materials as specified:

Concrete	903.03

Self Consolidating Concrete	903.06.01

Grout	903.08.02

Reinforcement Steel	905.01.01

Drilled Shaft Casing	906.03

Structural Steel Paint (Organic Zinc)	912.01.01

Water	919.08

Provide clay-mineral based slurry (processed attapulgite or bentonite) for mineral slurry.  Ensure that the mineral slurry has a mineral grain size that will remain in suspension and has sufficient viscosity and gel characteristics to transport excavated material to a suitable screening system.  Ensure that the percentage and specific gravity of the material used to make the mineral suspension is sufficient to maintain the stability of the excavation and to allow proper concrete placement.

Provide polymer slurry as recommended by the manufacturer.

51X.02.02  Equipment.

Provide equipment as specified:

Concrete Batching Plant	1010.01

Concrete Trucks	1010.02

Ensure that equipment does not introduce uncontrolled exhaust fumes into the surrounding areas, or other occupied areas adjacent to the work site.  Crane and drilling engine exhaust fumes will require their own separate exhaust systems adequately vented to the atmosphere away from any confined work sites.

Ensure that equipment used for final bottom cleaning does not have a centralizing guide at the tip.

Use excavation and drilling equipment having adequate capacity, including power, torque, and down thrust to excavate a hole of both the maximum specified diameter and to a depth of 20 percent beyond the depths shown on the plans when operated at rated capacity.

Provide Crosshole Sonic Logging (CSL) test equipment that includes the following components:

1.	A microprocessor-based CSL system for display of individual CSL records, analog-digital conversion and recording of CSL data, analysis of receiver responses, and printing of CSL logs.

2.	Ultrasonic source and receiver probes for 1.5-or 2-inch inner diameter pipe, as appropriate.

3.	An ultrasonic voltage pulser to excite the source with a synchronized triggering system to start the recording system.

4.	A depth measurement device to determine and record depths.

5.	Appropriate filter/amplification and cable systems for CSL testing.

51X.03  CONSTRUCTION

51X.03.01  Working Drawings and Calculations.

Submit six (6) copies of the following items to the RE for approval:

1.	A summary of the Contractor’s or his specialized drilled shaft Subcontractor's experience on projects of a similar nature and scope.  Select and obtain approval from the RE for the use of a specialty subcontractor.  Approval will be based on qualifications and previous experience on similar projects.

2.	List and size of proposed equipment including cranes, drills, augers, bailing buckets, final cleaning equipment, desanding equipment, slurry pumps, concrete pumps, temporary steel casing, slurry sampling and testing equipment.

3.	Details of equipment and procedures for drilled shaft installation, including drawings showing consecutive steps of drilled shaft installation and drawings with measurements showing that the proposed equipment can perform the specified work.  Identify in the drawings the areas that are planned to be used for staging the work.  Specify the proposed sequence of the drilled shaft installation including details of concrete placement and splicing and centering devices for reinforcement steel.

4.	Approval for the concrete mix design that is to be used for the work.

5.	Slurry details including proposed methods of mixing, placing and circulating.

6.	Details of shaft excavation methods.

7.	Details of proposed methods to clean the shaft after initial excavation.

8.	Procedures for control and removal of spoils.

9.	Details of shaft reinforcement steel, including methods to ensure centering, required cover, cage integrity during placement, placement procedures and cage support.

10.	Details of concrete placement including proposed operational procedures for concrete pump or tremie including initial placement, raising during placement, overfilling of the shaft concrete and provisions to prepare the completed shaft top at its final shaft top elevation.

51X.03.02  Shaft Drilling.

Perform the excavations required for the shafts through whatever materials are encountered, to the dimensions and elevations shown in the plans or otherwise required by these specifications.  Ensure that the equipment is capable of constructing shafts to a depth equal to the deepest shaft shown in the plans plus 15 feet or three times the shaft diameter, whichever is greater.

Provide, for all drilled shafts, an approved fixed template that is adequate to maintain the shaft position and alignment during all excavation and concreting operations.

Install a suitable temporary casing for the full depth of the drilled shaft.  Ensure that all drilled shafts meet construction tolerance criteria and are installed in accordance with the dimensions as shown on the plans, or as directed by the RE.

Ensure that the top center of each drilled shaft does not vary from the plan location by more than 3 inches.  At the top of the drilled shaft, ensure that reinforcement steel does not vary in plan distance from the plan shaft by more than 1 inch.  Ensure that the drilled shaft does not vary from the vertical by more than one percent of its length, as measured above ground and is not out of the required position at the top by more than 3 inches.

Protect any existing utility that is to remain within the drilled shaft installation work zone in accordance with the requirements of authorities having jurisdiction over same.  Repair or replace any construction-induced damage to the satisfaction of the governing authority.

Employ within the contract bid price, a licensed registered Land Surveyor, experienced in the type of work, who will establish lines and grades.  Assume responsibility for the correct location of drilled shafts and for keeping a record of drilled shafts that are installed.

Locate the drilled shaft locations and provide a stake out of the locations prior to the start of installation work.  Maintain all location stakes along with required elevation designations.

51X.03.03  Shaft Concrete.

Ensure that the handling, measuring, proportioning, mixing and placing of concrete conforms to these Specifications.  Place concrete only in the presence of the RE.

Place concrete by using concrete pumps or a tremie pipe from the bottom of the excavation upward so as to avoid segregation.  Do not inject air, water or slurry into the shaft concrete during placement.  Use a disposable foam or rubber plug in the concrete pump line or tremie pipe to separate the fresh concrete from the slurry at the start of concrete placement.  Insert the plug so that the first flow of concrete pushes the plug out of the pipe and prevents slurry mixing and contamination as the concrete placement commences.  Ensure that the concrete pump line or tremie consists of a tube constructed in sections that have flanged couplings fitted with gaskets.  Ensure the means of supporting the concrete pump line or tremie so as to permit free movement of the discharge end over the entire top of the concrete and to permit its being lowered rapidly when necessary to choke off or retard the flow.  If used, fill the tremie by a method that prevents washing of the concrete.  Submerge the discharge end completely in the concrete at all times after initiation of the concrete placement flow.  Ensure that the concrete line contains sufficient concrete to prevent any water entry.  Maintain the concrete level at the top of the drilled shaft until the concrete has set.

If concrete flow is halted and the concrete line’s discharge end is for any reason raised out of the shaft concrete, reinitiate the placement only after fully recharging the concrete line with fresh concrete by

1.	Inserting a foam or rubber plug or pig into the concrete line at the concrete hopper end,

2.	Placing the discharge end approximately 6 inches above the top of the shaft concrete,

3.	Recharging the pump or tremie line and depositing what will be classified as waste concrete on the top of the previously placed concrete,

4.	Discharging waste concrete until the line is fully recharged with fresh concrete and the pig is pushed completely through the line,

5.	Without halting the flow of fresh concrete plunging the discharge end of the concrete line into the shaft concrete to within 6 inches or less of the shaft bottom or to a level as directed by the RE,

6.	Continuing the concrete placement without further interruption, and

7.	Placing a final volume of additional concrete in the shaft that is no less than the volume of waste concrete placed to recharge the line in the process of resuming the concrete flow.

Apply this procedure without exception as necessary to avoid injecting any air, any water, any slurry, or any concrete that has flowed through a line filled with air, water, or slurry into the shaft concrete.

Do not initiate boring a new shaft hole that is within five drilled shaft diameters of a previously installed drilled shaft, until the concrete has been in place for a minimum of 2 days.

51X.03.04  Shaft Construction Timing.

Make every effort to plan, coordinate and carry out the work to minimize the time between the start of excavation and completion of shaft concrete placement.  In general, the time between shaft excavation and completion of concrete placement is expected to be eight (8) continuous hours or less.

For cases where two (2) or more continuous hours elapse between completion of excavation and commencement of concrete placement, remove any reinforcement steel already placed in the shaft, clean the shaft bottom, replace the reinforcement steel in the shaft and immediately commence the placement of the concrete.

51X.03.05  Shaft Reinforcement Steel.

Where shafts are extended at the direction of the RE to final authorized tip elevations that are lower than the estimated minimum tip elevations, extend no fewer than one-half of the vertical reinforcement steel (every other bar around the circumference) to the authorized tip elevation by lap splicing or mechanical splicing.  Firmly tie lap splices so as to support the full weight of the cage above the lap zone.  Add horizontal bands in the bottom extension zone at a vertical spacing that is no more than 6 inches center to center.

51X.03.06  Shaft Top Preparation.

If tremie concrete is used, consider the top-most concrete placed in the shaft to be waste concrete and either:

1.	Completely eject out of the top of the casing the wasted concrete or,

2.	Pump the waste upward to a level that is at least 2 feet clear distance above the plan shaft top level and allow it to cure in place for removal later.

Consider waste concrete to be the top 2 feet of initial concrete that is placed, plus

1.	The height of any additional volume of waste concrete deposited in the shaft where concrete placement was halted and restarted, plus

2.	Any additional amount necessary to produce full strength non-segregated concrete at the plan shaft top level.

Where the above waste concrete alternative 1 is selected, permit the waste concrete to evenly overflow the full top circumference of the casing.  Do not channel or bleed off by notches or holes cut in the casing top.  Any fresh concrete in the casing at a level above the plan shaft top level after ejecting all waste concrete may be dipped or pumped out to the plan top elevation while still plastic by methods and equipment approved by the RE, or be allowed to cure in place for removal later.

Final shaft top preparation may commence only after the drilled shaft concrete obtains its verification strength.  In lieu of concrete strength testing, the preparation may begin seven (7) full days after completion of concrete placement.  Final top preparation steps will consist of:

1.	Cutting off any extra casing above the top of casing elevation,

2.	Cutting off any cured over pour concrete to the plan shaft top elevation by approved methods,

3.	Dressing the final shaft top surface,

4.	Verification by the RE that the exposed concrete consists of full strength concrete with a typical, non-segregated mortar and aggregate distribution,

5.	Approved non-destructive strength testing by the Contractor where required by the RE to verify that concrete has attained its full design strength,

6.	Removal of additional concrete below the plan shaft top level as necessary to reach full-strength, non-segregated concrete, and

7.	Preparation of the shaft top key recess.

51X.03.7  Shaft Acceptance.

Provide a comparison of the computed volume of the excavation (theoretical) with the volume of concrete actually placed.  Plot depth versus volume chart.  Provide cooperation and whatever assistance necessary to accurately monitor the volume of concrete that is placed at all times during the pour.

Unaccepted drilled shafts are drilled shafts that are rejected by the RE because of damage, failure to advance through obstructions, mislocation, misalignment or failure to install the drilled shaft to the proper bearing stratum.  Submit a written plan of action to the RE for approval showing how to correct any problem and how to prevent a reoccurrence.  Repair the drilled shaft or replace it to the satisfaction of the RE.  To mitigate and/or to remedy unaccepted drilled shafts, the Contractor may be required to provide additional drilled shafts or supplement drilled shafts to meet specified requirements at no cost to the State.

When acceptably installed drilled shafts exceed specified tolerances, provide an accurate as-built survey.  If the load on any drilled shaft exceeds 10 percent of the specified load capacity, make as directed corrections.

51X.04  Measurement and Payment

The Department will measure and make payment as follows:

Item	Pay Unit

DRILLED SHAFT FOR SIGN STRUCTURE FOUNDATION	LINEAR FOOT

1********************************************************************************************************1

Division 600 – Miscellaneous Construction

Section 606 – Sidewalks, Driveways, and Islands

606.03.02  Concrete Sidewalks, Driveways, and Islands

H.	Protection and Curing.

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

THE last SENTENCE IS CHANGED TO:

Ensure vehicles and other loads are not placed on sidewalks, islands, and driveways until the concrete has attained compressive strength of 3000 pounds per square inch, as determined from 2 concrete cylinders field cured according to AASHTO T 23.

1********************************************************************************************************1

1********************************************************************************************************1

BDC09s-08 dated DEC 7, 2009

609.03.01 Beam Guide Rail

THE SEVENTH PARAGRAPH IS CHANGED TO:

Install flexible delineators with white retro reflective sheeting on the right side of the direction of traffic. Install flexible delineators with yellow retro reflective sheeting on the left side of the direction of traffic. Mount flexible delineators on BDC09S-10 Page 2 of 3 the block out of beam guide rail using either a “U” channel base on the I-beam block out or a flat base attached to a wood, polymer, or other solid top block out. Attach the base to the block out using an adhesive recommended by the manufacturer of the base and panel.

610.03.06 Ground Mounted Flexible Delineators

THE FIRST PARAGRAPH IS CHANGED TO:

Use white retro reflective sheeting for delineators located on the right side when facing in the direction of traffic. Use yellow retro reflective sheeting for delineators located on the left side when facing in the direction of traffic.

1********************************************************************************************************1

Section 610 – Traffic Stripes, Traffic Markings, and Rumble Strips

610.04  Measurement and Payment

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

THE FOLLOWING ITEM IS DELETED:

Item	Pay Unit

RPM, BI-DIRECTIONAL, WHITE LEns	UNIT

1********************************************************************************************************1

Section 611 – Crash Cushions

611.03.02  Crash Cushion

1********************************************************************************************************1

Complete and include the following

Use ____________ crash Cushion(s) on the project.

1********************************************************************************************************1

section 612 – signs

612.02	materials

1********************************************************************************************************1

BDC09s-01 dated apr 09, 2010

The following is deleted from the Materials list.

Non-Breakaway Sign Supports	911.02.03

the second paragraph is deleted.

1******************************************************************************************************1

612.03.02  Type GA Breakaway and Non-Breakaway Support Guide Signs

1********************************************************************************************************1

BDC09s-01 dated apr 09, 2010

The subpart Heading is changed to:

612.03.02  Type GA Breakaway Support Guide Signs

1********************************************************************************************************1

612.03.02  Type GA Breakaway Support Guide Signs

1******************************************************************************************************1

BDC09s-01 dated apr 09, 2010

C.	Constructing Pedestals

The Subpart is changed to:

Place reinforcement steel as specified in 504.03.01 before placing the concrete.  Ensure that concrete placement complies with the limitations as specified in 504.03.02.C.  Place concrete as specified in 504.03.02.D.  Cure concrete as specified in 504.03.02.F.

D.	Erecting Posts

The Subpart is changed to:

Erect posts as specified in 512.03.01.G.

the following is added:

F.	Constructing Anchor, Hinge, Bracket and Coupling Assemblies..At least 10 days before beginning the work, submit the manufacturer’s installation guide and installer’s certification to the RE.

Ensure that the installer is certified by the manufacturer.

Ensure that the manufacturer’s representative is present during the foundation pour and the installation of the first sign.  Install anchor, hinge, bracket and coupling assemblies according to the manufacturer’s recommendations.  The RE may require the system manufacturer’s representative to be present at all times during the installation to provide on-site technical support.

1*******************************************************************************************************1

612.04	measurement and payment

1******************************************************************************************************1

BDC09s-01 dated apr 09, 2010

The following Item is deleted:

Item	Pay Unit

GUIDE SIGN, TYPE GA, NON-BREAKAWAY SUPPORTS	SQUARE foot

1********************************************************************************************************1

1******************************************************************************************************1

include specifications upon ASSIGNING an APPROPRIATE SECTION/SUBSECTION NUMBERs if noise barriers are required

The following section is added:

Section 61x – noise barriers

1********************************************************************************************************1

1**************************************************************************************************1

include specifications upon ASSIGNING an APPROPRIATE SECTION/SUBSECTION NUMBERs if Architectural Treatments are required

The following section is added:

Section 61X – Architectural Treatments

1*****************************************************************************************************1

1*******************************************************************************************************1

include specifications upon ASSIGNING an APPROPRIATE SECTION/SUBSECTION NUMBERs if RUBBLE walls are required

sme

The following section is added:

Section 61x – RUBBLE walls

1*****************************************************************************************************1

Division 650 – Utilities

Section 651 – Water

1********************************************************************************************************1

651.02  Materials

include additional materials requirements as needed

*******************************************************************************************************1

1*******************************************************************************************************1

651.03.02  Water Pipe, Bridge

include OTHER CONSTRUCTION REQUIREMENTS AS NEEDED.

1*****************************************************************************************************1

Section 652 – Sanitary Sewers

1******************************************************************************************************1

652.02  Materials

include additional materials requirements as needed

1****************************************************************************************************1

652.03.01  Sewer Pipe

F.	Thrust Blocks.

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

The third sentence is changed to:

Ensure that thrust blocks do not come in contact with other utilities or structures without the approval of the RE.

1*****************************************************************************************************1

H.	Sewer Pipe Testing.

1.	Gravity Main Sewer Testing.

1******************************************************************************************************1

include leakage testing list

1

652.03.02  Sanitary Sewer Pipe, Bridge

1******************************************************************************************************1

INCLUDE Specification

1

Section 653 – Gas

653.03.01  Gas Main

A.	Prequalification.

1********************************************************************************************************1

INCLUDE list of pre-qualified subcontractors

List of pre-qualified subcontractors is as follows:

1*******************************************************************************************************1

C.	Handling and Storing.

1********************************************************************************************************1

INCLUDE utility location for pickup and return

1*****************************************************************************************************1

J.	Air-Pressure Test.

1*******************************************************************************************************1

INCLUDE pressures and durations for test

1**************************************************************************************************1

1**************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

Division 700 – Electrical

Section 701 – General Items

701.03.01  Existing Systems

1********************************************************************************************************1

provide the location to deliver and unload salvaged materials. different locations may be specified for electrical and/or its materials.

Deliver and unload salvaged materials to:

1********************************************************************************************************1

701.03.05  Rigid Nonmetallic Conduit

B.	Installation.

1*******************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

the last paragraph is changed to:

Install true tape marked in 1 foot increments for the length of the rigid non-metallic conduit.  Install a tracer wire continuously for the entire run of 1 of the conduits, including through the junction boxes mounted on the wall.  Splice the tracer wire only in the junction boxes.  Seal the rigid nonmetallic conduit with the tracer wire.  If wire or cable is not scheduled to be installed within the next 6 months, cap and seal the other conduits leaving the true tape inside.  Install marking tape in the trench above the conduit.

1*******************************************************************************************************1

701.03.07  Flexible Nonmetallic Conduit

B.	Installation.

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

the second paragraph is changed to:

Cut flexible nonmetallic conduit according to manufacturer’s recommendations.

the last paragraph is changed to:

Install true tape marked in 1 foot increments for the length of the flexible non-metallic conduit. Install a tracer wire continuously for the entire run of conduits, including through the junction boxes mounted on the wall.  Splice the tracer wire only in the junction boxes.  Seal the flexible nonmetallic conduit with the tracer wire.  If wire or cable is not scheduled to be installed within the next 6 months, cap and seal the other conduits leaving the true tape inside.  Install marking tape in the trench above the conduit.

1********************************************************************************************************1

701.03.15  Cable and Wire

C.	Connection and Coordination with Utility Services.

1*******************************************************************************************************1

confirm on the requirements for interim communication and power connections, and connections to njta network.  Also, for establishment of ip addresses, interim and permanent.

The following is added to the fourth paragraph:

At Substantial Completion, provide the RE with the letter of transfer from each utility company to be effective the next month after Substantial Completion or as directed by the RE.

1********************************************************************************************************1

701.04  Measurement and Payment

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

THE FOLLOWING IS ADDED:

If restoration of disturbed areas includes sidewalks, driveways and islands, the Department will make measurement and payment for sidewalks, driveways and islands as specified in 606.04.

1*******************************************************************************************************1

Section 702 – Traffic Signals

702.03  Construction

The following is added:

After placing a new, temporary or interim traffic signal system into operation, inspect the traffic signal system every 2 months.  Fill out a Contractor Maintenance Traffic Signal Inspection Report (Form EL-16C) when the traffic signal system becomes operational, when the traffic signal system is modified, and at every 2-month inspection.

Maintain as-built drawings of each signal modification.  Place copies of the as-built drawings for each traffic signal system modification, Forms EL-16C, and Forms EL-11C in a plastic pocket mounted inside the cabinet door of each controller cabinet.  Also provide a copy of all forms and as-built drawings to the RE.

If a new, temporary or interim traffic signal system fails or becomes damaged, repair and restore the traffic signal system to normal operation.  Begin repair of the traffic signal system within 2 hours of receiving notice of damage or malfunction from the Department, State police, or local authorities.  Ensure that workers assigned to such repair work continuously until the traffic signal resumes normal signal operation.

For each response to a system failure or damage, fill out a Contractor Maintenance Emergency Call Record (Form EL-11C) and place it in a plastic pocket mounted inside the cabinet door of each controller cabinet.

If the Contractor fails to respond to a failure or damage notification and begin work within 2 hours of notification, or does not continue to work until the traffic signal system resumes normal operation, the Department, in the interest of safety, will respond with its own forces to restore normal operation.  If the Department mobilizes its forces to effect repairs, the Contractor agrees to pay the Department a sum of $3000 for costs of mobilizing its forces and equipment.  In addition, the Contractor must pay the Department the actual cost of material used for the repair and pay the actual costs of police traffic protection.

702.03.11  Temporary and Interim Traffic Signal Systems

the first THROUGH FIFTH PARAGRAPHs are deletED:

Section 703 – highway lighting

703.03  Construction

The following is added:

Maintain up-to-date as-built drawings of the highway lighting system and temporary highway lighting system.  Place copies of the as-built drawings in a plastic pocket mounted inside the meter cabinet, and provide a copy to the RE

If the highway lighting system or temporary highway lighting system fails or becomes damaged, repair and restore the system to normal operation.  Begin repair of the signal system within 2 hours of receiving notice of damage or malfunction from the Department, State police, or local authorities.  Ensure workers assigned to such repair work continuously until the lighting system is restored to normal operation.

For each response to a system failure or damage, fill out a Contractor Maintenance Emergency Call Record (Form EL-11C) and place it in a plastic pocket mounted inside the cabinet door of each controller cabinet.

If the Contractor fails to respond to a failure or damage notification and begin work within 2 hours of notification, or does not continue to work until the lighting system is restored to normal operation, the Department, in the interest of safety, will respond with its own forces to restore normal operation.  If the Department mobilizes its forces to effect repairs, the Contractor agrees to pay the Department a sum of $3000 for costs of mobilizing its forces and equipment.  In addition, the Contractor must pay the Department the actual cost of material used for the repair and pay the actual costs of police traffic protection.

703.03.07  Temporary Highway Lighting System

1*******************************************************************************************************1

2**************************************************************************************2

Determine whether or not the Contractor must design the Temporary lighting system at a given location and include the following

The Contractor must design the Temporary lighting system at ___________________________

2**************************************************************************************2

2**************************************************************************************2

provide the locations to deliver and unload salvaged materials

Deliver and unload salvaged materials to:

2**************************************************************************************2

2**************************************************************************************2

the sixth PARAGRAPH is deletED:

the EIGHTH THROUGH tenth PARAGRAPHs are deletED:

2**************************************************************************************2

1*******************************************************************************************************1

Section 704 – Intelligent Transportation Systems (ITS)

1********************************************************************************************************1

if project includes connection to njta network, including direct fiber or wireless, confirm with its engineering on coordination requirements with njta.

1**************************************************************************************************1

704.03.01  General System (GS)

B.	Installation.

1*****************************************************************************************************1

2**************************************************************************************2

complete and include the following.

INsert THE existing system shutdown time frames, including days of the week, specific dates, and/or hours of the day(s).

The Department will allow existing system shutdowns for work at the _____________ Center from _____.  For each half hour the work extends beyond those time frames, the Department will assess liquidated damages of $500 per half hour.

2**************************************************************************************2

2**************************************************************************************2

INCLUDE THE PROJECT SPECIFIC CONSTRUCTION REQUIREMENTS not addressed in the plans/details for the control center system work required at the existing centers, and the controller its or communications hub.

6.	Control Center System.

BDC08s-02 dated Feb 17, 2009

THE FOLLOWING IS ADDED:

Supply and install equipment, software, software revisions, firmware and miscellaneous wiring and cabling required for the turn key remote operation of ITS field devices by the Department from the designated Traffic Operation Center.  Perform work as required to integrate the proposed systems into the various existing operating systems or subsystems used by the Department.  Comply with building installation requirements, restrictions and security requirements in the performance of work.  Submit a request for access to the RE at least 6 days in advance of work scheduled to be performed at a center.

2**************************************************************************************2

1**************************************************************************************************1

C.	Testing.

1*******************************************************************************************************1

2**************************************************************************************2

BDC08s-02 dated Feb 17, 2009

THE first paragraph IS CHANGED TO:

Perform wiring and cable testing, as specified in 701.03.15.D, before performing any other testing.  Complete the item, device and system testing as specified on the Department provided forms and instructions.

1.	Device Testing.

b.	Level B.

THE first SENTENCE IS CHANGED TO:

Demonstrate that each device is fully operational from the designated control center to the work site with the original equipment manufacturer’s software.

2**************************************************************************************2

2**************************************************************************************2

2.	Project Testing.

THE first sentence of the SECOND PARAGRAPH is CHANGED TO:

After the Contractor’s verification test, the Department will conduct a 14-day observational and functional test period of all systems on the Project.

2**************************************************************************************2

704.03.02  Camera Surveillance System (CSS)

B.	Installation.

1*******************************************************************************************************1

2**************************************************************************************2

complete and include the following.

INsert THE existing system shutdown time frames, including days of the week, specific dates, and/or hours of the day(s).

The Department will allow existing camera system shutdowns from _____.  For each half hour the work extends beyond those time frames, the Department will assess liquidated damages of $500 per half hour.

2**************************************************************************************2

2**************************************************************************************2

The following is added:

If directed by the RE, provide a bucket truck with safety equipment that can reach the height of the camera.  Operate the bucket truck for the Department to use to determine the camera’s final location and orientation, and for testing.

2**************************************************************************************2

2**************************************************************************************2

BDC08s-02 dated Feb 17, 2009

1.	Foundation CSS.

THE FOLLOWING IS ADDED:

Ensure that the anchor bolts are placed upon verification of the orientation of the lowering device to minimize the obstruction of desired camera view by the Camera Standard.

2.	Camera Standard.

THE FOLLOWING IS ADDED:

At least 30 days before beginning construction, submit working drawings for approval that include structural calculations meeting the specified criteria.  Ensure the calculations are signed and sealed by a Professional Engineer.

3.	Camera.

The first paragraph is changed to:

Mount the camera housing and camera according to the manufacturer’s recommendation.  Ensure that the camera’s field of view is unobstructed.  Perform tree trimming and site clearing to provide an unobstructed field of view as directed by the RE.  Set up “On Screen Display” to indicate the quadrant views with directional titles (e.g. NB view, EB view, SB view, WB view) displayed in the bottom right corner of the screen for each camera.  Leave the display blank for any quadrant not representing any highway view.  For a camera with multiple highway views, include route and directional title (e.g. Rt 1 NB view).  Also, establish a pan and tilt zones system and set up 4 presets for quick pan-tilt-zoom views prior to level B testing.  At least 6 days prior to Level C testing, submit a request to the RE for the Department to integrate each camera into the Nextiva control software.

2**************************************************************************************2

2**************************************************************************************2

The fourth paragraph is deleted.

2**************************************************************************************2

1*******************************************************************************************************1

F.	Equipment Training.

1********************************************************************************************************1

provide recommendation prior to final design submission for any special training, and/or if more than 10 personnel require the training.

1***************************************************************************************************1

704.03.03  Fiber Optic Cable

B.	Installation.

1*******************************************************************************************************1

complete and include the following.

INsert THE existing system shutdown time frames, including days of the week, specific dates, and/or hours of the day(s).

The Department will allow existing system shutdowns on the fiber network from _____.  For each half hour the work extends beyond those time frames, the Department will assess liquidated damages of $500 per half hour.

1**************************************************************************************************1

C.	Testing

1*******************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

The last paragraph is changed to:

After completion of Level 1 and 2 tests, perform network communication system testing and demonstrate that the communication system is fully operational to meet the material specifications and project requirements.  Complete the testing as specified on the Department provided forms and instructions.

1************************************************************************************************1

F.	Equipment Training.

1********************************************************************************************************1

provide recommendation prior to final design submission for any special training, and/or if more than 10 personnel require the training.

1********************************************************************************************************1

704.03.04  Controlled Traffic Signal System (CTSS)

B.	Installation.

1********************************************************************************************************1

complete and include the following.

INsert THE existing system shutdown time frames, including days of the week, specific dates, and/or hours of the day(s).

The Department will allow existing CTSS system shutdowns from _____.  For each half hour the work extends beyond those time frames, the Department will assess liquidated damages of $500 per half hour.

1******************************************************************************************************1

C.	Testing.

1******************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

THE FIRST PARAGRAPH IS CHANGED TO:

Perform testing as specified in 704.03.01.C, except do not perform Level B Testing.

1********************************************************************************************************1

F.	Equipment Training.

1********************************************************************************************************1

provide recommendation prior to final design submission for any special training, and/or if more than 10 personnel require the training.

1

704.03.05  Travel Time Systems (TTS)

B.	Installation.

1********************************************************************************************************1

complete and include the following.

INsert THE existing system shutdown time frames, including days of the week, specific dates, and/or hours of the day(s).

The Department will allow existing TTS system shutdowns from _____.  For each half hour the work extends beyond those time frames, the Department will assess liquidated damages of $500 per half hour.

1******************************************************************************************************1

C.	Testing.

1*******************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

THE FOLLOWING IS ADDED:

For TTS with transmit, both Level B and Level C Testing will be done with integration into TRANSCOM;s transmit software control system and the control center software management systems.

1********************************************************************************************************1

F.	Equipment Training.

1********************************************************************************************************1provide recommendation prior to final design submission for any special training, and/or if more than 10 personnel require the training.

1*******************************************************************************************************1

704.03.06  Road Weather Information System (RWIS)

B.	Installation.

1*********************************************************************************************************1complete and include the following.

INsert THE existing system shutdown time frames, including days of the week, specific dates, and/or hours of the day(s).

The Department will allow existing RWIS system shutdowns from _____.  For each half hour the work extends beyond those time frames, the Department will assess liquidated damages of $500 per half hour.

1********************************************************************************************************1

F.	Equipment Training.

1********************************************************************************************************1

provide recommendation prior to final design submission for any special training, and/or if more than 10 personnel require the training.

1*****************************************************************************************************1

704.03.07  Dynamic Message System (DMS)

B.	Installation.

1******************************************************************************************************1

2**************************************************************************************2

complete and include the following.

INsert THE existing system shutdown time frames, including days of the week, specific dates, and/or hours of the day(s).

The Department will allow existing DMS system shutdowns from _____.  For each half hour the work extends beyond those time frames, the Department will assess liquidated damages of $500 per half hour.

2**************************************************************************************2

2.	DMS Standard.

2**************************************************************************************2

until dms standard details are issued, Designer must contact its engineering prior to design on requirements for any proposed sites.  for proposed signs on ohss and bridge sites, those structures are still covered under Division 500.

2**************************************************************************************2

5.	DMS Sign Install and DMS Sign With Controller Install.

2**************************************************************************************2

BDC08s-02 dated Feb 17, 2009

VERIFY and REVISE if necessary, THE 4 MONTH DELIVERY TIME AFTER THE AWARD TO APPROPRIATE TIME FRAME BASED ON THE STAGING PLAN TO PREVENT EARLY DELIVERIES OF DMS SIGNS AND ASSOCIATED STORAGE REQUIREMENTS.

THE first PARAGRAPH is CHANGED TO:

Submit working drawings that include sign mounting and lifting calculations, and controller installation requirements.  Ensure the calculations are signed and sealed by a Professional Engineer.  Within 25 days after execution of the Contract, provide the address of the location for the delivery of the specified DMS signs.  Inspect and provide notice of acceptance as specified in 106.02.  The Department will provide for delivery of the signs within 4 months of award of the Contract.  Mount the sign on the standard, and make all wire and cable connections to the DMS sign controller according to the sign manufacturer’s recommendations.  When required by the type of sign, securely bolt the controller to the foundation in a vertical position using stainless steel hardware.  Seal the underground conduit entrance to the controller with a sealing compound.  Coordinate with the manufacturer, and provide access and support, for any warranty work covered by the DMS material.  Submit requests for warranty work in writing to the RE.  Details of the warranty will be provided with each DMS material, and includes replacement of the unit if the manufacturer can not fix the problem within one week.

2**************************************************************************************2

1****************************************************************************************************1

C.	Testing.

1*******************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

THE FOLLOWING IS ADDED:

For DMS specified for integration in Traffic Operations Center South, both Level B and Level C Testing will be done with integration into the Vanguard control software system.

1*****************************************************************************************************1

F.	Equipment Training.

1********************************************************************************************************1

provide recommendation prior to final design submission for any special training, and/or if more than 10 personnel require the training.

1*******************************************************************************************************1

704.03.08  Weigh in Motion System (WIMS)

B.	Installation.

1******************************************************************************************************1

complete and include the following.

INsert THE existing system shutdown time frames, including days of the week, specific dates, and/or hours of the day(s).

The Department will allow existing WIMS system shutdowns from _____.  For each hour the work extends beyond those time frames, the Department will assess liquidated damages of $1000 per hour.

1*******************************************************************************************************1

F.	Equipment Training.

1*******************************************************************************************************1

provide recommendation prior to final design submission for any special training, and/or if more than 10 personnel require the training.

1******************************************************************************************************1

704.03.09  Traffic Volume System (TVS)

B.	Installation.

1********************************************************************************************************1

complete and include the following.

INsert THE existing system shutdown time frames, including days of the week, specific dates, and/or hours of the day(s).

The Department will allow existing TVS system shutdowns from _____.  For each hour the work extends beyond those time frames, the Department will assess liquidated damages of $1000 per hour.

1******************************************************************************************************1

F.	Equipment Training.

1********************************************************************************************************1

provide recommendation prior to final design submission for any special training, and/or if more than 10 personnel require the training.

1*****************************************************************************************************1

Division 800 – Landscaping

Section 811 – Planting

811.03.01  Planting

E.	Excavation for Plant Pits and Beds.

1*******************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

THE last SENTENCE OF THE second PARAGRAPH IS CHANGED TO:

Obtain RE approval before reusing topsoil from the excavated pits.

1*****************************************************************************************************1

I.	Watering.

1****************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

THE first PARAGRAPH IS CHANGED TO:

Water plants with sufficient frequency and quantity to ensure that the soil surrounding the root system remains moist but not saturated.

1***************************************************************************************************1

811.03.02  Plant Establishment Period

1******************************************************************************************************1

2**************************************************************************************2

complete and include THE FOLLOWING

THE third and fourth paragraphs are changed to:

The Department will reinspect the plants annually for _____ years, beginning approximately 1 year after the start of the plant establishment period.  If the Department determines that plants need to be replaced after each inspection, replant plants as specified in 811.03.01 within 3 weeks of notification.  If replacing outside of the optimal planting season as specified in Table 811.03.01-1, only use containerized or balled and burlapped plants that are certified as being dug dormant.

2**************************************************************************************2

2.	Maintenance Bond.

2**************************************************************************************2

complete and include the bond amount (a percentage of planting value)

Provide a bond to the Department in the amount of $_____________.

2**************************************************************************************2

1******************************************************************************************************1

Division 900 – Materials

Section 901 – Aggregates

901.11  Soil Aggregate

1.	Composition of Soil Aggregate.

1*******************************************************************************************************1

BDC10s-03 dated Mar 17, 2010

The following is added to the last paragraph:

For Designation I-14, the Contractor may use up to 30 percent steel slag by weight of the coarse aggregate portion of the soil aggregate.  Obtain steel slag from a source listed on the QPL as specified in 901.01.  Use steel slag that was produced as a co-product of the steel making process.  Ensure that the steel slag consists of tough, durable pieces that are uniform in density and quality.  Stockpile steel slag as specified in 901.02.  Ensure steel slag for blending with I-14 Soil Aggregate does not exceed 0.50 percent expansion from hydration when tested according to ASTM D 4792.

SECTION 902 –ASPHALT

902.02.03  MIX DESIGN

THE FOLLOWING IS ADDED TO THE FIRST PARAGRAPH:

UNLESS OTHERWISE APPROVED BY THE ENGINEER, ONLY ONE SOURCE OF SUPPLY FOR HOT MIX ASPHALT SURFACE COURSE MAY BE USED ON THE PROJECT.

902.02.04 SAMPLING AND TESTING

*******************************************************************************************************************************

DETERMINATION OF CONFORMANCE TO THE VOLUMETRIC PROPERTIES BY SAMPLING AND TESTING AT THE HMA PLANT BY AN INDEPENDENT TESTING AGENCY AND/OR LABORATORY IS PREFERRED; HOWEVER, THE FOLLOWING CHANGES TO SUBSECTION 902.02.04 MAY BE USED AS AN ALTERNATE TO THE SAMPLING AND TESTING PROVISIONS LISTED IN SUBSECTION 902.02.04 TO DETERMINE CONFORMANCE TO THE SPECIFICATION REQUIREMENTS.

*******************************************************************************************************************************

THE FOLLOWING IS ADDED TO 902.02.04:

F.	Acceptance of HMA.  The Department may accept the HMA as specified in 902.02.04.A through 902-02.04 E by employing staff or an independent testing agency at the HMA plant during production.  The inspector who performs the quality assurance sampling shall be certified by the Society of Asphalt Technologists of New Jersey as an Asphalt Plant Technologist, Level 2.

Alternatively, the Department may accept the HMA by Certification of Compliance according to 106.07.

1*******************************************************************************************************1

Section 903 – Concrete

903.03.05  Control and Acceptance Testing Requirements

E.	Acceptance Testing for Strength for Pay-Adjustment Items.

1*******************************************************************************************************1

INCLUDE ONLY THE APPLICABLE ITEMS for pay adjustment

Concrete Items which are subject to pay adjustment and the base prices are as follows:

| ITEMS | DESCRIPTION | UNIT | BASE PRICE |
| --- | --- | --- | --- |
| 507021P | CONCRETE BRIDGE DECK | CY | $500.00 |
| 507036P | CONCRETE BRIDGE PARAPET | LF | $305.00 |
| 505039P | PRESTRESSED CONCRETE SLAB BEAM, (TYPE SII-36), 36" X 15" | LF | $125.00 |
| 505042P | PRESTRESSED CONCRETE SLAB BEAM, (TYPE SIII-36), 36" X 18" | LF | $130.00 |
| 505015P | PRESTRESSED CONCRETE BOX BEAM, (TYPE BI-36), 36" X 27" | LF | $170.00 |
| 505045P | PRESTRESSED CONCRETE SLAB BEAM, (TYPE SIV-36), 36" X 21" | LF | $160.00 |
| 505018P | PRESTRESSED CONCRETE BOX BEAM, (TYPE BII-36), 36" X 33" | LF | $170.00 |
| 505021P | PRESTRESSED CONCRETE BOX BEAM, (TYPE BIII-36), 36" X 39" | LF | $175.00 |
| 505024P | PRESTRESSED CONCRETE BOX BEAM, (TYPE BIV-36), 36" X 42" | LF | $185.00 |
| 505003P | PRETENSIONED PRESTRESSED CONCRETE BEAM, 45" | LF | $155.00 |
| 505006P | PRETENSIONED PRESTRESSED CONCRETE BEAM, 54" | LF | $155.00 |
| 505048P | PRESTRESSED CONCRETE SLAB BEAM, (TYPE SII-48), 48" X 15" | LF | $160.00 |
| 505051P | PRESTRESSED CONCRETE SLAB BEAM, (TYPE SIII-48), 48" X 18" | LF | $135.00 |
| 505009P | PRETENSIONED PRESTRESSED CONCRETE BEAM, 63" | LF | $185.00 |
| 505027P | PRESTRESSED CONCRETE BOX BEAM, (TYPE BI-48), 48" X 27" | LF | $215.00 |
| 505054P | PRESTRESSED CONCRETE SLAB BEAM, (TYPE SIV-48), 48" X 21" | LF | $215.00 |
| 505030P | PRESTRESSED CONCRETE BOX BEAM, (TYPE BII-48), 48" X 33" | LF | $185.00 |
| 505033P | PRESTRESSED CONCRETE BOX BEAM, (TYPE BIII-48), 48" X 39" | LF | $220.00 |
| 505036P | PRESTRESSED CONCRETE BOX BEAM, (TYPE BIV-48), 48" X 42" | LF | $230.00 |
| 505012P | PRETENSIONED PRESTRESSED CONCRETE BEAM, 72" | LF | $200.00 |
| 502045M | CAST-IN-PLACE CONCRETE PILE, DRIVEN, 12" DIAMETER | LF | $50.00 |
| 502090M | PRECAST CONCRETE PILE, DRIVEN, 12" X 12" | LF | $90.00 |
| 502132M | PRESTRESSED CONCRETE PILE, DRIVEN, 12" X 12" | LF | $50.00 |
| 502135M | PRESTRESSED CONCRETE PILE, DRIVEN, 14" X 14" | LF | $50.00 |
| 502138M | PRESTRESSED CONCRETE PILE, DRIVEN, 16" X 16" | LF | $50.00 |
| 502141M | PRESTRESSED CONCRETE PILE, DRIVEN, 18" X 18" | LF | $50.00 |
| 502144M | PRESTRESSED CONCRETE PILE, DRIVEN, 20" X 20" | LF | $75.00 |
| 502147M | PRESTRESSED CONCRETE PILE, DRIVEN, 22" X 22" | LF | $75.00 |
| 502150M | PRESTRESSED CONCRETE PILE, DRIVEN, 24" X 24" | LF | $75.00 |
| 502151M | PRESTRESSED CONCRETE PILE, DRIVEN, 30" X 30" | LF | $75.00 |
| 502156M | PRESTRESSED CONCRETE PILE, DRIVEN, 54" DIAMETER | LF | $200.00 |

1******************************************************************************************************1

903.03.06  Tables

Table 903.03.06-2  Requirements for Structural Concrete Items

1***************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

the seventh LINE under Cast-in-Place Items IS changed to:

| Table 903.03.06-2 Requirements for Structural Concrete Items |
| --- |
|  | Concrete Class | Slump1 (inches) | Percent Air Entrainment for Coarse Aggregate1 |
|  |  |  | No. 57 & No. 67 | No. 8 |
| Decks, Sidewalks, Curbs, Parapets, Concrete Patch | A | 3 ± 1 | 6.0 + 1.5 | 7.0 ± 1.5 |

1*************************************************************************************************1

Section 904 – Precast and Prestressed Concrete

904.01.02  Fabrication

1******************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

THE last SENTENCE OF part 2 IS CHANGED TO:

If using SCC, minimize or eliminate the use of vibrators to prevent segregation.

1*************************************************************************************************1

904.02.06  Quality Control and Acceptance Requirements

1*****************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

step 2 in the third paragraph is changed to:

2.	Dimensions not conforming to the tolerances specified in Table 904.02.02-1.

1*******************************************************************************************************1

Section 905 – Reinforcement Metals

905.01.05  Dowels

1*******************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

THe Entire subsection IS CHANGED TO:

Use plain reinforcement bars according to ASTM A 615, Grade 60.  Galvanize according to ASTM A 123.

1***************************************************************************************************1

905.03.03  Dowel Bars

1***********************************************************************************************1

BDC10s-01 dated Mar 29, 2010

THE first PARAGRAPH is CHANGED TO:

For dowel bars in transverse joints, use epoxy-coated, Grade 60, plain reinforcement steel according to ASTM A 615.  If shown on the Plans, use dowel bars fitted with end caps.  Ensure that the end caps are non-metallic and designed to prevent the entrance of grout or mortar into the expansion void.

1********************************************************************************************************1

1****************************************************************************************************1

BDC09s-11 dated JAN 26, 2010

SECTION 909 – DRAINAGE

THE FOLLOWING SUBPART IS ADDED:

909.02.09 Fiberglass Pipe for Bridge Storm Drainage

Fabricate fiberglass pipe conforming to ASTM D2996, RTRP-12EA1-2122 and fiberglass pipe fittings conforming to ASTM D3840.

Ensure that all fiberglass pipe, fittings and adhesives use pigmented resin throughout the wall and the color is concrete gray or designated color with UV stabilized resin.  Painted gel-coat or exterior coating is not acceptable.

Ensure that adhesives are in accordance with the pipe manufacturer and adhesive manufacturer’s recommendations.

1********************************************************************************************************1

Section 910 – Masonry Units

910.04  Stone Curb

1********************************************************************************************************1

provide lithology, color, and texture of stone curb

1

910.05  Stone Facing for Pier Shafts

1********************************************************************************************************1

provide lithology, color, and texture of Stone Facing for Pier Shafts

1********************************************************************************************************1

910.06  Stone Paving Block

1********************************************************************************************************1

provide color, texture, and uniformity of Stone Paving Block

1*******************************************************************************************************1

Section 911 – Signs, Sign Supports, and Delineators

911.02.02  Breakaway Sign Supports for Ground Mounted Signs

1*****************************************************************************************************1

BDC09s-01 dated apr 09, 2010

THE ENTIRE subpart is changed to:

Fabricate and construct breakaway sign supports for ground mounted signs using materials conforming to the requirements in Table 911.02.02-1.

Table 911.02.02-1  Materials for Breakaway Sign Supports

| Item | Test Method | Type or Grade | Galvanizing |
| --- | --- | --- | --- |
| Aluminum Materials (other than bracket) | 911.01.01 |  |  |
| Bracket | B308 | 6061-T6 |  |
| Structural steel shapes | ASTM A709 | Grade 36 | ASTM A123 |
| Steel Sheet | ASTM A1011 | Grade 36 | ASTM A 653 |
| Bolts (except special bolt for coupling) | ASTM A325 |  | ASTM A153 |
| Special bolt for coupling | ASTM A449 |  | ASTM A153 |
| Cap Screw | ASTM A307 |  | ASTM A153 |
| Lock Washer | ANSI B18-21-1 |  | ASTM A153 |
| Nut | ASTM A563 | Grade DH | ASTM A153 |
| Coupling | AMS 6378 F |  | ASTM A153 |
| Steel Hinge Plate | AISI 4130 |  | ASTM 123 |
| Anchor Rod | AISI 1045 |  |  |
| Anchor Coil | AISI 1008 |  |  |
| Anchor Washer | 908.04 |  |  |
| Anchor Ferrule | 908.04 |  |  |

Submit mill certificates for the component materials.

1********************************************************************************************************1

911.02.03  Non-Breakaway Sign Supports for Ground Mounted Signs

1*******************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

THE last SENTENCE OF THE second PARAGRAPH IS CHANGED TO:

Tie-wrap posts during shipment and handling to protect the finish.

1********************************************************************************************************1

911.03  Flexible Delineators

1*******************************************************************************************************1

BDC09s-08 dated DEC 07, 2009

1.	Delineator Dimensions.

b.	Guide Rail Mounted.

the entire text is changed to:

Ensure that the unit for beam guide rail mounted flexible delineators has a minimum width of 3 inches and a minimum thickness of 0.100 inch.  Use units of a height that will ensure that the top of the reflective area is 5 ± 2 inches above the top of post.

Design the base of the unit to mount over the I-beam blockout or to the top of a wood or synthetic blockout, of the beam guide rail.

c.	Barrier Curb Mounted.

the entire text is changed to:

For barrier curb mounted flexible delineators, use a delineator that is 3-1/2 × 3-1/2 inches, with a minimum thickness of 0.100 inch, and that has a base that forms a “T” shape with the panel for mounting on the side of the barrier curb, and is flexible or hinged so as to return to its original position after being struck.

THE FOLLOWING IS ADDED:

d.	Construction Barrier Curb Mounted.  For construction barrier curb top mounted flexible delineators, use a delineator that is 6 x 12 inches with a minimum thickness of 0.100 inch. For construction barrier curb side mounted flexible delineators, use a delineator that is 3-1/2 x 3-1/2 inches with a minimum thickness of 0.100 inch, and that has a base that forms a “T” shape with the panel for mounting on the barrier curb and is flexible or hinged so as to return to its original position after being struck.

4.	Retroreflective Sheeting.

b.	Guide Rail Mounted.

the entire text is changed to:

Ensure that the sheeting is a minimum of 3 inches square and is mounted on the upper portion of the delineator.

THE FOLLOWING IS ADDED:

d.	Construction Barrier Curb Mounted.  Ensure that the sheeting for top mounted flexible delineators is 6 x 12 inches and the sheeting for side mounted flexible delineators is 3-1/2 x 3-1/2 inches.

Submit a certification of compliance, as specified in 106.07, for delineators.

1********************************************************************************************************1

Section 912 – Paints, Coatings, Traffic Stripes, and Traffic Markings

912.03.01  Epoxy Traffic Stripes

B.	Glass Beads.

1********************************************************************************************************1

BDC09s-06 dated jun 15, 2009

THE FOLLOWING IS ADDED to the first PARAGRAPH:

Ensure that glass beads do not contain more than 200 ppm of lead, 200 ppm of antimony, or 200 ppm of arsenic.

1********************************************************************************************************1

912.03.02  Thermoplastic Traffic Markings

1*******************************************************************************************************1

BDC09s-06 dated jun 15, 2009

THE FOLLOWING IS ADDED to the first PARAGRAPH:

Ensure that glass beads do not contain more than 200 ppm of lead, 200 ppm of antimony, or 200 ppm of arsenic.

1********************************************************************************************************1

912.04.01  Latex Paint

1********************************************************************************************************1

BDC09s-06 dated jun 15, 2009

THE FOLLOWING IS ADDED to the second PARAGRAPH:

Ensure that glass beads do not contain more than 200 ppm of lead, 200 ppm of antimony, or 200 ppm of arsenic.

1********************************************************************************************************1

Section 914 – Joint Materials

914.04.01  Preformed Elastomeric (Compression Type)

B.	Joint Sealer.

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

THE last SENTENCE OF THE second PARAGRAPH IS CHANGED TO:

If splicing of a sealer is allowed, ensure that the sealer at the splice point has no significant misalignment at its sides or top and that misalignment at the bottom does not exceed half of the bottom wall thickness.

1********************************************************************************************************1

Section 917 – Landscaping Materials

917.10  Plant Materials

H.	Inspection.

1********************************************************************************************************1

complete and include THE FOLLOWING

THE second paragraph is changed to:

The Department may inspect plant materials before delivery to the Project Limits and upon delivery to the Project Limits before installation.  The Department may seal the inspected plant materials.  For plant material originating from nurseries farther than 100 miles from the Project Limits, stock plant material at a Contractor-provided holding yard that is acceptable to the Department.  The Department may inspect plant material originating from nurseries within 100 miles of the Project Limits at the nursery.  Ensure that all plant material is untied and located so that trunk or stem and branch structure can be easily inspected.  Provide sufficient notice to allow Department inspection at the nursery or holding yard and to allow time for Contractor reordering of rejected material.  Notify the RE at least ____(hours or days)___ in advance of delivery to the Project Limits for installation.  The Department will reject materials arriving with broken or missing seals, broken or loose balls, broken or pruned leaders, insufficient protection, or that have been damaged in transit.  The Department may randomly inspect the root system of the plant material by breaking open the earth balls.  Provide necessary assistance during Department inspections.

1********************************************************************************************************1

Section 918 – Electrical Materials

918.12  Pedestals, Poles, Transformer Bases, and Mast Bracket Arms

THE first sentence of the first PARAGRAPH is CHANGED TO:

Fabricate pedestals, poles, transformer bases, and mast bracket arms for traffic signal, highway lighting, and camera standards with materials according to the appropriate ASTM standard and the AASHTO Standard Specifications for Structural Supports for Highway Signs, Luminaires and Traffic Signals.

Division 1000 – Equipment

SECTION 1001 – TRAFFIC CONTROL EQUIPMENT

1********************************************************************************************************1

BDC08s-02 dated Feb 17, 2009

include the following subsections if ANY OF THESE ITEMS are REQUESTED BY Traffic Operations

The following subsection is added:

1001.04  PORTABLE VARIABLE MESSAGE SIGN W/REMOTE OPERATION

Provide a portable variable message sign as described under 1001.02 equipped with the required broadband cellular modem.

1001.05  Portable Trailer mounted CCTV CAMERA assembly

Provide a Portable Trailer Mounted CCTV Camera Assembly with the following:

A.	Trailer Platform

1.	Single Axle steel welded trailer with 2 inches adjustable ball hitch

2.	Heavy-duty safety chains

3.	Single drop torsion suspension or leaf springs

4.	Self lubricating wheel spindles

5.	Maximum size, including tongue, 14 feet long by 7 feet wide by 8 feet high

6.	Maximum payload 3500 pounds

7.	Tire size F7815 or F78-14ST with Tire Tools and a spare wheel mounted and locked on trailer

8.	DOT approved lighting package to include electrical brake and marker lights with wire connections

9.	Prime and paint customer’s choice of color

10.	Fitted with manual telescoping outriggers with adjustable jacks sized to counter full mast extension

11.	Four 3500 pounds, drop leg, top wind screw jacks

12.	Custom fabricated mounts for all options installed

13.	All equipment secured to prevent theft or separation from platform

14.	Stainless steel hardware to prolong trailer life

15.	24/7 operation in all weather conditions

16.	Wheel locks to secure trailer while deployed

17.	Two locking NEMA-4 equipment boxes for electronic components and camera storage

18.	One locking NEMA-4 equipment box for operational controls

19.	Max trailer weight of 3500 pounds when fully configured

20.	Wheels removable when trailer in deployed position

21.	Operation manual

B.	Mast

1.	150 pounds payload capacity

2.	29 feet to 32 feet of extension with capability to mount antenna at 20 feet, 25 feet or at the top, maximum nested length of mast is 10 feet - 3 to 9 sections

3.	Un –guyed

4.	Locking collars to allow the mast to remain extended indefinitely without air pressure

5.	Anodized and sealed exterior aluminum surfaces for long life

6.	Custom fabricated mount for cameras

7.	Folds down during transport for better height clearance

8.	Spiral conduit for cables

9.	 Compactly retractable when mast is nested into storage container at bottom of mast

10.	Automatically hydraulic (pneumatic) operation or power winch with a safety brake

C.	Electrical System

1.	12 VDC battery operated with multi crystal solar electric panel

2.	Fuse panel to protect electronics

3.	Four 110 watt solar panels on collapsible mounts

4.	Charge controller that automatically switches charging sources

5.	Isolated 12 VDC starting battery

6.	Provisions for operation on auxiliary power (Electric, Gasoline or fuel generated power source) for deployment

D.	Auxiliary Power Source

Auxiliary Power Source can either be gasoline or diesel operated power generator with a fuel tank capable of up to 72 hours operation without refueling.  Ensure that the engine is shock mounted to reduce vibration and locked in a ventilated enclosure.

E.	Inverter

1.	To provide main power when (AC) power is not available

2.	Battery charger

3.	Install all cables in weather tight conduits with sealed connections to equipment boxes

F.	Electronics

1.	Cellular (CDMA), microwave, or 802.11 bandwidth option

2.	Onboard Ethernet switch to connect cameras, bandwidth, and monitoring devices

3.	Work lights in all cabinets

4.	Remote trailer diagnostics (battery level, charging output, etc)

G.	Camera and Software

Ensure that the camera has the following characteristics:

1.	Weather resistant powder coated aluminum case with stainless steel hardware fittings

2.	Impact resistant viewing window

3.	Minimum resolution of NTSC 704 (H) x 480 (V)

4.	Backlight compensation

5.	Image stabilization

6.	Light Sensitivity 0.02 lux NIR Mode

7.	Auto Focus with Manual Focus capability

8.	Auto White Balance with Manual White Balance capability

9.	Motorized Zoom up to 16x optical, 10x digital

10.	Motorized Pan-Tilt, pan 360°, tilt 180°

11.	Thermostatically controlled heater and defroster -50° to 140°F operating range

12.	Windshield wiper

13.	24/7 operation in all weather conditions

14.	Time and date stamp

15.	Max power consumption 70 VA

Ensure that the software includes:

1.	Remote control of pan, tilt and zoom

2.	Ability to display streaming video in MPEG format, motion-JPEG, and single snapshot JPEG images, remotely central selectable through software

3.	Preset controls of pan/tilt/zoom combinations.  All presets to be accessible from drop-down menu with descriptive name of preset.  Set first 8 presets with quick- launch icons with graphical representation of the preset views.

4.	Ability to display all the project’s web cams in a single view screen

5.	Display of local time and weather conditions including temperature and humidity.

6.	Ability to save images to disk or e-mail images

7.	Ability to view archived images via a graphical calendar control and to store archived images at least every five minutes.

8.	Three levels of password protection admin, user & guest, individual user accounts

9.	Remote camera diagnostics and “self-healing” automatic problem rectification

10.	Ability to monitor and control the cameras from the web

Attachments

INclude fhwa attachments for FHWA funded projects

1********************************************************************************************************1

INclude THE FOLLOWING FOR fhwa funded projects

FHWA Attachment No. 1

Required Contract Provisions Federal-Aid Construction Contracts

I.	General

II.	Nondiscrimination

III.	Nonsegregated Facilities

IV.	Payment of Predetermined Minimum Wage

V.	Statements and Payrolls

VI.	Record of Materials, Supplies, and Labor

VII.	Subletting or Assigning the Contract

VIII.	Safety: Accident Prevention

IX.	False Statements Concerning Highway Projects

X.	Implementation of Clean Air Act and Federal Water Pollution Control Act

XI.	Certification Regarding Debarment, Suspension Ineligibility, and Voluntary Exclusion

XII.	Certification Regarding Use of Contract Funds for Lobbying

Attachments

A.	Employment Preference for Appalachian Contracts (included in Appalachian contracts only)

I	GENERAL

1.	These contract provisions shall apply to all work performed on the contract by the contractor's own organization and with the assistance of workers under the contractor's immediate superintendence and to all work performed on the contract by piecework, station work, or by subcontract.

2.	Except as otherwise provided for in each section, the contractor shall insert in each subcontract all of the stipulations contained in these Required Contract Provisions, and further require their inclusion in any lower tier subcontract or purchase order that may in turn be made. The Required Contract Provisions shall not be incorporated by reference in any case. The prime contractor shall be responsible for compliance by any subcontractor or lower tier subcontractor with these Required Contract Provisions.

3.	A breach of any of the stipulations contained in these Required Contract Provisions shall be sufficient grounds for termination of the contract.

4.	A breach of the following clauses of the Required Contract Provisions may also be grounds for debarment as provided in 29 CFR 5.12:

Section I, paragraph 2;

Section IV, paragraphs 1, 2, 3, 4, and 7;

Section V, paragraphs 1 and 2a through 2g.

5.	Disputes arising out of the labor standards provisions of Section IV (except paragraph 5) and Section V of these Required Contract Provisions shall not be subject to the general disputes clause of this contract. Such disputes shall be resolved in accordance with the procedures of the U.S. Department of Labor (DOL) as set forth in 29 CFR 5, 6, and 7. Disputes within the meaning of this clause include disputes between the contractor (or any of its subcontractors) and the contracting agency, the DOL, or the contractor's employees or their representatives.

6.	Selection of Labor:  During the performance of this contract, the contractor shall not:

a.	discriminate against labor from any other State, possession, or territory of the United States (except for employment preference for Appalachian contracts, when applicable, as specified in Attachment A), or

b.	employ convict labor for any purpose within the limits of the project unless it is labor performed by convicts who are on parole, supervised release, or probation.

II.	NONDISCRIMINATION

(Applicable to all Federal-aid construction contracts and to all related subcontracts of $10,000 or more.)

1.	Equal Employment Opportunity:  Equal employment opportunity (EEO) requirements not to discriminate and to take affirmative action to assure equal opportunity as set forth under laws, executive orders, rules, regulations (28 CFR 35, 29 CFR 1630 and 41 CFR 60) and orders of the Secretary of Labor as modified by the provisions prescribed herein, and imposed pursuant to 23 U.S.C. 140 shall constitute the EEO and specific affirmative action standards for the contractor's project activities under this contract. The Equal Opportunity Construction Contract Specifications set forth under 41 CFR 60-4.3 and the provisions of the American Disabilities Act of 1990 (42 U.S.C. 12101 et seq.) set forth under 28 CFR 35 and 29 CFR 1630 are incorporated by reference in this contract. In the execution of this contract, the contractor agrees to comply with the following minimum specific requirement activities of EEO:

a.	The contractor will work with the State highway agency (SHA) and the Federal Government in carrying out EEO obligations and in their review of his/her activities under the contract.

b.	The contractor will accept as his operating policy the following statement:

"It is the policy of this Company to assure that applicants are employed, and that employees are treated during employment, without regard to their race, religion, sex, color, national origin, age or disability. Such action shall include: employment, upgrading, demotion, or transfer; recruitment or recruitment advertising; layoff or termination; rates of pay or other forms of compensation; and selection for training, including apprenticeship, preapprenticeship, and/or on-the-job training."

2.	EEO Officer:  The contractor will designate and make known to the SHA contracting officers an EEO Officer who will have the responsibility for and must be capable of effectively administering and promoting an active contractor program of EEO and who must be assigned adequate authority and responsibility to do so.

3.	Dissemination of Policy:  All members of the contractor's staff who are authorized to hire, supervise, promote, and discharge employees, or who recommend such action, or who are substantially involved in such action, will be made fully cognizant of, and will implement, the contractor's EEO policy and contractual responsibilities to provide EEO in each grade and classification of employment. To ensure that the above agreement will be met, the following actions will be taken as a minimum:

a.	Periodic meetings of supervisory and personnel office employees will be conducted before the start of work and then not less often than once every six months, at which time the contractor's EEO policy and its implementation will be reviewed and explained. The meetings will be conducted by the EEO Officer.

b.	All new supervisory or personnel office employees will be given a thorough indoctrination by the EEO Officer, covering all major aspects of the contractor's EEO obligations within thirty days following their reporting for duty with the contractor.

c.	All personnel who are engaged in direct recruitment for the project will be instructed by the EEO Officer in the contractor's procedures for locating and hiring minority group employees.

d.	Notices and posters setting forth the contractor's EEO policy will be placed in areas readily accessible to employees, applicants for employment and potential employees.

e.	The contractor's EEO policy and the procedures to implement such policy will be brought to the attention of employees by means of meetings, employee handbooks, or other appropriate means.

4.	Recruitment:  When advertising for employees, the contractor will include in all advertisements for employees the notation: "An Equal Opportunity Employer." All such advertisements will be placed in publications having a large circulation among minority groups in the area from which the project work force would normally be derived.

a.	The contractor will, unless precluded by a valid bargaining agreement, conduct systematic and direct recruitment through public and private employee referral sources likely to yield qualified minority group applicants. To meet this requirement, the contractor will identify sources of potential minority group employees, and establish with such identified sources procedures whereby minority group applicants may be referred to the contractor for employment consideration.

b.	In the event the contractor has a valid bargaining agreement providing for exclusive hiring hall referrals, he is expected to observe the provisions of that agreement to the extent that the system permits the contractor's compliance with EEO contract provisions. (The DOL has held that where implementation of such agreements have the effect of discriminating against minorities or women, or obligates the contractor to do the same, such implementation violates Executive Order 11246, as amended.)

c.	The contractor will encourage his present employees to refer minority group applicants for employment. Information and procedures with regard to referring minority group applicants will be discussed with employees.

5.	Personnel Actions:  Wages, working conditions, and employee benefits shall be established and administered, and personnel actions of every type, including hiring, upgrading, promotion, transfer, demotion, layoff, and termination, shall be taken without regard to race, color, religion, sex, national origin, age or disability. The following procedures shall be followed:

a.	The contractor will conduct periodic inspections of project sites to insure that working conditions and employee facilities do not indicate discriminatory treatment of project site personnel.

b.	The contractor will periodically evaluate the spread of wages paid within each classification to determine any evidence of discriminatory wage practices.

c.	The contractor will periodically review selected personnel actions in depth to determine whether there is evidence of discrimination. Where evidence is found, the contractor will promptly take corrective action. If the review indicates that the discrimination may extend beyond the actions reviewed, such corrective action shall include all affected persons.

d.	 The contractor will promptly investigate all complaints of alleged discrimination made to the contractor in connection with his obligations under this contract, will attempt to resolve such complaints, and will take appropriate corrective action within a reasonable time. If the investigation indicates that the discrimination may affect persons other than the complainant, such corrective action shall include such other persons. Upon completion of each investigation, the contractor will inform every complainant of all of his avenues of appeal.

6.	Training and Promotion:

a.	The contractor will assist in locating, qualifying, and increasing the skills of minority group and women employees, and applicants for employment.

b.	Consistent with the contractor's work force requirements and as permissible under Federal and State regulations, the contractor shall make full use of training programs, i.e., apprenticeship, and on-the-job training programs for the geographical area of contract performance. Where feasible, 25 percent of apprentices or trainees in each occupation shall be in their first year of apprenticeship or training. In the event a special provision for training is provided under this contract, this subparagraph will be superseded as indicated in the special provision.

c.	The contractor will advise employees and applicants for employment of available training programs and entrance requirements for each.

d.	The contractor will periodically review the training and promotion potential of minority group and women employees and will encourage eligible employees to apply for such training and promotion.

7.	Unions:  If the contractor relies in whole or in part upon unions as a source of employees, the contractor will use his/her best efforts to obtain the cooperation of such unions to increase opportunities for minority groups and women within the unions, and to effect referrals by such unions of minority and female employees. Actions by the contractor either directly or through a contractor's association acting as agent will include the procedures set forth below:

a.	The contractor will use best efforts to develop, in cooperation with the unions, joint training programs aimed toward qualifying more minority group members and women for membership in the unions and increasing the skills of minority group employees and women so that they may qualify for higher paying employment.

b.	The contractor will use best efforts to incorporate an EEO clause into each union agreement to the end that such union will be contractually bound to refer applicants without regard to their race, color, religion, sex, national origin, age or disability.

c.	The contractor is to obtain information as to the referral practices and policies of the labor union except that to the extent such information is within the exclusive possession of the labor union and such labor union refuses to furnish such information to the contractor, the contractor shall so certify to the SHA and shall set forth what efforts have been made to obtain such information.

d.	In the event the union is unable to provide the contractor with a reasonable flow of minority and women referrals within the time limit set forth in the collective bargaining agreement, the contractor will, through independent recruitment efforts, fill the employment vacancies without regard to race, color, religion, sex, national origin, age or disability; making full efforts to obtain qualified and/or qualifiable minority group persons and women. (The DOL has held that it shall be no excuse that the union with which the contractor has a collective bargaining agreement providing for exclusive referral failed to refer minority employees.) In the event the union referral practice prevents the contractor from meeting the obligations pursuant to Executive Order 11246, as amended, and these special provisions, such contractor shall immediately notify the SHA.

8.	Selection of Subcontractors, Procurement of Materials and Leasing of Equipment:  The contractor shall not discriminate on the grounds of race, color, religion, sex, national origin, age or disability in the selection and retention of subcontractors, including procurement of materials and leases of equipment.

a.	The contractor shall notify all potential subcontractors and suppliers of his/her EEO obligations under this contract.

b.	Disadvantaged business enterprises (DBE), as defined in 49 CFR 23, shall have equal opportunity to compete for and perform subcontracts which the contractor enters into pursuant to this contract. The contractor will use his best efforts to solicit bids from and to utilize DBE subcontractors or subcontractors with meaningful minority group and female representation among their employees. Contractors shall obtain lists of DBE construction firms from SHA personnel.

c.	The contractor will use his best efforts to ensure subcontractor compliance with their EEO obligations.

9.	Records and Reports:  The contractor shall keep such records as necessary to document compliance with the EEO requirements. Such records shall be retained for a period of three years following completion of the contract work and shall be available at reasonable times and places for inspection by authorized representatives of the SHA and the FHWA.

a.	The records kept by the contractor shall document the following:

1.	The number of minority and non-minority group members and women employed in each work classification on the project;

2.	The progress and efforts being made in cooperation with unions, when applicable, to increase employment opportunities for minorities and women;

3.	The progress and efforts being made in locating, hiring, training, qualifying, and upgrading minority and female employees; and

4.	The progress and efforts being made in securing the services of DBE subcontractors or subcontractors with meaningful minority and female representation among their employees.

b.	The contractors will submit an annual report to the SHA each July for the duration of the project, indicating the number of minority, women, and non-minority group employees currently engaged in each work classification required by the contract work. This information is to be reported on Form FHWA-1391. If on-the-job training is being required by special provision, the contractor will be required to collect and report training data.

III.	NONSEGREGATED FACILITIES

(Applicable to all Federal-aid construction contracts and to all related subcontracts of $10,000 or more.)

a.	 By submission of this bid, the execution of this contract or subcontract, or the consummation of this material supply agreement or purchase order, as appropriate, the bidder, Federal-aid construction contractor, subcontractor, material supplier, or vendor, as appropriate, certifies that the firm does not maintain or provide for its employees any segregated facilities at any of its establishments, and that the firm does not permit its employees to perform their services at any location, under its control, where segregated facilities are maintained. The firm agrees that a breach of this certification is a violation of the EEO provisions of this contract. The firm further certifies that no employee will be denied access to adequate facilities on the basis of sex or disability.

b.	As used in this certification, the term "segregated facilities" means any waiting rooms, work areas, restrooms and washrooms, restaurants and other eating areas, timeclocks, locker rooms, and other storage or dressing areas, parking lots, drinking fountains, recreation or entertainment areas, transportation, and housing facilities provided for employees which are segregated by explicit directive, or are, in fact, segregated on the basis of race, color, religion, national origin, age or disability, because of habit, local custom, or otherwise. The only exception will be for the disabled when the demands for accessibility override (e.g. disabled parking).

c.	The contractor agrees that it has obtained or will obtain identical certification from proposed subcontractors or material suppliers prior to award of subcontracts or consummation of material supply agreements of $10,000 or more and that it will retain such certifications in its files.

IV.	PAYMENT OF PREDETERMINED MINIMUM WAGE

(Applicable to all Federal-aid construction contracts exceeding $2,000 and to all related subcontracts, except for projects located on roadways classified as local roads or rural minor collectors, which are exempt.)

1.	General:

a.	All mechanics and laborers employed or working upon the site of the work will be paid unconditionally and not less often than once a week and without subsequent deduction or rebate on any account [except such payroll deductions as are permitted by regulations (29 CFR 3) issued by the Secretary of Labor under the Copeland Act (40 U.S.C. 276c)] the full amounts of wages and bona fide fringe benefits (or cash equivalents thereof) due at time of payment. The payment shall be computed at wage rates not less than those contained in the wage determination of the Secretary of Labor (hereinafter "the wage determination") which is attached hereto and made a part hereof, regardless of any contractual relationship which may be alleged to exist between the contractor or its subcontractors and such laborers and mechanics. The wage determination (including any additional classifications and wage rates conformed under paragraph 2 of this Section IV and the DOL poster (WH-1321) or Form FHWA-1495) shall be posted at all times by the contractor and its subcontractors at the site of the work in a prominent and accessible place where it can be easily seen by the workers. For the purpose of this Section, contributions made or costs reasonably anticipated for bona fide fringe benefits under Section 1(b)(2) of the Davis-Bacon Act (40 U.S.C. 276a) on behalf of laborers or mechanics are considered wages paid to such laborers or mechanics, subject to the provisions of Section IV, paragraph 3b, hereof. Also, for the purpose of this Section, regular contributions made or costs incurred for more than a weekly period (but not less often than quarterly) under plans, funds, or programs, which cover the particular weekly period, are deemed to be constructively made or incurred during such weekly period. Such laborers and mechanics shall be paid the appropriate wage rate and fringe benefits on the wage determination for the classification of work actually performed, without regard to skill, except as provided in paragraphs 4 and 5 of this Section IV.

b.	Laborers or mechanics performing work in more than one classification may be compensated at the rate specified for each classification for the time actually worked therein, provided, that the employer's payroll records accurately set forth the time spent in each classification in which work is performed.

c.	All rulings and interpretations of the Davis-Bacon Act and related acts contained in 29 CFR 1, 3, and 5 are herein incorporated by reference in this contract.

2.	Classification:

a.	The SHA contracting officer shall require that any class of laborers or mechanics employed under the contract, which is not listed in the wage determination, shall be classified in conformance with the wage determination.

b.	The contracting officer shall approve an additional classification, wage rate and fringe benefits only when the following criteria have been met:

1.	the work to be performed by the additional classification requested is not performed by a classification in the wage determination;

2.	the additional classification is utilized in the area by the construction industry;

3.	the proposed wage rate, including any bona fide fringe benefits, bears a reasonable relationship to the wage rates contained in the wage determination; and

4.	with respect to helpers, when such a classification prevails in the area in which the work is performed.

c.	If the contractor or subcontractors, as appropriate, the laborers and mechanics (if known) to be employed in the additional classification or their representatives, and the contracting officer agree on the classification and wage rate (including the amount designated for fringe benefits where appropriate), a report of the action taken shall be sent by the contracting officer to the DOL, Administrator of the Wage and Hour Division, Employment Standards Administration, Washington, D.C. 20210. The Wage and Hour Administrator, or an authorized representative, will approve, modify, or disapprove every additional classification action within 30 days of receipt and so advise the contracting officer or will notify the contracting officer within the 30-day period that additional time is necessary.

d.	In the event the contractor or subcontractors, as appropriate, the laborers or mechanics to be employed in the additional classification or their representatives, and the contracting officer do not agree on the proposed classification and wage rate (including the amount designated for fringe benefits, where appropriate), the contracting officer shall refer the questions, including the views of all interested parties and the recommendation of the contracting officer, to the Wage and Hour Administrator for determination. Said Administrator, or an authorized representative, will issue a determination within 30 days of receipt and so advise the contracting officer or will notify the contracting officer within the 30-day period that additional time is necessary

e.	The wage rate (including fringe benefits where appropriate) determined pursuant to paragraph 2c or 2d of this Section IV shall be paid to all workers performing work in the additional classification from the first day on which work is performed in the classification.

3.	Payment of Fringe Benefits:

a.	Whenever the minimum wage rate prescribed in the contract for a class of laborers or mechanics includes a fringe benefit which is not expressed as an hourly rate, the contractor or subcontractors, as appropriate, shall either pay the benefit as stated in the wage determination or shall pay another bona fide fringe benefit or an hourly case equivalent thereof.

b.	If the contractor or subcontractor, as appropriate, does not make payments to a trustee or other third person, he/she may consider as a part of the wages of any laborer or mechanic the amount of any costs reasonably anticipated in providing bona fide fringe benefits under a plan or program, provided, that the Secretary of Labor has found, upon the written request of the contractor, that the applicable standards of the Davis-Bacon Act have been met. The Secretary of Labor may require the contractor to set aside in a separate account assets for the meeting of obligations under the plan or program.

4.	Apprentices and Trainees (Programs of the U.S. DOL) and Helpers:

a.	Apprentices:

1.	Apprentices will be permitted to work at less than the predetermined rate for the work they performed when they are employed pursuant to and individually registered in a bona fide apprenticeship program registered with the DOL, Employment and Training Administration, Bureau of Apprenticeship and Training, or with a State apprenticeship agency recognized by the Bureau, or if a person is employed in his/her first 90 days of probationary employment as an apprentice in such an apprenticeship program, who is not individually registered in the program, but who has been certified by the Bureau of Apprenticeship and Training or a State apprenticeship agency (where appropriate) to be eligible for probationary employment as an apprentice.

2.	The allowable ratio of apprentices to journeyman-level employees on the job site in any craft classification shall not be greater than the ratio permitted to the contractor as to the entire work force under the registered program. Any employee listed on a payroll at an apprentice wage rate, who is not registered or otherwise employed as stated above, shall be paid not less than the applicable wage rate listed in the wage determination for the classification of work actually performed. In addition, any apprentice performing work on the job site in excess of the ratio permitted under the registered program shall be paid not less than the applicable wage rate on the wage determination for the work actually performed. Where a contractor or subcontractor is performing construction on a project in a locality other than that in which its program is registered, the ratios and wage rates (expressed in percentages of the journeyman-level hourly rate) specified in the contractor's or subcontractor's registered program shall be observed.

3.	Every apprentice must be paid at not less than the rate specified in the registered program for the apprentice's level of progress, expressed as a percentage of the journeyman-level hourly rate specified in the applicable wage determination. Apprentices shall be paid fringe benefits in accordance with the provisions of the apprenticeship program. If the apprenticeship program does not specify fringe benefits, apprentices must be paid the full amount of fringe benefits listed on the wage determination for the applicable classification. If the Administrator for the Wage and Hour Division determines that a different practice prevails for the applicable apprentice classification, fringes shall be paid in accordance with that determination.

4.	In the event the Bureau of Apprenticeship and Training, or a State apprenticeship agency recognized by the Bureau, withdraws approval of an apprenticeship program, the contractor or subcontractor will no longer be permitted to utilize apprentices at less than the applicable predetermined rate for the comparable work performed by regular employees until an acceptable program is approved.

b.	Trainees:

1.	Except as provided in 29 CFR 5.16, trainees will not be permitted to work at less than the predetermined rate for the work performed unless they are employed pursuant to and individually registered in a program which has received prior approval, evidenced by formal certification by the DOL, Employment and Training Administration.

2.	The ratio of trainees to journeyman-level employees on the job site shall not be greater than permitted under the plan approved by the Employment and Training Administration. Any employee listed on the payroll at a trainee rate who is not registered and participating in a training plan approved by the Employment and Training Administration shall be paid not less than the applicable wage rate on the wage determination for the classification of work actually performed. In addition, any trainee performing work on the job site in excess of the ratio permitted under the registered program shall be paid not less than the applicable wage rate on the wage determination for the work actually performed.

3.	Every trainee must be paid at not less than the rate specified in the approved program for his/her level of progress, expressed as a percentage of the journeyman-level hourly rate specified in the applicable wage determination. Trainees shall be paid fringe benefits in accordance with the provisions of the trainee program. If the trainee program does not mention fringe benefits, trainees shall be paid the full amount of fringe benefits listed on the wage determination unless the Administrator of the Wage and Hour Division determines that there is an apprenticeship program associated with the corresponding journeyman-level wage rate on the wage determination which provides for less than full fringe benefits for apprentices, in which case such trainees shall receive the same fringe benefits as apprentices.

4.	In the event the Employment and Training Administration withdraws approval of a training program, the contractor or subcontractor will no longer be permitted to utilize trainees at less than the applicable predetermined rate for the work performed until an acceptable program is approved.

c.	Helpers:

Helpers will be permitted to work on a project if the helper classification is specified and defined on the applicable wage determination or is approved pursuant to the conformance procedure set forth in Section IV.2. Any worker listed on a payroll at a helper wage rate, who is not a helper under a approved definition, shall be paid not less than the applicable wage rate on the wage determination for the classification of work actually performed.

5.	Apprentices and Trainees (Programs of the U.S. DOT):

Apprentices and trainees working under apprenticeship and skill training programs which have been certified by the Secretary of Transportation as promoting EEO in connection with Federal-aid highway construction programs are not subject to the requirements of paragraph 4 of this Section IV. The straight time hourly wage rates for apprentices and trainees under such programs will be established by the particular programs. The ratio of apprentices and trainees to journeymen shall not be greater than permitted by the terms of the particular program.

6.	Withholding:

The SHA shall upon its own action or upon written request of an authorized representative of the DOL withhold, or cause to be withheld, from the contractor or subcontractor under this contract or any other Federal contract with the same prime contractor, or any other Federally-assisted contract subject to Davis-Bacon prevailing wage requirements which is held by the same prime contractor, as much of the accrued payments or advances as may be considered necessary to pay laborers and mechanics, including apprentices, trainees, and helpers, employed by the contractor or any subcontractor the full amount of wages required by the contract. In the event of failure to pay any laborer or mechanic, including any apprentice, trainee, or helper, employed or working on the site of the work, all or part of the wages required by the contract, the SHA contracting officer may, after written notice to the contractor, take such action as may be necessary to cause the suspension of any further payment, advance, or guarantee of funds until such violations have ceased.

7.	Overtime Requirements:

No contractor or subcontractor contracting for any part of the contract work which may require or involve the employment of laborers, mechanics, watchmen, or guards (including apprentices, trainees, and helpers described in paragraphs 4 and 5 above) shall require or permit any laborer, mechanic, watchman, or guard in any workweek in which he/she is employed on such work, to work in excess of 40 hours in such workweek unless such laborer, mechanic, watchman, or guard receives compensation at a rate not less than one-and-one-half times his/her basic rate of pay for all hours worked in excess of 40 hours in such workweek.

8.	Violation:

Liability for Unpaid Wages; Liquidated Damages: In the event of any violation of the clause set forth in paragraph 7 above, the contractor and any subcontractor responsible thereof shall be liable to the affected employee for his/her unpaid wages. In addition, such contractor and subcontractor shall be liable to the United States (in the case of work done under contract for the District of Columbia or a territory, to such District or to such territory) for liquidated damages. Such liquidated damages shall be computed with respect to each individual laborer, mechanic, watchman, or guard employed in violation of the clause set forth in paragraph 7, in the sum of $10 for each calendar day on which such employee was required or permitted to work in excess of the standard work week of 40 hours without payment of the overtime wages required by the clause set forth in paragraph 7.

9.	Withholding for Unpaid Wages and Liquidated Damages:

The SHA shall upon its own action or upon written request of any authorized representative of the DOL withhold, or cause to be withheld, from any monies payable on account of work performed by the contractor or subcontractor under any such contract or any other Federal contract with the same prime contractor, or any other Federally-assisted contract subject to the Contract Work Hours and Safety Standards Act, which is held by the same prime contractor, such sums as may be determined to be necessary to satisfy any liabilities of such contractor or subcontractor for unpaid wages and liquidated damages as provided in the clause set forth in paragraph 8 above.

V.	STATEMENTS AND PAYROLLS

(Applicable to all Federal-aid construction contracts exceeding $2,000 and to all related subcontracts, except for projects located on roadways classified as local roads or rural collectors, which are exempt.)

1.	Compliance with Copeland Regulations (29 CFR 3):

The contractor shall comply with the Copeland Regulations of the Secretary of Labor which are herein incorporated by reference.

2.	Payrolls and Payroll Records:

a.	Payrolls and basic records relating thereto shall be maintained by the contractor and each subcontractor during the course of the work and preserved for a period of 3 years from the date of completion of the contract for all laborers, mechanics, apprentices, trainees, watchmen, helpers, and guards working at the site of the work.

b.	The payroll records shall contain the name, the social security number of each such employee; his or her correct classification; hourly rates of wages paid (including rates of contributions or costs anticipated for bona fide fringe benefits or cash equivalent thereof the types described in Section 1(b)(2)(B) of the Davis Bacon Act); daily and weekly number of hours worked; deductions made; and actual wages paid.  In addition, for Appalachian contracts, the payroll records shall contain a notation indicating whether the employee does, or does not, normally reside in the labor area as defined in Attachment A, paragraph 1.  Whenever the Secretary of Labor, pursuant to Section IV, paragraph 3b, has found that the wages of any laborer or mechanic include the amount of any costs reasonably anticipated in providing benefits under a plan or program described in Section 1(b)(2)(B) of the Davis Bacon Act, the contractor and each subcontractor shall maintain records which show that the commitment to provide such benefits is enforceable, that the plan or program is financially responsible, that the plan or program has been communicated in writing to the laborers or mechanics affected, and show the cost anticipated or the actual cost incurred in providing benefits. Contractors or subcontractors employing apprentices or trainees under approved programs shall maintain written evidence of the registration of apprentices and trainees, and ratios and wage rates prescribed in the applicable programs.

c.	Each contractor and subcontractor shall furnish, each week in which any contract work is performed, to the SHA resident engineer a payroll of wages paid each of its employees (including apprentices, trainees, and helpers, described in Section IV, paragraphs 4 and 5, and watchmen and guards engaged on work during the preceding weekly payroll period). The payroll submitted shall set out accurately and completely all of the information required to be maintained under paragraph 2b of this Section V. This information may be submitted in any form desired. Optional Form WH-347 is available for this purpose and may be purchased from the Superintendent of Documents (Federal stock number 029-005-0014-1), U.S. Government Printing Office, Washington, D.C. 20402. The prime contractor is responsible for the submission of copies of payrolls by all subcontractors.

d.	Each payroll submitted shall be accompanied by a "Statement of Compliance," signed by the contractor or subcontractor or his/her agent who pays or supervises the payment of the persons employed under the contract and shall certify the following:

1.	that the payroll for the payroll period contains the information required to be maintained under paragraph 2b of this Section V and that such information is correct and complete;

2.	that such laborer or mechanic (including each helper, apprentice, and trainee) employed on the contract during the payroll period has been paid the full weekly wages earned, without rebate, either directly or indirectly, and that no deductions have been made either directly or indirectly from the full wages earned, other than permissible deductions as set forth in the Regulations, 29 CFR 3;

3.	that each laborer or mechanic has been paid not less that the applicable wage rate and fringe benefits or cash equivalent for the classification of worked performed, as specified in the applicable wage determination incorporated into the contract.

e.	The weekly submission of a properly executed certification set forth on the reverse side of Optional Form WH-347 shall satisfy the requirement for submission of the "Statement of Compliance" required by paragraph 2d of this Section V.

f.	The falsification of any of the above certifications may subject the contractor to civil or criminal prosecution under 18 U.S.C. 1001 and 31 U.S.C. 231.

g.	The contractor or subcontractor shall make the records required under paragraph 2b of this Section V available for inspection, copying, or transcription by authorized representatives of the SHA, the FHWA, or the DOL, and shall permit such representatives to interview employees during working hours on the job. If the contractor or subcontractor fails to submit the required records or to make them available, the SHA, the FHWA, the DOL, or all may, after written notice to the contractor, sponsor, applicant, or owner, take such actions as may be necessary to cause the suspension of any further payment, advance, or guarantee of funds. Furthermore, failure to submit the required records upon request or to make such records available may be grounds for debarment action pursuant to 29 CFR 5.12.

VI.	RECORD OF MATERIALS, SUPPLIES, AND LABOR

1.	On all Federal-aid contracts on the National Highway System, except those which provide solely for the installation of protective devices at railroad grade crossings, those which are constructed on a force account or direct labor basis, highway beautification contracts, and contracts for which the total final construction cost for roadway and bridge is less than $1,000,000 (23 CFR 635) the contractor shall:

a.	Become familiar with the list of specific materials and supplies contained in Form FHWA-47, "Statement of Materials and Labor Used by Contractor of Highway Construction Involving Federal Funds," prior to the commencement of work under this contract.

b.	Maintain a record of the total cost of all materials and supplies purchased for and incorporated in the work, and also of the quantities of those specific materials and supplies listed on Form FHWA-47, and in the units shown on Form FHWA-47.

c.	Furnish, upon the completion of the contract, to the SHA resident engineer on Form FHWA-47 together with the data required in paragraph 1b relative to materials and supplies, a final labor summary of all contract work indicating the total hours worked and the total amount earned.

2.	At the prime contractor's option, either a single report covering all contract work or separate reports for the contractor and for each subcontract shall be submitted.

VII.	SUBLETTING OR ASSIGNING THE CONTRACT

1.	The contractor shall perform with its own organization contract work amounting to not less than 30 percent (or a greater percentage if specified elsewhere in the contract) of the total original contract price, excluding any specialty items designated by the State. Specialty items may be performed by subcontract and the amount of any such specialty items performed may be deducted from the total original contract price before computing the amount of work required to be performed by the contractor's own organization (23 CFR 635).

a.	"Its own organization" shall be construed to include only workers employed and paid directly by the prime contractor and equipment owned or rented by the prime contractor, with or without operators. Such term does not include employees or equipment of a subcontractor, assignee, or agent of the prime contractor.

b.	"Specialty Items" shall be construed to be limited to work that requires highly specialized knowledge, abilities, or equipment not ordinarily available in the type of contracting organizations qualified and expected to bid on the contract as a whole and in general are to be limited to minor components of the overall contract.

2.	The contract amount upon which the requirements set forth in paragraph 1 of Section VII is computed includes the cost of material and manufactured products which are to be purchased or produced by the contractor under the contract provisions.

3.	The contractor shall furnish (a) a competent superintendent or supervisor who is employed by the firm, has full authority to direct performance of the work in accordance with the contract requirements, and is in charge of all construction operations (regardless of who performs the work) and (b) such other of its own organizational resources (supervision, management, and engineering services) as the SHA contracting officer determines is necessary to assure the performance of the contract.

4.	No portion of the contract shall be sublet, assigned or otherwise disposed of except with the written consent of the SHA contracting officer, or authorized representative, and such consent when given shall not be construed to relieve the contractor of any responsibility for the fulfillment of the contract. Written consent will be given only after the SHA has assured that each subcontract is evidenced in writing and that it contains all pertinent provisions and requirements of the prime contract.

VIII.	SAFETY: ACCIDENT PREVENTION

1.	In the performance of this contract the contractor shall comply with all applicable Federal, State, and local laws governing safety, health, and sanitation (23 CFR 635). The contractor shall provide all safeguards, safety devices and protective equipment and take any other needed actions as it determines, or as the SHA contracting officer may determine, to be reasonably necessary to protect the life and health of employees on the job and the safety of the public and to protect property in connection with the performance of the work covered by the contract.

2.	 It is a condition of this contract, and shall be made a condition of each subcontract, which the contractor enters into pursuant to this contract, that the contractor and any subcontractor shall not permit any employee, in performance of the contract, to work in surroundings or under conditions which are unsanitary, hazardous or dangerous to his/her health or safety, as determined under construction safety and health standards (29 CFR 1926) promulgated by the Secretary of Labor, in accordance with Section 107 of the Contract Work Hours and Safety Standards Act (40 U.S.C. 333).

3.	Pursuant to 29 CFR 1926.3, it is a condition of this contract that the Secretary of Labor or authorized representative thereof, shall have right of entry to any site of contract performance to inspect or investigate the matter of compliance with the construction safety and health standards and to carry out the duties of the Secretary under Section 107 of the Contract Work Hours and Safety Standards Act (40 U.S.C. 333).

IX.	FALSE STATEMENTS CONCERNING HIGHWAY PROJECTS

In order to assure high quality and durable construction in conformity with approved plans and specifications and a high degree of reliability on statements and representations made by engineers, contractors, suppliers, and workers on Federal-aid highway projects, it is essential that all persons concerned with the project perform their functions as carefully, thoroughly, and honestly as possible. Willful falsification, distortion, or misrepresentation with respect to any facts related to the project is a violation of Federal law. To prevent any misunderstanding regarding the seriousness of these and similar acts, the following notice shall be posted on each Federal-aid highway project (23 CFR 635) in one or more places where it is readily available to all persons concerned with the project:

NOTICE TO ALL PERSONNEL ENGAGED ON FEDERAL-AID HIGHWAY PROJECTS

18 U.S.C. 1020 reads as follows:

"Whoever, being an officer, agent, or employee of the United States, or of any State or Territory, or whoever, whether a person, association, firm, or corporation, knowingly makes any false statement, false representation, or false report as to the character, quality, quantity, or cost of the material used or to be used, or the quantity or quality of the work performed or to be performed, or the cost thereof in connection with the submission of plans, maps, specifications, contracts, or costs of construction on any highway or related project submitted for approval to the Secretary of Transportation; or

Whoever knowingly makes any false statement, false representation, false report or false claim with respect to the character, quality, quantity, or cost of any work performed or to be performed, or materials furnished or to be furnished, in connection with the construction of any highway or related project approved by the Secretary of Transportation; or

Whoever knowingly makes any false statement or false representation as to material fact in any statement, certificate, or report submitted pursuant to provisions of the Federal-aid Roads Act approved July 1, 1916, (39 Stat. 355), as amended and supplemented;

Shall be fined not more that $10,000 or imprisoned not more than 5 years or both."

X.	IMPLEMENTATION OF CLEAN AIR ACT AND FEDERAL WATER POLLUTION CONTROL ACT

(Applicable to all Federal-aid construction contracts and to all related subcontracts of $100,000 or more.)

By submission of this bid or the execution of this contract, or subcontract, as appropriate, the bidder, Federal-aid construction contractor, or subcontractor, as appropriate, will be deemed to have stipulated as follows:

1.	That any facility that is or will be utilized in the performance of this contract, unless such contract is exempt under the Clean Air Act, as amended (42 U.S.C. 1857 et seq., as amended by Pub.L. 91-604), and under the Federal Water Pollution Control Act, as amended (33 U.S.C. 1251 et seq., as amended by Pub.L. 92-500), Executive Order 11738, and regulations in implementation thereof (40 CFR 15) is not listed, on the date of contract award, on the U.S. Environmental Protection Agency (EPA) List of Violating Facilities pursuant to 40 CFR 15.20.

2.	That the firm agrees to comply and remain in compliance with all the requirements of Section 114 of the Clean Air Act and Section 308 of the Federal Water Pollution Control Act and all regulations and guidelines listed thereunder.

3.	That the firm shall promptly notify the SHA of the receipt of any communication from the Director, Office of Federal Activities, EPA, indicating that a facility that is or will be utilized for the contract is under consideration to be listed on the EPA List of Violating Facilities.

4.	That the firm agrees to include or cause to be included the requirements of paragraph 1 through 4 of this Section X in every nonexempt subcontract, and further agrees to take such action as the government may direct as a means of enforcing such requirements.

XI.	CERTIFICATION REGARDING DEBARMENT, SUSPENSION, INELIGIBILITY AND VOLUNTARY EXCLUSION

1.	Instructions for Certification - Primary Covered Transactions:

(Applicable to all Federal-aid contracts - 49 CFR 29)

a.	By signing and submitting this proposal, the prospective primary participant is providing the certification set out below.

b.	The inability of a person to provide the certification set out below will not necessarily result in denial of participation in this covered transaction. The prospective participant shall submit an explanation of why it cannot provide the certification set out below. The certification or explanation will be considered in connection with the department or agency's determination whether to enter into this transaction. However, failure of the prospective primary participant to furnish a certification or an explanation shall disqualify such a person from participation in this transaction.

c.	The certification in this clause is a material representation of fact upon which reliance was placed when the department or agency determined to enter into this transaction. If it is later determined that the prospective primary participant knowingly rendered an erroneous certification, in addition to other remedies available to the Federal Government, the department or agency may terminate this transaction for cause of default.

d.	The prospective primary participant shall provide immediate written notice to the department or agency to whom this proposal is submitted if any time the prospective primary participant learns that its certification was erroneous when submitted or has become erroneous by reason of changed circumstances.

e.	The terms "covered transaction," "debarred," "suspended," "ineligible," "lower tier covered transaction," "participant," "person," "primary covered transaction," "principal," "proposal," and "voluntarily excluded," as used in this clause, have the meanings set out in the Definitions and Coverage sections of rules implementing Executive Order 12549. You may contact the department or agency to which this proposal is submitted for assistance in obtaining a copy of those regulations.

f.	The prospective primary participant agrees by submitting this proposal that, should the proposed covered transaction be entered into, it shall not knowingly enter into any lower tier covered transaction with a person who is debarred, suspended, declared ineligible, or voluntarily excluded from participation in this covered transaction, unless authorized by the department or agency entering into this transaction.

g.	The prospective primary participant further agrees by submitting this proposal that it will include the clause titled "Certification Regarding Debarment, Suspension, Ineligibility and Voluntary Exclusion-Lower Tier Covered Transaction," provided by the department or agency entering into this covered transaction, without modification, in all lower tier covered transactions and in all solicitations for lower tier covered transactions.

h.	A participant in a covered transaction may rely upon a certification of a prospective participant in a lower tier covered transaction that is not debarred, suspended, ineligible, or voluntarily excluded from the covered transaction, unless it knows that the certification is erroneous. A participant may decide the method and frequency by which it determines the eligibility of its principals. Each participant may, but is not required to, check the nonprocurement portion of the "Lists of Parties Excluded From Federal Procurement or Nonprocurement Programs" (Nonprocurement List) which is compiled by the General Services Administration.

i.	Nothing contained in the foregoing shall be construed to require establishment of a system of records in order to render in good faith the certification required by this clause. The knowledge and information of participant is not required to exceed that which is normally possessed by a prudent person in the ordinary course of business dealings.

j.	Except for transactions authorized under paragraph f of these instructions, if a participant in a covered transaction knowingly enters into a lower tier covered transaction with a person who is suspended, debarred, ineligible, or voluntarily excluded from participation in this transaction, in addition to other remedies available to the Federal Government, the department or agency may terminate this transaction for cause or default.

* * * * *

Certification Regarding Debarment, Suspension, Ineligibility and Voluntary Exclusion--Primary Covered Transactions

1.	The prospective primary participant certifies to the best of its knowledge and belief, that it and its principals:

a.	Are not presently debarred, suspended, proposed for debarment, declared ineligible, or voluntarily excluded from covered transactions by any Federal department or agency;

b.	Have not within a 3-year period preceding this proposal been convicted of or had a civil judgement rendered against them for commission of fraud or a criminal offense in connection with obtaining, attempting to obtain, or performing a public (Federal, State or local) transaction or contract under a public transaction; violation of Federal or State antitrust statutes or commission of embezzlement, theft, forgery, bribery, falsification or destruction of records, making false statements, or receiving stolen property;

c.	Are not presently indicted for or otherwise criminally or civilly charged by a governmental entity (Federal, State or local) with commission of any of the offenses enumerated in paragraph 1b of this certification; and

d.	Have not within a 3-year period preceding this application/proposal had one or more public transactions (Federal, State or local) terminated for cause or default.

2.	Where the prospective primary participant is unable to certify to any of the statements in this certification, such prospective participant shall attach an explanation to this proposal.

* * * * *

2.	Instructions for Certification - Lower Tier Covered Transactions:

(Applicable to all subcontracts, purchase orders and other lower tier transactions of $25,000 or more - 49 CFR 29)

a.	By signing and submitting this proposal, the prospective lower tier is providing the certification set out below.

b.	The certification in this clause is a material representation of fact upon which reliance was placed when this transaction was entered into. If it is later determined that the prospective lower tier participant knowingly rendered an erroneous certification, in addition to other remedies available to the Federal Government, the department, or agency with which this transaction originated may pursue available remedies, including suspension and/or debarment.

c.	The prospective lower tier participant shall provide immediate written notice to the person to which this proposal is submitted if at any time the prospective lower tier participant learns that its certification was erroneous by reason of changed circumstances.

d.	The terms "covered transaction," "debarred," "suspended," "ineligible," "primary covered transaction," "participant," "person," "principal," "proposal," and "voluntarily excluded," as used in this clause, have the meanings set out in the Definitions and Coverage sections of rules implementing Executive Order 12549. You may contact the person to which this proposal is submitted for assistance in obtaining a copy of those regulations.

e.	The prospective lower tier participant agrees by submitting this proposal that, should the proposed covered transaction be entered into, it shall not knowingly enter into any lower tier covered transaction with a person who is debarred, suspended, declared ineligible, or voluntarily excluded from participation in this covered transaction, unless authorized by the department or agency with which this transaction originated.

f.	The prospective lower tier participant further agrees by submitting this proposal that it will include this clause titled "Certification Regarding Debarment, Suspension, Ineligibility and Voluntary Exclusion-Lower Tier Covered Transaction," without modification, in all lower tier covered transactions and in all solicitations for lower tier covered transactions.

g.	A participant in a covered transaction may rely upon a certification of a prospective participant in a lower tier covered transaction that is not debarred, suspended, ineligible, or voluntarily excluded from the covered transaction, unless it knows that the certification is erroneous. A participant may decide the method and frequency by which it determines the eligibility of its principals. Each participant may, but is not required to, check the Nonprocurement List.

h.	Nothing contained in the foregoing shall be construed to require establishment of a system of records in order to render in good faith the certification required by this clause. The knowledge and information of participant is not required to exceed that which is normally possessed by a prudent person in the ordinary course of business dealings.

i.	Except for transactions authorized under paragraph e of these instructions, if a participant in a covered transaction knowingly enters into a lower tier covered transaction with a person who is suspended, debarred, ineligible, or voluntarily excluded from participation in this transaction, in addition to other remedies available to the Federal Government, the department or agency with which this transaction originated may pursue available remedies, including suspension and/or debarment.

* * * * *

Certification Regarding Debarment, Suspension, Ineligibility and Voluntary Exclusion--Lower Tier Covered Transactions:

1.	The prospective lower tier participant certifies, by submission of this proposal, that neither it nor its principals is presently debarred, suspended, proposed for debarment, declared ineligible, or voluntarily excluded from participation in this transaction by any Federal department or agency.

2.	Where the prospective lower tier participant is unable to certify to any of the statements in this certification, such prospective participant shall attach an explanation to this proposal.

* * * * *

XII.	CERTIFICATION REGARDING USE OF CONTRACT FUNDS FOR LOBBYING

(Applicable to all Federal-aid construction contracts and to all related subcontracts which exceed $100,000 - 49 CFR 20)

1.	The prospective participant certifies, by signing and submitting this bid or proposal, to the best of his or her knowledge and belief, that:

a.	No Federal appropriated funds have been paid or will be paid, by or on behalf of the undersigned, to any person for influencing or attempting to influence an officer or employee of any Federal agency, a Member of Congress, an officer or employee of Congress, or an employee of a Member of Congress in connection with the awarding of any Federal contract, the making of any Federal grant, the making of any Federal loan, the entering into of any cooperative agreement, and the extension, continuation, renewal, amendment, or modification of any Federal contract, grant, loan, or cooperative agreement.

b.	If any funds other than Federal appropriated funds have been paid or will be paid to any person for influencing or attempting to influence an officer or employee of any Federal agency, a Member of Congress, an officer or employee of Congress, or an employee of a Member of Congress in connection with this Federal contract, grant, loan, or cooperative agreement, the undersigned shall complete and submit Standard Form-LLL, "Disclosure Form to Report Lobbying," in accordance with its instructions.

2.	This certification is a material representation of fact upon which reliance was placed when this transaction was made or entered into. Submission of this certification is a prerequisite for making or entering into this transaction imposed by 31 U.S.C. 1352. Any person who fails to file the required certification shall be subject to a civil penalty of not less than $10,000 and not more than $100,000 for each such failure.

3.	The prospective participant also agrees by submitting his or her bid or proposal that he or she shall require that the language of this certification be included in all lower tier subcontracts, which exceed $100,000 and that all such recipients shall certify and disclose accordingly.

ATTACHMENT A - EMPLOYMENT PREFERENCE FOR APPALACHIAN CONTRACTS

(Applicable to Appalachian contracts only.)

1.	During the performance of this contract, the contractor undertaking to do work which is, or reasonably may be, done as on-site work, shall give preference to qualified persons who regularly reside in the labor area as designated by the DOL wherein the contract work is situated, or the subregion, or the Appalachian counties of the State wherein the contract work is situated, except:

a.	To the extent that qualified persons regularly residing in the area are not available.

b.	For the reasonable needs of the contractor to employ supervisory or specially experienced personnel necessary to assure an efficient execution of the contract work.

c.	For the obligation of the contractor to offer employment to present or former employees as the result of a lawful collective bargaining contract, provided that the number of nonresident persons employed under this subparagraph 1c shall not exceed 20 percent of the total number of employees employed by the contractor on the contract work, except as provided in subparagraph 4 below.

2.	The contractor shall place a job order with the State Employment Service indicating (a) the classifications of the laborers, mechanics and other employees required to perform the contract work, (b) the number of employees required in each classification, (c) the date on which he estimates such employees will be required, and (d) any other pertinent information required by the State Employment Service to complete the job order form. The job order may be placed with the State Employment Service in writing or by telephone. If during the course of the contract work, the information submitted by the contractor in the original job order is substantially modified, he shall promptly notify the State Employment Service.

3.	The contractor shall give full consideration to all qualified job applicants referred to him by the State Employment Service. The contractor is not required to grant employment to any job applicants who, in his opinion, are not qualified to perform the classification of work required.

4.	If, within 1 week following the placing of a job order by the contractor with the State Employment Service, the State Employment Service is unable to refer any qualified job applicants to the contractor, or less than the number requested, the State Employment Service will forward a certificate to the contractor indicating the unavailability of applicants. Such certificate shall be made a part of the contractor's permanent project records. Upon receipt of this certificate, the contractor may employ persons who do not normally reside in the labor area to fill positions covered by the certificate, notwithstanding the provisions of subparagraph 1c above.

5.	The contractor shall include the provisions of Sections 1 through 4 of this Attachment A in every subcontract for work which is, or reasonably may be, done as on-site work.

FHWA Attachment No. 1

Required Contract Provisions, Federal-Aid Construction Contracts (Form FHWA-1273).

V.	STATEMENTS AND PAYROLLS

2.	Payrolls and Payroll Records:

1********************************************************************************************************1

BDC10s-06 dated Mar 31, 2010

THE FOLLOWING SUBPART IS changed to:

b.	The payroll records shall contain the name, the last four digits of the social security number of each such employee; his or her correct classification; hourly rates of wages paid (including rates of contributions or costs anticipated for bona fide fringe benefits or cash equivalent thereof the types described in Section 1(b)(2)(B) of the Davis Bacon Act); daily and weekly number of hours worked; deductions made; and actual wages paid. In addition, for Appalachian contracts, the payroll records shall contain a notation indicating whether the employee does, or does not, normally reside in the labor area as defined in Attachment A, paragraph 1.  Whenever the Secretary of Labor, pursuant to Section IV, paragraph 3b, has found that the wages of any laborer or mechanic include the amount of any costs reasonably anticipated in providing benefits under a plan or program described in Section 1(b)(2)(B) of the Davis Bacon Act, the contractor and each subcontractor shall maintain records which show that the commitment to provide such benefits is enforceable, that the plan or program is financially responsible, that the plan or program has been communicated in writing to the laborers or mechanics affected, and show the cost anticipated or the actual cost incurred in providing benefits. Contractors or subcontractors employing apprentices or trainees under approved programs shall maintain written evidence of the registration of apprentices and trainees, and ratios and wage rates prescribed in the applicable programs. Contractors or subcontractors shall maintain complete social security numbers and home addresses for employees. Government agencies are entitled to request or review all relevant payroll information, including social security numbers and addresses of employees. Contractors and subcontractors are required to provide such information upon request.

1********************************************************************************************************1

FHWA Attachment No. 2

Standard Federal Equal Employment Opportunity Construction Contract Specifications (Executive Order 11246)

- As used in these Specifications:

- Covered area means the geographical area in which the Project is located.

- Director means Director, Office of Federal Contract Compliance Programs, United States Department of Labor or any person to whom the Director delegates authority.

- Employer identification number means the Federal Social Security number used on the Employer’s Quarterly Federal Tax Return, US Treasury Department Form 941.

- Minority includes:

- Black (a person having origins in any of the black African racial groups not of Hispanic origin);

- Hispanic (a person of Mexican, Puerto Rican, Cuban, Central or South American or other Spanish culture or origin, regardless of race);

- Asian and Pacific Islander (a person having originals in any of the original peoples of the Far East, Southeast Asia, the Indian Subcontinent, or the Pacific Islands); and

- American Indian or Alaskan Native (a person having origins in any of the original peoples of North America and maintaining identifiable tribal affiliations through membership and participating or community identification).

- Whenever the Contractor, or any subcontractor at any tier, subcontracts a portion of the work involving any construction trade, it shall physically include in each subcontract in excess of $10,000 the provisions of these specifications and the Notice which contains the applicable goals for minority and female participation and which is set forth in the solicitations from which this contract resulted.

- The Contractor shall implement the specific affirmative action standards provided in paragraphs 6a through p of these specifications. The goals set forth in the solicitation from which this contract resulted are expressed as percentages of the total hours of employment and training of minority and female utilization the Contractor should reasonably be able to achieve in each construction trade in which it has employees in the covered area. Covered Construction Contractors performing construction work in geographical areas where they do not have a Federal or federally assisted construction contract shall apply the minority and female goals established for the geographical area where the work is being performed. The Contractor is expected to make substantially uniform progress in meeting its goals in each craft during the period specified.

- Neither the provisions of any collective bargaining agreement nor the failure by a union with whom the Contractor has a collective bargaining agreement to refer either minorities or women shall excuse the Contractor’s obligations under these Specifications, Executive Order 111246, or the regulations promulgated pursuant thereto.

- In order for the nonworking training hours of apprentices and trainees to be counted in meeting the goals, such apprentices and trainees must be employed by the Contractor during the training period, and the Contractor must have made a commitment to employ the apprentices and trainees at the completion of their training, subject to the availability of employment opportunities. Trainees must be trained pursuant to training programs approved by the US Department of Labor.

- The Contractor shall take specific affirmative actions to ensure equal employment opportunity. The evaluation of the Contractor’s compliance with these specifications shall be based upon its effort to achieve maximum results from its actions.  The Contractor shall document these efforts fully, and shall implement affirmative action steps at least as extensive as the following:

- Ensure and maintain a working environment free of harassment, intimidation, and coercion at all sites in all facilities at which the Contractor’s employees are assigned to work. The Contractor, where possible, will assign two or more women to each construction project. The contractor shall specifically ensure that all foreman, superintendents, and other on-site supervisory personnel are aware of and carry out the Contractor’s obligation to maintain such a working environment with specific attention to minority or female individual working at such sites or in such facilities.

- Establish and maintain a current list of minority and female recruitment sources, provide written notification to minority and female recruitment sources and to community organizations when the Contractor or its unions have employment opportunities available, and maintain a record of the organizations’ responses.

- Maintain a current file of the names, addresses and telephone numbers of each minority and female off-the-street applicant and minority or female referral from a union, a recruitment source or community and of what action was taken with respect to each such individual. If such individual was sent to the union hiring hall for referral and was not referred back to the Contractor by the union or, if referred back to the Contractor, this shall be documented in the file with the reason therefore, along with whatever additional actions the Contractor may have taken.

- Provide immediate written notification to the Director when the union or unions with which the Contractor has a collective bargaining agreement has not referred to the contractor a minority person or women sent by the Contractor, or when the Contractor has other information that the union referral process has impeded the Contractor’s efforts to meet its obligations.

- Develop on-the-job training opportunities and/or participate in training programs for the area which expressly include minorities and women including upgrading programs and apprenticeship and trainee programs relevant to the Contractor’s employment needs, especially those programs funded or approved by the Department of Labor. The Contractor shall provide notice of these programs to the source compiles under 6b above.

- Disseminate the Contractor’s EEO policy by providing notice of the policy to unions and training programs and requesting their cooperation in assisting the Contractor in meeting its EEO obligations by including it in any policy manual and collective bargaining agreement; by publicizing it in the company newspaper, annual report, etc; by specific review of the policy with all management personnel and with all minority and female employees at least once a year; and by posting the company EEO policy on bulletin boards accessible to all employees at each location where construction work is performed.

- Review, at least annually, the company’s EEO policy and affirmative action obligations under these specifications with all employees having any responsibility for hiring, assignment, layoff, termination or other employment decisions including specific review of these items with on site supervisory personnel such as Superintendents, General Foremen, etc., prior to the initiation of construction work at any job site. A written record shall be made and maintained identifying the time and place of these meetings, persons attending, subject matter discussed, and disposition of the subject matter.

- Disseminate the Contractor’s EEO policy externally by including it in any advertising in the news median, specifically including minority and female news media, and providing written notification to and discussing the Contractor’s EEO policy with other Contractors and Subcontractors with whom the Contractor does or anticipates doing business.

- Direct its recruitment efforts, both oral and written, to minority, female and community organizations, to schools with minority and female students and to minority and female recruitment and training organizations serving the Contractor’s recruitment area and employment needs. Not later than one month prior to the date for the acceptance of applications for apprenticeship or other training by any recruitment source, the Contractor shall send written notification to organizations such as the above, describing the openings, screening procedures, and tests to be used in the selection process.

- Encourage present minority and female employees to recruit other minority persons and females and, where reasonable, provide after school, summer and vacation employment to minority and female youth both on the site and in other areas of a Contractor’s work force.

- Validate all tests and other selection requirements where there is an obligation to do so under 41 CFR Part 60-3.

- Conduct, at least annually, an inventory and evaluation at least of all minority and female personnel for promotional opportunities and encourage these employees to seek or to prepare for, through appropriate training, etc., such opportunities.

- Ensure that seniority practices, job classifications, work assignments and other personnel practices do not have a discriminatory effect by continually monitoring all personnel and employment related activities to ensure that the EEO policy and the Contractor’s obligations under these specifications are being carried out.

- Ensure that all facilities and company activities are nonsegregated except that separate or single-user toilet and necessary changing facilities shall be provided to assure privacy between the sexes.

- Document and maintain a record of all solicitations of offers for subcontracts from minority and female construction Contraction and suppliers, including circulation of solicitations to minority and female contractor associations and other business associations.

- Conduct a review, at least annually, of all supervisors’ adherence to and performance under the Contractor’s EEO policies and affirmative action obligations.

- Contractors are encouraged to participate in voluntary associations which assist in fulfilling one or more of their affirmative action obligations (6a through p). The efforts of a Contractor association, joint contractor union, Contractor-Community, or other similar group of which the Contractor is a member and participant may be asserted as fulfilling any one or more of its obligations under 6A through p of these Specifications provided that the Contractor actively participates in the group, make every effort to assure that the group has a positive impact on the employment of minorities and females in the industry, ensures that the concrete benefits of the program are reflected in the Contractor’s minority and female work force participation, make a good faith effort to meet its individual goals and can provide access to documentation which demonstrates the effectiveness of actions taken on behalf of the Contractor. The obligation to comply, however, is the Contractor’s and failure of such a group to fulfill an obligation shall not be a defense for the Contractor’s noncompliance.

- A single goal for minorities and a separate single goal for women have been established. The Contractor, however, is required to provide equal employment opportunity and to take affirmative action for all minority groups, both male and female, and all women both minority and nonminority. Consequently, the Contractor may be in violation of the Executive Order if a particular group is employed in a substantially disparate manner (for example, even though the Contractor has achieved its goals for women generally, the Contractor may be in violation of the Executive Order if a specific minority group of women is underutilized).

- The Contractor shall not use the goals or affirmative action standards to discriminate against any person because of race, color, religion, sex, or national origin.

- The Contractor shall not enter any Subcontract with any person or firm debarred from Government contracts pursuant to Executive Order 11246.

- The Contractor shall carry out such sanctions and penalties for violation of these specifications and of the Equal Opportunity Clause, including suspensions, termination and cancellation of existing subcontracts as may be imposed or ordered pursuant to Executive Order 11246, as amended, and its implementing regulations, by the Office of Federal Contract Compliance Programs. Any Contractor who fails to carry out such sanctions and penalties shall be in violation of these specifications and Executive Order 11246 as amended.

- The Contractor, in fulfilling its obligations under these specifications, shall implement specific affirmative action steps, at least as extensive as those standards prescribed in paragraph 6 of these specifications, so as to achieve maximum results from its efforts to ensure equal employment opportunity. If the Contractor fails to comply with the requirements of the Executive Order, the implementing regulations or these specifications, the Director shall proceed in accordance with 41 CFR 60-4.8.

- The Contractor shall designate a responsible official to monitor all employment related activity to ensure that the company EEO policy is being carried out, to submit reports relating to the provisions hereof as may be required by the Government and to keep records.  Records shall at least include for each employee the name, address, telephone number, construction trade, union affiliation if any, employee identification number when assigned, social security number, race, sex, status (such as mechanic, apprentice, trainee, helper, or laborer), dates of changes in status, hours worked per week in the indicated trade, rate of pay, and locations at which the work was performed. Records shall be maintained in an easily understandable and retrievable form; however, to the degree that existing records satisfy this requirement, contractors shall not be required to maintain separate records.

- Nothing herein provided shall be construed as a limitation upon the application of other laws which establish different standards of compliance or upon the application of requirements for the hiring of local or other area residents (such as those under the Public Works Employment Act of 1977 and the community Development Block Grant Program).

- Noncompliance by the Contractor with the requirements of the Affirmative Action Program for Equal Employment Opportunity may be cause for delaying or withholding monthly and final payments pending corrective and appropriate measures by the Contractor to the satisfaction of the Department.

FHWA Attachment No. 3

NOTICE OF REQUIREMENT FOR AFFIRMATIVE ACTION TO ENSURE EQUAL OPPORTUNITY (EXECUTIVE ORDER 11246)

- The goals for minority and female participation, in the covered area, expressed in percentage terms for the Contractor’s aggregate work force in each trade, on all construction work are as shown on Page 2.

These goals are applicable to all the Contractor’s construction work (whether or not it is Federal or federally assisted) performed in the covered area. If the Contractor performs construction work in a geographical area located outside of the covered area, it shall apply the goals established for such geographical area where the work is actually performed. With regard to this second area, the Contractor also is subject to the goals for both its federally involved and nonfederally involved construction.

The Contractor’s compliance with the Executive Order and the regulations in 41 CFR Part 60-4 shall be based on its implementation of the Equal Opportunity Clause, specific affirmative action obligations required by the specifications set forth in 41 CFR 60-4. (3) a, and its efforts to meet the goals. The hours of minority and female employment and training must be substantially uniform throughout the length of the contract, and in each trade, and the Contractor shall make a good faith effort to employ minorities and women evenly on each of its projects. The transfer of minority or female employees or trainees from Contractor to Contractor or from project to project for sole purpose of meeting the Contractor’s goals shall be a violation of the contract, the Executive Order and the regulations in 41 CFR Part 60-4. Compliance with the goals will be measured against the total work hours performed.

- The Contractor will provide the Department with written notification in triplicate within 10 working days of award of any construction subcontract in excess of $10,000 at any tier for construction work under the contract resulting from this solicitation. The notification will list the name, address and telephone number of the subcontractor; employer identification number of the subcontractor; estimated dollar amount of the subcontract; estimated starting and completion dates of the subcontract; and the geographical area in which the contract is to be performed.

- As used in this Notice and in the Contract resulting from this solicitation the covered area is the county or counties in which the Project is located.

- If a project is located in more than one county, the minority work hours goal, only, will be determined by the county which serves as the primary source of hiring or, if workers are obtained almost equally from one or more counties, the single minority goal will be the average of the affected county goals.

Work Hour Goals In Each Trade For Minority And Female Participation

| COUNTY | MINORITY PARTICIPATION | FEMALE PARTICIPATION |
| --- | --- | --- |
|  | PERCENT | PERCENT |
| Atlantic | 18.2 | 6.9 |
| Bergen | 15 | 6.9 |
| Burlington | 17.3 | 6.9 |
| Camden | 17.3 | 6.9 |
| Cape May | 14.5 | 6.9 |
| Cumberland | 16 | 6.9 |
| Essex | 17.3 | 6.9 |
| Gloucester | 17.3 | 6.9 |
| Hudson | 12.8 | 6.9 |
| Hunterdon | 17 | 6.9 |
| Mercer | 16.4 | 6.9 |
| Middlesex | 15 | 6.9 |
| Monmouth | 9.5 | 6.9 |
| Morris | 17.3 | 6.9 |
| Ocean | 17 | 6.9 |
| Passaic | 12.9 | 6.9 |
| Salem | 12.3 | 6.9 |
| Somerset | 17.3 | 6.9 |
| Sussex | 17 | 6.9 |
| Union | 17.3 | 6.9 |
| Warren | 1.6 | 6.9 |

FHWA Attachment No. 4

State Of New Jersey Equal Employment Opportunity

For Contracts Funded By FHWA

The parties to this Agreement do hereby agree that the provisions of NJSA 10:2-1 through 10:2-4 and NJSA 10:5-31 et seq (PL 1975, c 127, as amended and supplemented) dealing with discrimination in employment on public contracts, and the rules and regulations promulgated pursuant thereunto, are hereby made a part of this contract and are binding upon them.

During the performance of this contract, the Contractor agrees as follows:

a.	The Contractor or subcontractor, where applicable, will not discriminate against any employee or applicant for employment because of age, race, creed, color, national origin, ancestry, marital status or sex. The Contractor will take affirmative action to ensure that such applicants are recruited and employed, and that employees are treated during employment, without regard to their age, race, creed, color, national origin, ancestry, marital status or sex. Such action shall include but not be limited to the following: employment, upgrading, demotion, or transfer, recruitment or recruitment advertising; layoff or termination; rates of pay or other forms of compensation; and selection for training, including apprenticeship. The Contractor agrees to post in conspicuous places, available to employees and applicants for employment, notices to be provided by the Division of Civil Rights/Affirmative Action setting forth provisions of this nondiscrimination clause;

b.	The Contractor or subcontractor, where applicable will, in all solicitations or advertisements for employees placed by or on behalf of the Contractor, state that all qualified applicants will receive consideration for employment without regard to age, race, creed, color, national origin, ancestry, marital status or sex;

c.	The Contractor or subcontractor, where applicable, will send to each labor union or representative of workers with which it has a collective bargaining agreement or other contract or understanding, a notice, to be provided by the Division of Civil Rights/Affirmative Action, advising the labor union or workers’ representative of the contractor’s commitments under this act and shall post copies of the notice in conspicuous places available to employees and applicants for employment.

The notices referred to in paragraphs a and c may be obtained from the Supervising Engineer of Construction or his representative at the preconstruction conference.

FHWA Attachment No. 5

EMERGING SMALL BUSINESS ENTERPRISE UTILIZATION ATTACHMENT

FHWA FUNDED CONTRACTS

I	UTILIZATION OF EMERGING SMALL BUSINESS ENTERPRISE (ESBE) AS CONTRACTORS, MATERIALS SUPPLIERS AND EQUIPMENT LESSORS.

The New Jersey Department of Transportation (NJDOT) advises each contractor or subcontractor that failure to carry out the requirements set forth in this attachment shall constitute a breach of contract and, after the notification of the applicable federal agency, may result in termination of the agreement or contract by the Department or such remedy as the Department deems appropriate. Requirements set forth in this section shall also be physically included in all subcontracts in accordance with USDOT requirements.

II	POLICY.

It is the policy of the NJDOT that Emerging Small Business Enterprises (ESBE), as defined in Section IV, Part B below, shall have an opportunity to participate in the performance of contracts financed in whole or in part with federal funds. In furtherance of this policy the NJDOT has established an Emerging Small Business Enterprise Program. This program is designed to promote participation and shared economic opportunity by smaller firms who qualify as ESBE’s in NJDOT construction contracts and is undertaken pursuant to the authority contained in 23 CFR Part 26.

III.	CONTRACTOR’S ESBE OBLIGATION.

The contractor agrees to ensure that ESBE’s, as defined in Section IV, Part B below, have an equal opportunity to participate in the performance of contracts and subcontracts financed in whole or in part with federal funds. In performing work under this agreement with the NJDOT, the contractor shall take all necessary and reasonable steps in accordance with the provisions of this attachment to ensure that ESBE’s have the maximum opportunity to compete for and perform contracts. The contractor shall not discriminate on the basis of race, color, national origin, or sex in the performance of any contract obligation including, but not limited to, its performance of its obligations under this ESBE attachment.

IV.	GOALS FOR THIS PROJECT.

A.	This project includes a goal of awarding       percent of the total contract value to subcontractors, equipment lessors and/or material suppliers, which qualify as ESBE’s.

1.	Failure to meet the minimum goal placed on this project, or to provide a good faith effort to meet the minimum goal, may be grounds for rejection of the bid as being non-responsive.

2.	As a source of information only, an ESBE Directory is available from the Division of Civil Rights/Affirmative Action. Use of this listing does not relieve the contractor of its responsibility to seek out ESBE’s not listed, prior to bid. If a contractor proposes to use an ESBE contractor not listed in the ESBE Directory, the proposed ESBE firm must submit a completed certification application to the Division of Civil Rights/Affirmative Action, fifteen (15) days prior to bid date.

B.	DEFINITIONS.

1.	Emerging Small Business Enterprise is defined as: a for-profit business concern classified as a small business pursuant to the appropriate Small Business Administration regulations, and which is owned and controlled by individuals who do not exceed the personal net worth criteria ($750,000) established in 49 CFR Part 26.

2.	Owned and Controlled is defined as: that at least 51% of the ownership interests as well as the management and daily business operations of the firm reside in individuals whose personal net worth does not exceed the requirements established in 49 CFR, Part 26.

V.	COUNTING ESBE PARTICIPATION.

A.	Each ESBE is subject to a certification procedure to ensure its ESBE eligibility status prior to the award of contract. In order to facilitate this process it is advisable for the bidder to furnish names of proposed ESBE’s to the Department 15 days before bid opening. Once a firm is determined to be a bona fide ESBE by the Division of Civil Rights/Affirmative Action, the total dollar value of the contract awarded to the ESBE is counted toward the applicable goal.

B.	The contractor may count toward its ESBE goal only expenditures to ESBE’s that perform a commercially useful function in the work of a contract. An ESBE is considered to perform a commercially useful function when it is responsible for execution of a distinct element of the work of a contract and carrying out its responsibility by actually performing, managing and supervising the work involved. To determine whether an ESBE is performing a commercially useful function, the contractor shall evaluate the amount of work contracted, industry practice and other relevant factors.

C.	If a ESBE does not perform or exercise responsibility for at least 30 percent of the total cost of its contract with its own work force, or the ESBE subcontracts a greater portion of the work of a contract than would be expected on the basis of normal industry practice for the type of work involved, you must presume that it is not performing a commercially useful function.

D.	If the prime contractor is a certified ESBE, payments made to the contractor for work performed by the contractor will be applied toward the ESBE goal. Payments made to the prime contractor for work performed by non-ESBE’s will not be applied toward the ESBE goal.

E.	The prime contractor may count 60 percent of its expenditures to ESBE suppliers that are not manufacturers, provided that the ESBE supplier performs a commercially useful function in the supply process. The contractor may count 100% of its expenditure to ESBE suppliers who are also manufacturers. Manufacturers receive 100% credit toward the ESBE goal.

VI	GOOD FAITH EFFORT.

To demonstrate sufficient reasonable efforts to meet the ESBE contract goals, a bidder shall document the steps it has taken to obtain ESBE participation, including but not limited to the following:

A.	Attendance at a pre-bid meeting, if any, scheduled by the Department to inform ESBE’s of prime contracting and subcontracting opportunities under a given solicitation.

B.	Advertisement in general circulation media, trade association publications, and small business publications for at least 20 days before bids are due. If 20 days are not available, publication for a shorter reasonable time is acceptable.

C.	Written notification to ESBE’s that their interest in the contract is solicited;

D.	Efforts made to select portions of the work proposed to be performed by ESBE’s in order to increase the likelihood of achieving the stated goal;

E.	Efforts made to negotiate with ESBE’s for specific bids including at a minimum:

1.	The names, addresses and telephone numbers of ESBE’s that were contacted;

2.	A description of the information provided to ESBE’s regarding the plans and specifications for the work to be performed; and

3.	A statement of why additional agreements with ESBE’s were not reached;

F.	Information regarding each ESBE the bidder contacted and rejected as unqualified and the reasons for the bidder’s conclusion;

G.	Efforts made to assist the ESBE in obtaining bonding or insurance required by the bidder or the department.

NOTE:	If the Division of Civil Rights/Affirmative Action determines that the apparent successful low bidder has failed to meet the requirements of this section, the bidder will be afforded the opportunity for an administrative reconsideration of that determination prior to the award or rejection of the contract. As part of the administrative reconsideration process, the bidder will have the opportunity to provide written documentation or argument concerning the issue of whether it met the goal or made adequate good faith efforts to do so. NJDOT will send the bidder a written decision on reconsideration, explaining the basis for finding that the bidder did or did not meet the goal or make adequate good faith efforts to do so. The result of the reconsideration process is not administratively appealable to the USDOT.

VII	SUBMISSION OF REQUIRED DOCUMENTS.

A.	The following shall be submitted either with the bid or to the Division of Civil Rights and Affirmative Action no later than seven (7) State business days after the date of receipt of bids.

1.	ESBE Form “A2” - Schedule of ESBE Participation. List all ESBE’s participating in the contract; listing the scope of work, dollar value and percent of total contract to be performed.

2.	Supplement to ESBE Form “A2”- A list of all subcontractors who submitted bids or quotes on this project.

3.	ESBE Form B - Affidavit of Emerging Small Business Enterprise. Each proposed ESBE not listed in the NJDOT ESBE directory must submit Form B attesting to its validity as an ESBE. (All firms must be certified by the Department’s ESBE Coordinator prior to award of the contract).

4.	Request for Exemption - In the event that the bidder fails to meet the specified goal, they must submit within Seven State business days of the bid, a written request for exemption to the goal. This request must include a written statement addressing Items A through G in Article VI of this attachment in addition to an accounting of the reason(s) why each items in the bid proposal was not subcontracted. Submittal of such request does not imply departmental approval. An assessment of the material will be conducted by the Department’s Division of Civil Rights/Affirmative Action.

5.	The name of the person who is serving as its ESBE Liaison Officer

B.	The State Highway Engineer will be the sole judge of proper compliance and action taken in fulfilling the requirements as set forth herein.

VIII	ESBE LIAISON OFFICER.

A.	The contractor shall designate an ESBE Liaison Officer who shall be responsible for the administration if its ESBE program in accordance with the requirements of this attachment.

IX	OBLIGATIONS AFTER AWARD OF THE CONTRACT.

If at any time following the award of contract, the contractor intends to sublet any portion(s) of the work under said contract, or intends to purchase material or lease equipment not contemplated during preparation of bids, said contractor shall take the following actions:

1.	Notify the Resident Engineer, in writing, of the type and approximate value of the work the contractor intends to accomplish by such subcontract, purchase order or lease.

2.	Attempt to obtain a qualified ESBE to perform the work.

3.	Submit the Post-Award ESBE Certification Form to the Regional Supervising Engineer with his application to sublet or prior to purchasing material or leasing equipment. Post Award ESBE forms may be obtained from the Resident Engineer.

X	CONSENT BY DEPARTMENT TO SUBLETTING.

The Department will not approve any subcontract proposed by the Contractor unless and until said contractor has complied with the terms of this attachment.

XI	SELECTION AND RETENTION OF SUBCONTRACTORS.

A.	The contractor is further obligated to provide the Resident Engineer with a listing of firms, organizations or enterprises solicited and those utilized as subcontractors on the proposed project. Such listing shall clearly delineate which firms are classified as an ESBE.

B.	The contractor shall identify all efforts it made to identify and retain an ESBE as a substitution subcontractor when the arrangements with the original ESBE proved unsuccessful shall be submitted in writing to the Department’s ESBE Coordinator for approval. Work in the category concerned shall not begin until such approval is granted in writing.

C.	Notification of a subcontractor’s termination will be sent to the Department by the contractor through the Resident Engineer. Said termination notice will state whether the subcontractor is an ESBE and the reason for termination.

XII	CONCILIATION.

Allegations of breach of any obligation contained in these ESBE provisions will be investigated by the Federal Office of Contract Compliance in conjunction with the Division of Civil Rights/Affirmative Action of the New Jersey Department of Transportation and the Federal Highway Administration.

XIII	DOCUMENTATION.

A.	The Department or the federal funding agencies may at any time require such information as is deemed necessary in the judgement of the Department to ascertain the compliance of any bidder or contractor with the terms of these provisions.

B.	Record and Reports.

The Contractor shall keep such records as are necessary to determine compliance with its Emerging Small Business Enterprise Utilization obligations. The records kept by the contractor will be designed to indicate:

1.	The names of ESBE contractors, equipment lessors and material suppliers contacted for work on this project.

2.	Work, services and materials which are not performed or supplied by the prime contractor.

3.	The actual dollar value of work subcontracted and awarded to ESBE’s.

4.	Efforts taken in seeking out and utilizing ESBE’s. This would include solicitations, quotes and bids regarding project work items, supplies, leases, or other contract items.

5.	Documentation of all correspondence, contacts, telephone calls, or other actions taken to obtain the services of ESBE’s on this project.

6.	Records of all ESBE’s who have submitted quotes/bids to the contractor on the project.

C.	Submit reports, as required by the Department, on those contracts and other business transactions executed with ESBE’s in such form and manner as may be prescribed by the Department.

D.	All such records must be maintained for a period of three (3) years following acceptance of final payment and will be available for inspection by the Department.

XIV	PAYMENT TO SUBCONTRACTORS.

The Contractor agrees to pay its subcontractors in accordance with the Specifications

XV	NON-COMPLIANCE.

Failure by the bidder to comply with these provisions may result in rejection of the bid. The contractor may further be declared ineligible for future Department contracts.

FHWA Attachment No. 5

DISADVANTAGED BUSINESS ENTERPRISE UTILIZATION ATTACHMENT

FHWA FUNDED CONTRACTS

I	UTILIZATION OF DISADVANTAGED BUSINESSES AS CONTRACTORS, MATERIAL SUPPLIERS AND EQUIPMENT LESSORS.

The New Jersey Department of Transportation (NJDOT) advises each contractor or subcontractor that failure to carry out the requirements set forth in this attachment shall constitute a breach of contract and, after the notification of the applicable federal agency, may result in termination of the agreement or contract by the Department or such remedy as the Department deems appropriate. Requirements set forth in this section shall also be physically included in all subcontracts in accordance with USDOT requirements.

II	POLICY

It is the policy of NJDOT that Disadvantaged Business Enterprises, as defined in 49 CFR, Part 26; Titles I & V of the Intermodal Surface Transportation Efficiency Act of 1991 (ISTEA); the Transportation Equity Act for the 21st Century (TEA-21); and Section V, Part B below, shall have equal opportunity to participate in the performance of contracts financed in whole or in part with federal funds under this agreement. Consequently, the DBE requirements of 49 CFR, Part 26, Subsections A, C and F apply to this agreement.

III	CONTRACTOR’S DBE OBLIGATION

The NJDOT and its Contractor agree that Disadvantaged Business Enterprises, as defined in 49 CFR Part 26, Subpart A; and in the Intermodal Surface Transportation Efficiency Act of 1991 (ISTEA) and the Transportation Equity Act for the 21st Century (TEA-21), and Section V, Part B below, have equal opportunity to participate in the performance of contracts and subcontracts financed in whole or in part with federal funds provided under this agreement. In this regard, the NJDOT and all Contractors shall take all necessary and reasonable steps in accordance with 49 CFR, Part 26 to ensure that Disadvantaged Businesses are given equal opportunity to compete for and to perform on NJDOT federally funded contracts.  The NJDOT and its Contractors shall not discriminate on the basis of race, color, national origin, or sex in the award and performance of USDOT assisted contracts.

IV	COMPLIANCE

To signify and affirm compliance with the provisions of this attachment, the bidder shall complete the Schedule of DBE Participation (Form A) included in the bid package and all forms and documents required in Sections VII and VIII of these provisions which will be made a part of the resulting contract.

V	GOALS FOR THIS PROJECT

A.	This Project includes a goal of awarding      percent of the total contract value to subcontractors, equipment lessors and/or material suppliers that qualify as Disadvantaged Business Enterprises (DBEs).

1.	Failure to meet the minimum goal placed on this project, or to provide a “good faith effort” to meet the minimum goal, may be grounds for rejection of the bid as being non-responsive.

2.	As a source of information only, a Disadvantaged Business Enterprise Directory is available from the Division of Civil Rights and Affirmative Action. Use of this listing does not relieve the Contractor of their responsibility to seek out other DBE’s not listed, prior to bid.  If a contractor proposes to use a DBE contractor not listed in the DBE Directory, the proposed DBE firm must submit a completed certification application to the Division of Civil Rights and Affirmative Action, fifteen (15) days prior to bid date.

B.	DEFINITIONS

1.	Disadvantaged Business Enterprise is a firm, “Owned and controlled” by socially and economically disadvantaged individuals that is also a small business concern, as defined pursuant to Section 3 of the Small Business Act and Small Business Administration Regulations (13 CFR, Part 121) which also does not exceed the revenue cap on averaged annual gross receipts applicable to the firm’s particular Standard Industrial Classification (SIC Code).

2.	Owned and Controlled is defined as a firm which is at least fifty-one (51%) percent owned by one or more disadvantaged individuals, or in the case of a publicly owned business, at least fifty-one (51%) percent of the stock is owned by one or more disadvantaged individuals, and whose management and daily business operations are controlled by one or more such individuals.

3.	Any individual in one of the following groups who is also a U.S. Citizen or lawfully admitted permanent resident presumed to be socially and economically disadvantaged under the DBE Program.

- Black Americans – includes any persons having origins in any of the black racial groups of Africa;

- Hispanic Americans - includes persons of Mexican, Puerto Rican, Cuban, Dominican, Central or South American, or other Spanish or Portuguese culture; or origin, regardless of race;

- Native American - includes persons who are American Indians, Eskimos, Aleuts or Native Hawaiians;

- Asian-Pacific Americans - includes persons whose origins are from Japan, China, Taiwan, Korea, Burma (Myanmar), Vietnam, Laos, Cambodia (Kampuchea), Thailand, Malaysia, Indonesia, the Philippines, Brunei, Samoa, Guam, the U.S. Trust Territories of the Pacific Islands (Republic of Palau) the Commonwealth of the Northern Mariana Islands, Macao, Fiji, Tonga, Kiribati, Juvalu, Nauru, Federated States of  Micronesia or Hong Kong;

- Subcontinent Asian Americans - includes persons whose origins are from India, Pakistan, Bangladesh, Bhutan, the Maldives Islands, Nepal or Sri Lanka;

- Women - regardless of race;

- Other - Any additional groups whose members are designated as socially and economically disadvantaged by the Small Business Administration, at such time as the SBA designation becomes effective; or a determination made by the NJDOT’s Division of Civil Rights and Affirmative Action, on a case-by-case basis;

VI	COUNTING DBE PARTICIPATION

A.	Each DBE is subject to a certification procedure to ensure its DBE eligibility status prior to award of contract. In order to facilitate this process it is advisable for the bidder to furnish the names of proposed DBE’s to the Department fifteen (15) days before bid opening. Once a firm is determined to be a bona fide DBE by the Division of Civil Rights and Affirmative Action, the total dollar value of the contract awarded to the DBE is counted toward the applicable DBE goal.

B.	The Contractor may count toward its DBE goal only expenditures to DBE’s that perform a commercially useful function in the work of a contract. A DBE is considered to perform a commercially useful function when it is responsible for execution of a distinct element of the work of a contract and carrying out its responsibility by actually performing, managing and supervising the work involved.  To determine whether a DBE is performing a commercially useful function, the Contractor shall evaluate the amount of work subcontracted, industry practice and other relevant factors.

C.	If a DBE does not perform or exercise responsibility for at least 30 percent of the total cost of its contract with its own workforce, or the DBE subcontracts a greater portion of the work of a contract than would be expected on the basis of normal industry practice for the type of work involved, you must presume that it is not performing a commercially useful function.

D.	If the prime Contractor is a certified DBE, payments made to the Contractor for work performed by the Contractor will be applied toward the DBE goal. Payments made to the Contractor for work performed by non-DBE’s will not be applied toward the goal.

E.	The prime Contractor may count 60 percent of its expenditures to DBE suppliers who are not Manufacturers, provided that the DBE supplier performs a commercially useful function in the supply process.  The contractor may count 100% of its expenditure to DBE suppliers who are also manufacturers. Manufacturers receive 100% credit toward the DBE goal.

F.	When a DBE subcontractor sublets part of the work of its contract to another firm, the value of the subcontract work may be counted towards the DBE goals only if the subcontractor itself is a DBE.  Work that a DBE subcontractor subcontracts to a non-DBE firm, does not count toward DBE goals.

VII	GOOD FAITH EFFORT

To demonstrate sufficient reasonable efforts to meet the DBE contract goals, a bidder shall document the steps it has taken to obtain DBE participation, including but not limited to the following:

A.	Attendance at a pre-bid meeting, if any, scheduled by the Department to inform DBE’s of subcontracting opportunities under a given solicitation.

B.	Advertisement in general circulation media, trade association publications, as well as minority-focus media for at least 20 days before bids are due.  If 20 days are not available, publication for a shorter reasonable time is acceptable.

C.	Written notification to DBE’s that their interest in the contract is solicited;

D.	Efforts made to select portions of the work proposed to be performed by DBEs in order to increase the likelihood of achieving the stated goal;

E.	Efforts made to negotiate with DBE’s for specific sub-bids including at a minimum:

- The names, addresses and telephone numbers of DBE’s that were contacted;

- A description of the information provided to DBE’s regarding the plans and Specifications for portions of the work to be performed; and

- A statement of why additional agreements with DBE’s were not reached;

F	Information regarding each DBE the bidder contacted and rejected as unqualified and the reasons for the bidder’s conclusion;

G.	Efforts made to assist the DBE in obtaining bonding or insurance required by the Bidder or the Department.

NOTE: If the Division of Civil Rights and Affirmative Action determines that the apparent successful low bidder has failed to meet the requirements of this section, the bidder will be afforded the opportunity for administrative consideration prior to the award or rejection of the contract. As part of the administrative reconsideration process, the bidder will have the opportunity to provide written documentation or argument concerning the issue of whether it met the goal or made adequate good faith efforts to do so. NJDOT will send the bidder a written decision on reconsideration, explaining the basis for finding that the bidder did or did not meet the goal or make adequate good faith efforts to do so. The result of the reconsideration process is not administratively appealable to the USDOT.

VIII	AFFIRMATIVE ACTION PLANS

A.	General contractors are required to submit their firm’s Affirmative Action Program annually to the Division of Civil Rights and Affirmative Action.  Until such time as these programs are submitted and approved, Contractors must have their programs in the Division of Civil Rights and Affirmative Action no later than seven (7) State business days after the date of receipt of bids.

B.	This program will include, but is not limited to the following:

- The name of the Contractor’s D/ESBE Liaison Officer to administer the firm’s Disadvantaged Business Program.

- An explanation of the affirmative action methods used in seeking out and considering Disadvantaged Business Enterprises as subcontractors, material suppliers or equipment lessors.

- An explanation of affirmative action methods intended to be used in seeking out and considering Disadvantaged Business Enterprises as subcontractors, material suppliers or equipment lessors. This refers to the Contractor’s ongoing responsibility, i.e., Disadvantaged Business Enterprise/Affirmative Action activities after the award of the contract and for the duration of said project.

C.	The following shall be submitted either with the bid or to the Division of Civil Rights and Affirmative Action no later than seven (7) State business days after the date of receipt of bids.

- DBE Form “A” - Schedule of DBE Participation. List all DBE’s participating in the contract listing the scope of work, dollar value and percent of total contract to be performed.

- Supplement to DBE Form “A” - A list of all subcontractors who submitted bids or quotes on this project.

- DBE Form B - Affidavit of Disadvantaged Business Enterprise. Each proposed DBE not listed in the NJDOT DBE directory must submit Form B attesting to its validity as a DBE. (All firms must be certified by the Department’s D/ESBE Liaison Officer prior to award of the contract).

- Request for Exemption - In the event that the bidder fails to meet the specified goal, they must submit within seven State business days of the bid, a written request for exemption to the goal.  This request must include a written statement addressing Items A through G in Article VII of this attachment in addition to an accounting of the reason(s) why each items in the bid proposal was not subcontracted. Submittal of such request does not imply Departmental approval. An assessment of the material will be conducted by the Department’s Division of Civil Rights and Affirmative Action.

IX	AFFIRMATIVE ACTION AFTER AWARD OF THE CONTRACT

If at any time following the award of contract, the Contractor intends to sublet any portion(s) of the work under said contract, or intends to purchase material or lease equipment not contemplated during preparation of bids, said Contractor shall take affirmative action:

- To notify the Resident Engineer, in writing, of the type and approximate value of the work which the Contractor intends to accomplish by such subcontract, purchase order or lease.

- To signify and affirm compliance with the provisions of this Section, the Contractor shall submit the Post-Award DBE Certification Form to the Regional Supervising Engineer with his application to sublet or prior to purchasing material or leasing equipment. Post Award DBE forms may be obtained from the Resident Engineer.

- To give disadvantaged firms equal consideration with non-minority firms in negotiation for any subcontracts, purchase orders or leases.

- If a prime contractor fails to meet its original DBE obligation, they must request an exemption to the goal following criteria in Section VIII (C)(4) and provide a good faith effort thereof. This request must include a written statement addressing each of the Good Faith Efforts outlined in Section VII, A-G.

X	CONSENT BY DEPARTMENT TO SUBLETTING

The Department will not approve any subcontract proposed by the Contractor unless and until said Contractor has complied with the terms of this attachment.

XI	SELECTION AND RETENTION OF SUBCONTRACTORS

A.	The Contractor is further obligated to provide the Resident Engineer with a listing of firms, organizations or enterprises solicited and those utilized as subcontractors on the proposed project. Such listing shall clearly delineate which firms are classified as disadvantaged.

B.	Efforts made to identify and retain a Disadvantaged Business Enterprise as a substitution subcontractor when the arrangements with the original DBE proved unsuccessful, shall be submitted in writing to the Department’s D/ESBE Liaison Officer for approval. Work in the category concerned shall not begin until such approval is granted in writing.

C.	Notification of a subcontractor’s termination will be sent to the Department by the Contractor through the Resident Engineer. Said termination notice will include the subcontractor’s ethnic classification and reason for termination.

XII	CONCILIATION

In cases of alleged discrimination regarding these DBE provisions and guidelines, an investigation will be undertaken by the Federal Office of Contract Compliance in conjunction with the Division of Civil Rights and Affirmative Action of the New Jersey Department of Transportation and the Federal Highway Administration.

XIII	DOCUMENTATION

A.	The Department or the federal funding agencies may at any time require such information as is deemed necessary in the judgment of the Department to ascertain the compliance of any bidder or contractor with the terms of these provisions.

B.	Record and Reports.

The Contractor shall keep such records as are necessary to determine compliance with its Disadvantaged Business Enterprise Utilization obligations. The records kept by the Contractor will be designed to indicate:

- The names of disadvantaged subcontractors, equipment lessors and material suppliers contacted for work on this project.

- The type of work to be done, materials to be utilized or services to be performed other than the work of the prime contractor on the project.

- The actual dollar value of work subcontracted and awarded to DBE’s.

- The progress being made and efforts taken in seeking out and utilizing Disadvantaged Business Enterprises.  This would include solicitations, quotes and bids regarding project work items, supplies, leases, etc.

- Documentation of all correspondence, contacts, telephone calls, etc., to obtain the services of Disadvantaged Business Enterprises on this project.

- Records of all DBE’s and non-DBEs who have submitted quotes/bids to the Contractor on the project.

C.	Submit reports, as required by the Department, on those contracts and other business transactions executed with Disadvantaged Business Enterprises in such form and manner as may be prescribed by the Department.

D.	All such records must be maintained for a period of three (3) years following acceptance of final payment and will be available for inspection by the Department.

XIV	PAYMENT TO SUBCONTRACTORS

The Contractor agrees to pay its subcontractors in accordance with the Specifications.

XV	NON-COMPLIANCE

Failure by the bidder to comply with the Specifications may result in rejection of the bid. The Contractor may further be declared ineligible for future Department contracts.

FHWA Attachment No. 5 (A)

INCENTIVE PROGRAM DISADVANTAGED BUSINESS ENTERPRISE UTILIZATION ATTACHMENT FOR FHWA FUNDED CONTRACTS

I	PURPOSE.

To ensure that certified Disadvantaged Business Enterprises (DBE’s), as defined in 49 CFR Part 26, have the maximum opportunity to compete for and perform on Department construction projects.

II	INTENT.

To encourage prime contractors to utilize the services of DBE’s who have not previously been prime contractors or subcontractors on Department projects, and afford DBE’s the opportunity to again experience in Department construction contract work.

III	ELIGIBILITY.

Only prime contractors and DBE’s certified prior to the date of bid, or prospective DBE’s that have submitted to the Division of Civil Rights/Affirmative Action on or before the day of bid a completed “New Jersey Department of Transportation Disadvantaged Business Enterprise Disclosure Affidavit” (PR-131) and all required documentation and have never been either prime contractor or subcontractor on Department construction projects will be eligible for participation in this program. A list of those eligible DBE’s will be available from the Division of Civil Rights/Affirmative Action. Any bidder who submits the name of a certified first-time DBE as part of its goal commitment is also eligible. Any DBE participating in the program must submit to the prime contractor a certification that they have never been either a prime contractor or subcontractor on a Department construction project under their present name or any other name. The prime contractor shall submit this certification with their required DBE submission.

IV	INCENTIVE.

Prime contractors utilizing first-time DBE’s will be given a credit toward their goal percentage identified in companion document “Disadvantaged Business Enterprise Utilization Attachment For FHWA Funded Contracts”, dated September 1987, revised January 1989, September 1992 and May 1995, equal to the actual dollar amount subcontracted to a first time DBE with the total project credit limited to two percent (2%) of the total bid price but not to exceed $200,000. This extra credit will reduce the goal percentage award as well as be applicable to the reduced goal percentage.

V	PROGRAM REQUIREMENTS.

A.	A prime contractor may present any number of first time DBE’s for each project. Credit will be given only for the actual amount subcontracted up to the limits established in IV above.

B.	The prime contractor shall be responsible for the entire DBE goal percentage established for the project.

C.	Failure to use a first time DBE shall cause the original goal award percentage prior to applying first time DBE credits to remain in effect.

D.	Failure to meet the goal award percentage, coupled with a lack of good faith effort as determined by the Division of Civil Rights/Affirmative Action, will be considered to be non-compliance on the part of the prime contractor who may be placed in show cause and subsequently be grounds for rejection of the bid as nonresponsive.

FHWA Attachment No.6

EQUAL EMPLOYMENT OPPORTUNITY SPECIAL PROVISIONS

1.	General

a.	Equal employment opportunity requirements not to discriminate and to take affirmative action to assure equal employment opportunity as required by Executive Order 11246 and Executive Order 11375 are set forth in Required Contract Provisions (Form FHWA-1273) and these Special Provisions which are imposed pursuant to Section 140 of Title 23 USC, as established by Section 22 of the Federal Aid Highway Act of 1968. The requirements set forth in these Special Provisions shall constitute the specific affirmative action requirements for project activities under this contract and supplement the Equal Employment Opportunity requirements set forth in the Required Contract Provisions.

b.	The Contractor will work with the State agencies and the Federal Government in carrying out Equal Employment Opportunity obligations and in their review of activities under the contract.

c.	The Contractor and all subcontractors holding subcontracts, not including material suppliers, of $10,000 or more, will comply with the following minimum specific requirement activities of Equal Employment Opportunity.  The Contractor will include these requirements in every subcontract of $10,000 or more with such modification of language as is necessary to make them binding on the subcontractor.  (The equal employment opportunity requirements of Executive Order 11246, as set forth in Volume 6, Chapter 4, Section 1, Subsection 1 of the Federal-Aid Highway Program Manual, are applicable to material suppliers as well as contractors and subcontractors).

d.	Noncompliance by the Contractor with the requirements of the Affirmative Action Program for Equal Employment Opportunity may be cause for delaying or withholding monthly and final payments pending corrective and appropriate measures by the Contractor to the satisfaction of the Department.

2.	Equal Employment Opportunity Policy

The Contractor will accept as its operating policy the following statement which is designed to further the provisions of equal employment opportunity to all persons without regard to their race, color, religion, sex, or national origin, and to promote the full realization of equal employment opportunity through a positive continuing program:

It is the policy of this Company to assure that applicants are employed, and that employees are treated during employment, without regard to their race, religion, sex, color, or national origin.  Such action shall include employment, upgrading, demotion, or transfer; recruitment or recruitment advertising; layoff or termination; rates of pay or other forms of compensation; and selection for training, including apprenticeship, preapprenticeship, and on-the-job training.

3.	Equal Employment Opportunity Officer

The Contractor will designate and make known to the Department contracting officers an equal opportunity officer (hereinafter referred to as the EEO Officer) who will have the capability, authority and responsibility to effectively implement and promote an active contractor program of equal employment opportunity.

4.	Dissemination of Policy

a.	All members of the Contractor’s staff who are authorized to hire, supervise, promote, and discharge employees, or who recommended such action, or who are substantially involved in such action, will be made fully cognizant of, and will implement, the Contractor’s equal employment opportunity policy and contractual responsibilities to provide equal employment opportunity in each grade and classification of employment.  To ensure compliance, the following minimum actions will be taken:

(1)	An initial project site meeting with key supervisory and office personnel will be conducted before or at the start of work, and then not less than once every 6 months, at which time the Contractor’s equal employment opportunity program will be reviewed and explained.  The meetings will be conducted by the EEO Officer or other knowledgeable company official.

(2)	All new supervisory and office personnel will be given a thorough indoctrination by the EEO Officer or other knowledgeable company official covering all major aspects of the Contractor’s equal employment opportunity obligations within 30 days following their reporting for duty with the Contractor.

(3)	All personnel engaged in direct recruitment for the project will be instructed by the EEO Officer or appropriate company official concerning the Contractor’s procedures for locating and hiring minority and female employees.

b.	In order to make the Contractor’s equal employment opportunity policy known to all employees, prospective employees and potential sources of employees, i.e., schools, employment agencies, labor unions (where appropriate), college placement officers, etc., the Contractor will take the following actions:

(1)	Notices and posters setting forth the Contractor’s equal employment opportunity policy will be placed in areas readily accessible to employees, applicants for employment and potential employees.

(2)	The Contractor’s equal employment opportunity policy and the procedures to implement such policy will be brought to the attention of employees by means of meetings, employee handbooks, and/or other appropriate means.

5.	Recruitment

a.	When advertising for employees, the Contractor will include in all advertisements for employees the notation: “An Equal Opportunity Employer”.  All such advertisements will be published in newspapers or other publications having a large circulation among minority groups in the area from which the project work force would normally be derived.

b.	The Contractor will, unless precluded by a valid bargaining agreement, conduct systematic and direct recruitment through public and private employee referral sources likely to yield qualified minority and female applicants, including, but not limited to, State employment agencies, schools, colleges and minority-oriented organizations.  To meet this requirement, the Contractor will, through his EEO Officer, identify sources of potential minority and female employees, and establish procedures with such sources whereby applicants may be referred to the Contractor for employment consideration.

In the event the Contractor has a valid bargaining agreement providing for exclusive hiring hall referrals, he is expected to observe the provisions of that agreement to the extent that the system permits the Contractor’s compliance with the equal employment opportunity contract provisions.  (The US Department of Labor has held that where implementation of such agreements have the effect of discriminating against minorities or females, or obligates the Contractor to do the same, such implementation violates Executive Order 11246, as amended).

c.	The Contractor will encourage his present employees to refer minority and female applicants for employment by posting appropriate notices or bulletins in areas accessible to all such employees.  In addition, information and procedures pertaining to the referral of applicants will be discussed with employees.

6.	Personnel Actions

Wages, working conditions and employee benefits shall be established and administered, and personnel actions of every type, including hiring, upgrading, promotion, transfer, demotion, layoff, and termination, shall be taken without regard to race, color, religion, sex, or national origin.  The following procedures shall be followed:

a.	The Contractor will conduct a project site inspection at the start of work, and periodically thereafter, to ensure that working conditions and employee facilities do not indicate discriminatory treatment of project site personnel.

b.	The Contractor will periodically evaluate the spread of wages paid within each classification to determine any evidence of discriminatory wage practices.

c.	The Contractor will periodically review selected personnel actions in depth to determine whether there is evidence of discrimination.  Where evidence is found, the Contractor will promptly take corrective action.  If the review indicates that the discrimination may extend beyond the actions reviewed, such corrective action shall include all affected persons.

d.	The Contractor will promptly investigate all complaints of alleged discrimination made to the Contractor in connection with its obligations under this contract, and will resolve or attempt to resolve such complaints, within a reasonable time.  If the investigation indicates that the discrimination may affect persons other than the complainant, corrective action shall include such other persons.  Upon completion of each investigation, the Contractor will inform complainants of available avenues of appeal.

7.	Training Special Provisions

As part of the Contractor’s equal employment opportunity affirmative action program, training shall be provided as follows:

The Contractor shall provide on-the-job training aimed at developing full journey people in the type of craft or job classification involved.

The number of training positions will be____, where feasible, consisting of at least____ APPRENTICES and ____TRAINEES. TRAINEE HOURS=_____.

Apprentices are defined as registered members of an approved apprenticeship program recognized by the United States Department of Labor (USDOL) Bureau of Apprenticeship and Training (BAT) or a New Jersey State apprenticeship agency recognized by USDOL BAT (e.g., New Jersey Department of Education).  Graduates of the Pre-Apprenticeship Training Cooperative Program shall be classified as apprentices.  Trainees are defined as skilled, semi-skilled or lower level management individuals receiving training per one of the approved NJDOT “Revised Standard Training Guidelines” (available from the Division of Civil Rights).

Where feasible, at least 50% of the training positions will be assigned to Skilled Crafts which include but are not limited to Carpenters, Dockbuilders, Electricians, Ironworkers and Operating Engineers.

a.	Contractor Submission and NJDOT Approval of the Initial Training Program.

At or after the preconstruction conference and prior to the start of work, the Contractor shall submit a training program to the Resident Engineer for his or her review and comments prior to Division of Civil Rights review and approval. The Contractor’s training program shall include:

(1)	the number of trainees or apprentices to be trained in all selected Training Positions,

(2)	the Standard Program Hours for all positions,

(3)	an estimate of the Minimum Available Hours actually feasible on the project toward completion of the Standard Program Hours per position,

(4)	a training schedule of Estimated Start Dates for the apprentices or trainees, developed and coordinated with the project’s work progress schedule,

(5)	Training Guidelines for all positions, and

(6)	which training will be provided by the Contractor and which by Subcontractors.

The number of apprentices and trainees shall be distributed among the work classifications on the basis of the Contractor’s needs and the availability of journeypeople in the various crafts within a reasonable area of recruitment.  The Contractor shall submit timely, revised training programs as required throughout the project to ensure that feasible and Maximum Available Training is provided.  Maximum Available Training is defined as bringing each apprentice or trainee onto the project when work first becomes available in his/her craft and providing all available training until hours are no longer available.

b.	Assignment of Training to Subcontractors

In the event that portions of the contract work are subcontracted, the Contractor shall determine how many, if any, of the apprentices or trainees are to be trained by subcontractors, provided, however, that the Contractor shall retain the primary responsibility for meeting the training requirements imposed by these Training Special Provisions. The  Contractor shall also ensure that these Training Special Provisions are made applicable to such subcontracts.

c.	Requirements for Recruitment, Selection and Approval of Apprentices and Trainees

(1)	Apprentices or trainees should be in their first year of apprenticeship or training.  The Contractor shall interview and screen trainee candidates to determine if their actual work experience is equivalent to or exceeds that offered by the training program prior to submitting candidates, via the Resident Engineer, to the Division for review and approval or disapproval.

(2)	Training and upgrading of minorities (e.g., Blacks, Asians or Pacific Islanders, Native Americans or Alaskan Natives, Hispanics) and females toward journeyperson status is a primary objective of these Training Special Provisions.  Accordingly, the Contractor shall make every effort to enroll minorities and females, by conducting systematic and direct recruitment through public and private sources likely to yield minority and female apprentices or trainees, to the extent that such persons are available within a reasonable area of recruitment.  This training commitment is not intended, and shall not be used, to discriminate against any applicant for training, whether a member of a minority group or not.

(3)	No employee shall be employed as an apprentice or trainee in any position in which he or she has successfully completed a training course leading to journeyperson status or in which he or she has been employed as a journeyperson.  The Contractor shall satisfy this requirement by including appropriate questions in the employment application or by other suitable means and by submitting an accurate and complete “Apprentice/Trainee Approval Memorandum.” Regardless of the methods used, the Contractor’s records should document the findings in each case.

(4)	Skilled craft trainees may complete up to 3,000 total training hours on NJDOT projects, with an extension of an additional 1,000 hours permitted on a case-by-case basis.  Semi-skilled and lower-level management trainees attain journeyperson status upon completion of a training guideline and may complete up to three (3) different positions.

d.	Apprenticeship and Training Programs

(1)	The minimum length and type of training for each position  will be established in the training program selected by the Contractor and approved by NJDOT and the Federal Highway Administration.  NJDOT will approve a program if it is reasonably calculated to meet the equal employment opportunity obligations of the Contractor and to qualify the average apprentice or trainee for journeyperson status in the craft concerned by the end of the training period.

(2)	Apprenticeship programs registered with the US Department of Labor, Bureau of Apprenticeship and Training, or with a State apprenticeship agency recognized by USDOL BAT and training programs approved but not necessarily sponsored by the US Department of Labor, Employment and Training Administration, Bureau of Apprenticeship and Training shall also be considered acceptable provided such programs are being administered in a manner consistent with the equal employment obligations of Federal-aid highway construction contracts.  Approval or acceptance of a training program shall be obtained from the NJDOT Division of Civil Rights prior to commencing work on the positions covered by the Contractor’s training program.  The Division will review guidelines developed by the Contractor for approval or disapproval in accordance with the Training Guideline Approval Process described in the “Revised Standard Training Guidelines”.  The Division will also review existing guidelines for revision based on the same process.

(3)	It is the intention of these provisions that training be provided in construction crafts rather than clerk-typist or secretarial-type positions.  Training is permitted in lower level management positions (e.g., timekeepers), where the training is oriented toward project site applications.  Training in semi-skilled laborer positions is permitted provided that significant and meaningful training is available on the project site.  Some offsite, classroom training (e.g., safety, first aid instruction) may be permitted as long as such training is an integral part of an approved training program and does not comprise a significant part of the overall training.

e.	Reimbursement of the Contractor for Providing Training

(1)	The Contractor will be credited for each apprentice or trainee employed on the construction site who is currently enrolled or becomes enrolled in an approved program and will be reimbursed for such apprentices or trainees as provided hereinafter.  Payment  will be made under the pay item Trainees at the bid price in the Proposal per person-hour of training given an employee on this contract in accordance with an approved training program. If approved, payment will be made for training persons in excess of the number specified herein.  This reimbursement will be made even though the Contractor receives additional training program funds from other sources, provided such other sources do not specifically prohibit the Contractor from receiving other reimbursement.  Offsite, classroom training reimbursement may only be made to the Contractor when the company does one or more of the following and the apprentices or trainees are concurrently employed on a Federal-aid project:  contributes to the cost of the training and/or provides instruction to apprentices or trainees or pays their wages during the offsite, classroom training (e.g., safety, first aid instruction) period.

(2)	The Contractor shall pay apprentices and trainees according to the project-specific New Jersey Department of Labor Prevailing Wage Rate Determination for the project.

f.	Documentation Required to be Signed by Apprentices or Trainees and provided to NJDOT

(1)	At the start of training, the Contractor shall provide the Resident Engineer and each apprentice or trainee with an applicable “Training Guideline” and, at the conclusion of training, an accurate and complete “Training Certificate for Reporting Hours to NJDOT”, showing hours of training satisfactorily completed.

(2)	The Contractor shall maintain and submit an accurate and complete “NJDOT Contractor’s 1409 Quarterly Training Report” to the Resident Engineer within ten (10) days of the end of each training quarter (e.g., January 10, April 10, July 10, October 10); a copy shall also be given to each apprentice or trainee.

(3)	The Contractor shall maintain and submit accurate and complete “Biweekly Training Reports” to the Resident Engineer, and each apprentice or trainee, as periodic reports documenting performance under these Training Special Provisions.

g.	Training and Promotion

(1)	The Contractor shall assist in locating, qualifying, and increasing the skills of minority and female employees, and applicants for employment.

(2)	The Contractor shall advise employees and applicants for employment of available training programs and entrance requirements.

(3)	The Contractor shall periodically review the training and promotion potential of minority and female employees and encourage eligible employees to apply for such training and promotion.

h.	Determining Good Faith Compliance

(1)	Per the approved program or guideline, the Contractor shall provide Maximum Available Training to apprentices and trainees by beginning their training as soon as feasible with the start of craft work utilizing the skill involved on the project construction site and by retaining them as long as training opportunities exist in their crafts or until their training program positions are completed.

(2)	The Contractor shall recall apprentices or trainees released due to reductions in force when the work scope permits and they are available to return.  When they are unavailable to resume training on the project site, the Contractor shall submit written proof of recall efforts and replacement candidates and/or positions in a timely manner.  The Contractor shall not terminate apprentices or trainees prior to completion of their training program positions without NJDOT consultation and authorization.  Apprentices or trainees are not required to be on board for the entire length of the contract.

(3)	The Contractor shall have fulfilled the contractual responsibilities under these Training Special Provisions if the company has provided Acceptable Training to the number of apprentices or trainees specified in this contract and/or by providing the remaining hours required to complete training positions begun by apprentices or trainees on other projects.  The number trained shall be determined on the basis of the total number enrolled on the contract for a significant period.

(4)	The Contractor shall be responsible for demonstrating all steps that have been taken in pursuance of enrolling minorities and females in the training program positions, prior to a determination as to whether the Contractor is in compliance with these Training Special Provisions.

(5)	The Contractor shall submit to the Resident Engineer written training program summaries at the 50% time and/or cost stage of the contract and also prior to project completion, describing all good faith actions and particularly addressing Maximum Available Training for incomplete training positions, per the procedure found in the revised “Instructions for Implementing the Training Special Provisions”.

i.	Enforcement Measures and Contractor’s Rating

(1)	Payment will not be made if either the failure to provide the required training or the failure to hire the apprentice or trainee as a journeyperson is caused by the Contractor and evidences a lack of good faith on the part of the Contractor in meeting the requirements of these Training Special Provisions.

(2)	Per established procedures and scheduled Contract Compliance Reviews, the Contractor’s performance will be rated and reviewed periodically by the Department.

(3)	Noncompliance with these Training Special Provisions may be cause for delaying or withholding monthly and final payments, pending corrective and appropriate measures by the Contractor to the satisfaction of the Department, per Item 1d of these EEO Special Provisions.

8.	Unions

If the Contractor relies in whole or in part upon unions as a source of employees, the Contractor will make maximum effort to obtain the cooperation of such unions to increase opportunities for minorities and females within the unions, and to effect such union referrals to the construction project.  Actions by the Contractor, either directly or through a contractor’s association acting as agent, will include the procedures set forth below:

a.	The Contractor will use maximum effort to develop, in cooperation with the unions, joint training programs aimed at qualifying more minorities and females for union membership and increasing their skills in order to qualify for higher paying employment.

b.	The Contractor will use maximum effort to incorporate an equal employment opportunity clause into each union agreement to the end that such union will be contractually bound to refer applicants without regard to their race, color, religion, sex, or national origin.

c.	The Contractor will obtain information concerning the referral practices and policies of the labor unions except that to the extent such information is within the exclusive possession of the labor unions and they refuse to furnish this information to the Contractor, the Contractor shall so certify to the Department and shall set forth what efforts have been made to obtain this information.

d.	In the event the unions are unable to provide the Contractor with a reasonable flow of minority and female referrals within the time limit set forth in the collective bargaining agreement, the Contractor will through independent recruitment efforts, fill the employment vacancies without regard to race, color, religion, sex, or national origin, making full efforts to obtain qualified and/or qualifiable minorities and females.  (The US Department of Labor has held that it shall be no excuse that the union with which the Contractor has a collective bargaining agreement providing for exclusive referral failed to refer minority employees).  In the event the union referral practice prevents the Contractor from meeting the obligations pursuant to Executive Order 11246, as amended, and these special provisions, such Contractor shall immediately notify the Department.

9.	Subcontracting

a.	The Contractor will use maximum effort to solicit bids from and to utilize minority subcontractors or subcontractors with meaningful minority and female representation among their employees.  Contractors may use lists of minority-owned construction firms as issued by the Department.

b.	The Contractor will use maximum effort to ensure subcontractor compliance with the equal employment opportunity obligations.

10.	Documents and Reports

a.	The Contractor will maintain such documents as are necessary to determine compliance with the contract’s equal employment opportunity requirements.  Documents will include the following:

(1)	the number of minorities, non-minorities, and females employed in each work classification on the Project.

(2)	the progress and efforts being made in cooperation with unions to increase employment opportunities for minorities and females (applicable only to Contractors who rely in whole or in part on unions as a source of their work force).

(3)	the progress and efforts being made in locating, hiring, training, qualifying, and upgrading minority and female employees, and

(4)	the progress and efforts being made in securing the services of minority and female subcontractors or subcontractors with meaningful minority and female representation among their employees.

b.	All such documents must be retained for a period of 3 years following completion of the contract work and shall be available at reasonable times and places for inspection by authorized representatives of the Department and the Federal Highway Administration.

c.	The contractor and each subcontractor must submit monthly employment and wage data to the Department via a web based application using electronic Form CC-257R.  Instructions for registering and receiving the authentication code to access the web based application can be found at:

http://www.state.nj.us/transportation/business/procurement/ConstrServ/documents/NJ_StimulusReportingNotification-Contractor.pdf

Instructions on how to complete Form CC257 are provided in the web application.  Submit Form CC-257R through the web based application within 10 days following the end of the reporting month.  Submission of this form also satisfies the requirement of the form FHWA 1391.

All employment and wage data must be accurate and consistent with the certified payroll records.  The contractor is responsible for ensuring that their subcontractors comply with these reporting requirements.  Failure by the contractor to submit Monthly Employment Utilization Report may impact the contractor’s prequalification rating with the Department.

FHWA Attachment No.7

SPECIAL CONTRACT PROVISIONS FOR INVESTIGATING, REPORTING AND RESOLVING EMPLOYMENT DISCRIMINATION AND SEXUAL HARASSMENT COMPLAINTS

The contractor hereby agrees to the following requirements in order to implement fully the nondiscrimination provisions of the Supplemental Specifications.

The Contractor agrees that in instances when it receives from any person working on the project site a verbal or written complaint of employment discrimination, prohibited under N.J.S.A. 10:5-1 et seq., 10:2-1 et seq., 42 U.S.C. 2000(d) et seq., 42 U.S.C. 2000 (e) et seq. and Executive Order 11246, it shall take the following actions:

1.	Within one (1) working day commence an investigation of the complaint which shall include but not be limited to interviewing the complainant, the respondent, and all possible witnesses to the alleged act or acts of discrimination or sexual harassment.

2.	Prepare and keep for its use and file a detailed written investigative report which includes the following information:

a)	Investigatory activities and findings.

b)	Dates and parties involved and activities involved in resolving the complaint.

c)	Resolution and corrective action taken if discrimination or sexual harassment is found to have taken place.

d)	A signed copy of resolution of complaint by complainant and contractor.

In addition to keeping in its files the above-noted detailed written investigative report, the contractor shall keep for possible future review by the Department all other records, including but not limited to, interview memos and statements.

3.	Upon the request of the Department, provides to the Department within ten (10) calendar days a copy of its detailed written investigative report and all other records on the complaint investigation and resolution.

4.	Take appropriate disciplinary action against any contractor employee, official or agent who has committed acts of discrimination or sexual harassment against any contractor employee or person working on the project. If the person committing the discrimination is a subcontractor employee, then the contractor is required to attempt to effectuate corrective and/or disciplinary action by the subcontractor in order to establish compliance with project’s contract requirements.

5.	Take appropriate disciplinary action against any contractor employee, official or agent who retaliates, coerces or intimidates any complaint and/or person who provides information or assistance to any investigation of complaints of discrimination or sexual harassment. If the person retaliating, coercing or intimidating a complainant or other person assisting an investigation is a subcontractor’s employee, then the contractor is required to attempt to effectuate corrective and/or disciplinary action by the subcontractor in order to establish compliance with the project’s contract requirements.

6.	Ensure to the maximum extent possible that the privacy interests of all persons who give confidential information in aid of the contractor’s employment discrimination investigation are protected.

In conjunction with the above requirements, the contractor shall develop and post a written sexual harassment policy for its work force.

Failure by the contractor to comply with the above requirements may be cause for the New Jersey Department of Transportation to institute against the contractor any and all enforcement proceedings and/or sanctions authorized by the contract or by state and/or federal law.