## Slide 1: Proposed Readoption with Substantial Amendments to N.J.A.C. 14:7, Natural Gas Pipelines
Monday, April 25, 2022
10:00 a.m.
Via Zoom

## Slide 2: Comments and Question and Answer
All registrants may comment. Those who have indicated that they wish to speak will be called upon first by the moderator. Anyone else wishing to speak may raise their hand and ask to be added to the list.
If Questions arise for the presenters, they should be typed into the Q & A tab on your screen.
Please keep questions specific to the presentations and the topics discussed in the draft rule proposal amendments.

## Slide 3: Comments and Question and Answer (Cont.)
The purpose of this stakeholder meeting is to solicit input from the public and interested parties on the proposed readoption with amendments of rules at N.J.A.C. 14:7 which govern natural gas pipelines.

## Slide 4
SUBCHAPTER 1. CONSTRUCTION, OPERATION AND MAINTENANCE OF
TRANSMISSION AND DISTRIBUTION NATURAL GAS PIPELINES

## Slide 5: N.J.A.C. 14:7-1.1, scope and applicability
This subchapter sets forth the purpose and scope of the subchapter.
A reference to the Code of Federal Regulations has been added.
N.J.A.C. 14:7-1.1A, definitions
Definitions for “Flowable fill”, “Gas” and “Lower Explosive Limit” have been added. The definition for "Covered task" has been clarified.

## Slide 6
"Covered task" means an activity, identified by the operator, that:
  Is performed on a pipeline facility;
  Is an operations, maintenance or new construction task;
  Is performed as a requirement of 49 CFR Part 192; and
  Affects the operation or integrity of the pipeline.
N.J.A.C. 14:7-1.1A, definitions (cont.)

## Slide 7
N.J.A.C. 14:7-1.2, Compliance with federal code
No changes.
N.J.A.C. 14:7-1.3, Classification of pipeline locations
No changes.
N.J.A.C. 14:7-1.4, Proscribed areas
No changes.

## Slide 8
N.J.A.C. 14:7-1.6, quality control of field welding
No changes.
N.J.A.C. 14:7-1.7, fabrication details
No changes.
N.J.A.C. 14:7-1.8, Pipelines near railroads and highways
No changes.

## Slide 9
N.J.A.C. 14:7-1.9, distribution system valve requirements and emergency response drills
Section 9(f) has been added to require emergency drills to take place once every twenty-four months and sets forth the requirements of who shall participate.
Section 9(g) has been added to require operators notify Board staff in advance and provide a final audit report within two months.

## Slide 10
N.J.A.C. 14:7-1.10, Valve assessment and emergency closure plan – transmission pipelines
Section 10(f) has been amended to specify that emergency closure drills shall take place during normal business hours.
N.J.A.C. 14:7-1.11, installation of pipe
Section 11(e) has been added to require 12 inches of separation between the pipe and flowable fill.
Section 11(g) has been amended to require a tracer wire to be installed on all new or replacement plastic pipe. Operators must obtain Bureau of Pipeline Safety approval to use alternate means of locating pipes.

## Slide 11
N.J.A.C. 14:7-1.11, installation of pipe (cont.)
Section 11(g) has been amended to allow the use of alternate tracer wires.
Section 11(h) has been amended to add additional subsurface warning tape requirements based on the pipe diameter.
N.J.A.C. 14:7-1.12, Minimum cover over natural gas pipelines
No changes.

## Slide 12
N.J.A.C. 14:7-1.13, projections
No changes.
N.J.A.C. 14:7-1.14, pressure testing
No changes.
N.J.A.C. 14:7-1.15, Meter and regulator stations: electric installations
No changes.

## Slide 13
N.J.A.C. 14:7-1.16, Odorization
No changes.
N.J.A.C. 14:7-1.17, incidents and service interruptions - reporting
Incorporates N.J.A.C. 14:3-3.7 and 14:3-6.4 through 6.6 reporting requirements with modifications
The term “incident” is used in place of “accident” and the term “operator” is used in place of “utility” throughout.

## Slide 14
N.J.A.C. 14:7-1.17, incidents and service interruptions – reporting (Cont.)
Pipeline operators must notify the Board’s Division of Reliability and Security within one hour of learning of a reportable incident versus the 2 hours currently required by Chapter 3.
Reportable interruptions now apply to a group of 100 or more customers during the heating season between November 15 and March 15 for 30 minutes or to a group of 100 or more customers for 1 hour during the non-heating season.
All other interruptions previously classified as two-hour interruptions are now reportable when the interruption lasts 1 hour.

## Slide 15
N.J.A.C. 14:7-1.18, Proposed construction
No changes.
N.J.A.C. 14:7-1.19, gas leak classification and repair
New section 19(a) has been added to require a gas leak to be repaired in a timeframe based on their classification.
New section 19(b) has been added to provide the leak grading criteria.
New section 19(c) has been added to require operator qualification for individuals performing leak classification under this section.
New section 19(d) has been added to require Incident Command training for leak response personnel.

## Slide 16
N.J.A.C. 14:7-1.20, monthly inspection patrols and leak detection surveys
Section 20(b) has been amended to include population density as a consideration when determining if more frequent leak surveys are necessary.
Section 20(d) of the proposed rule currently shows a change “bare and coated cathodically unprotected steel.” This is a mistake as no changes are being made to this section.
N.J.A.C. 14:7-1.21, Public outreach
No changes.

## Slide 17
N.J.A.C. 14:7-1.22, Damage prevention
Section 22(c)(4) has been added to require operators to provide on site inspection and continuing surveillance for directional drills within close proximity to gas facilities.
N.J.A.C. 14:7-1.23, review of operating and maintenance standards
No changes.

## Slide 18
N.J.A.C. 14:7-1.24, oversight of construction, operations, and maintenance activities
Section 24(b) has been amended to require operator crews performing construction to be inspected at least once per work day.
New Section 24(g) has been added to require individuals performing covered tasks, as previously defined, to meet the operator’s qualification program.
N.J.A.C. 14:7-1.25, Directional drilling operations
No changes.

## Slide 19
N.J.A.C. 14:7-1.26, operator reporting requirements
Section 26(c)(4) has been added to require operators to submit the Liquefied Natural Gas Facilities Annual Report to the Bureau of Pipeline Safety.
Section 26(d)(1) has been amended to have the leak classification status report to be broken down by municipality.
Section 26(f) has been added to require notification prior to performing integrity digs on transmission pipelines.
Section 26(g) has been added to require notification to the Bureau of Pipeline Safety of all Maximum Allowable Operating Pressure (MAOP) exceedances.

## Slide 20
SUBCHAPTER 2. VIOLATIONS, INFORMAL CONFERENCES, CIVIL ADMINISTRATIVE
PENALTIES AND ADJUDICATORY HEARINGS

## Slide 21
N.J.A.C. 14:7-2.1, scope and purpose
No changes.
N.J.A.C. 14:7-2.2, notices of probable violation
No changes.
N.J.A.C. 14:7-2.3, Response by alleged violator to notice of probable violation
No changes.

## Slide 22
N.J.A.C. 14:7-2.4, failure of alleged violator to submit answering certification
No changes.
N.J.A.C. 14:7-2.5, notice of administrative order and civil administrative penalty assessment (aonocapa)
No changes.
N.J.A.C. 14:7-2.6, adjudicatory hearings
No changes.

## Slide 23
N.J.A.C. 14:7-2.7, civil administrative penalty determination
Section 7(a) has been amended to incorporate by reference the civil administrative penalty amounts specified in the federal code.

## Slide 24
We will now take your public comments in the order that you registered for this event.
Thank you.