LOW FLOW SAMPLING

DATA SHEET

SHEET _____ OF _____

| SITE: |  | CONSULTING FIRM: |  |  |
| --- | --- | --- | --- | --- |
| DATE: |  | FIELD PERSONNEL: |  |  |
| WEATHER: |  |  |  |  |
| MONITOR WELL #: |  | WELL DEPTH: |  |  | SCREENED/OPEN INTERVAL: |  |  |
| WELL PERMIT #: |  | WELL DIAMETER: |  | Inches |  |  |
| PID/FID READINGS (ppm): | BACKGROUND: |  |  | PUMP INTAKE DEPTH: ________ ft below TOC |  |
|  | BENEATH OUTER CAP: |  |  | DEPTH TO WATER BEFORE PUMP INSTALLATION : ________ ft below TOC |  |
|  | BENEATH INNER CAP: |  |  |  |  |
| TIME | PURGING | SAMPLING | pH (pH units) | SPECIFIC CONDUCTIVITY (mS/cm) | REDOX POTENTIAL (mv) | DISSOLVED OXYGEN (mg/l) | TURBIDITY (NTU) | TEMPERATURE (degrees C) | PUMPING RATE (ml/min) | DEPTH TO WATER (ft below TOC) |
|  |  |  | READING | CHANGE* | READING | CHANGE* | READING | CHANGE* | READING | CHANGE* | READING | CHANGE* | READING | CHANGE* |  |  |
|  |  |  |  | NA |  | NA |  | NA |  | NA |  | NA |  | NA |  |  |
| COMMENTS: |

*INDICATOR PARAMETERS HAVE STABLIZED WHEN 3 CONSECUTIVE READINGS ARE WITHIN: ± 0.1 for pH; ± 3% for Specific Conductivity and Temperature;

± 10 mv for Redox Potential; and ± 10% for Dissolved Oxygen and Turbidity